## Slide 1: Image Sharing Based on Chinese Remainder Theorem
Institute of Information Systems and Applications
Department of Computer Science
National Tsing Hua University
Hsinchu, Taiwan 30013
http://www.cs.nthu.edu.tw/~cchen

## Slide 2: Illustration

## Slide 3: Outline
Introduction
Background Review
Proposed Method
Experimental Results
Conclusion

## Slide 4: Introduction
To avoid the information is carried by only a single individual
Data are partitioned into n shadows and are distributed to n participants
By collecting at least k out of n shadows, we can completely recover the original data (information)
A (k,n)-threshold technique based on CRT is introduced

## Slide 5: Background Review for (k,n)-threshold Techniques
The secret value S is used to generate n shadows
Any k or more shadows can recover the secret value S
Fewer than k shadows cannot reveal the secret value S
Commonly used (k,n)-threshold schemes for sharing
Shamir [Sham1979]
Blakley [Blak1979]
Asmuth and Bloom [Asmu1983]

## Slide 6: Shamir (1979)
Based on polynomial interpolation
Sharing
  Given k distinct points in the 2-d plane, determine a unique polynomial of degree k-1
  Put the secret message to the constant term, generate n shadow messages which are distributed to n participants
Recovering
  Polynomial interpolation to find the secret message

## Slide 7: Blakley (1979)
Uses the characteristic of geometry
Sharing
  Chooses a point Q which contains the secret value S in the k-dimensional space
  Select n hyper-planes passing through the point Q as n shadows
Recovering
  Collect at least k hyper-planes
  Solving a linear system of equations
Q
L1
L2
L3

## Slide 8: Asmuth and Bloom (1983)
Requirements
  A sequence of pairwise relatively prime positive integers
Sharing
  Modular arithmetic
  Random integer α
Recovering
  Based on Chinese Remainder Theorem to solve Congruence Eqs.

## Slide 9: Background Review-Thien and Lin (2002)
1. Suppress all pixels whose gray values are larger than 250 to 250.
2. Permute the pixels
3.
Permuted Image
q(x)≡a0+a1x+…+ak-1xk-1 (mod 251)
a0 | a1 | … | ak-１ | …
q(r1) |  | 
q(rn) |  | 
．．．
Shadow Images
k pixels

## Slide 10: Background Review-Thien and Lin
1. Collect any k shadow images.
q(r1) |  | 
Shadow Images
Polynomial interpolation
q(rk) |  | 
．．．
q(x)≡a0+a1x+…+ak-1xk-1 (mod 251)
Permuted Image
a0 | a1 | … | ak-１ | …
2.
3. Permute the pixels inversely.

## Slide 11: Background Review-Thien and Lin
Distortion
  Suppress pixels whose gray values are larger than 250 to 250.
Permuted Image
a0 | a1 | … | ak-１ | …
If p<250→store p
If p250→store 250 and p-250
250 | a0-250 | … | ak-2 | ak-１
Array E

## Slide 12: Chinese Remainder Theorem
Let m1, m2,…, mk be integers with gcd(mi, mj)=1 whenever i j. There exists a unique solution x for the following simultaneous congruence equations in [0, m1m2mk)

## Slide 13: Solution for Chinese Remainder Theorem

## Slide 14: Background Review- Mignotte’s Scheme vs. Asmuth’s Scheme
Mignotte’s Scheme | Asmuth’s Scheme
gcd(mi, mj)=1, for | gcd(mi, mj)=1, for
CRT | CRT

## Slide 15: Background Review-Ulutas (Sharing)
p0 | p1 | … |  | 
 |  | … |  | 
 |  | … |  | pn
Secret Image
1. Select a set {m0<m1<…<mn} which satisfies
(i) gcd(mi, mj) = 1, for 1ijn (ii) M = ＞ m0 *
2.
If p m0 If p < m0
y =p-m0+m0 y = p+m0
0t t+1 <m1*…*mk
yi ≡ y mod mi for i=1,2,…n
y1 | 
y2 | 
yn | 
Shadow Images
．．．

## Slide 16: Background Review-Ulutas (Revealing)
．．．
y1 | 
y2 | 
yk | 
Shadow Images
CRT→y
If
p = m0+y mod m0
Else
p = y mod m0
If p m0 If p < m0
y =p-m0+m0 y = p+m0
0t t+1 <m1*…*mk
Notes: 在還原的部分
1.收集到k張的shadow images
2.使用中國餘式定理去還原對應的y值，接著因為剛剛有把pixel值分成≥m0和<m0，
所以在還原時我們求出random integer alpha來區分這兩種情形
3.如果alpha小於等於t，則pixel值為m0+y mod m0，
否則pixel值為y mod m0
用這個方式則可以求得秘密影像

## Slide 17: Proposed Method
https://lh4.ggpht.com/T7Qsp9L8qYLtaLk4-4Zgt8Nwy_FfvnDdxSL8c3BSF2Lk5X-CKjfxGjhbfbyHy5iHsB3YRA=s151

## Slide 18: Proposed Method
Based on Ulutas scheme [Ulut2009], we proposed a method which uses the color image as the secret image.
There are three values R, G, and B in each pixel of the color image, we need to compute these three values respectively.
To strengthen the robustness and the reliability of our method, we encrypt the secret values using the simple exclusive-or (XOR) cipher with a 24-bit long key.
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
+random integer→shares
Last significant bit

## Slide 19: The Proposed Sharing Method
Original Secret image
Encryption with XOR
Shadow image 1
Shadow image 2
………………
Shadow image n
Sharing scheme

## Slide 20: The Proposed Revealing Method
.…………
Chinese Remainder Theorem
Revealing scheme
Decryption with XOR
Revealed image

## Slide 21: The Proposed Sharing Method
1. Do the XOR operation on each R,G,B values
2. Determine a set of integers {m0, m1, m2, …, mn} which satisfies
  (i) m0=128<m1<…<mn<256; (ii) gcd(mi, mj) = 1, for 0ijn;
  (iii) M = ＞ m0 *
3.
Pixel
R
G
B
h=r, g, b,
yr
yg
yb
mod mi
\
XOR
ＲＲＲＲＲＲＲＲＧＧＧＧＧＧＧＧＢＢＢＢＢＢＢＢ
♁１００１０１０１１００１０１０００１１０１０１１
Encrypted R, G, B values
Shadow pixel
4.

## Slide 22: The Proposed Revealing Method
．．．
y1 | 
y2 | 
yk | 
Shadow images
CRT→yr、yg 、yb
h=r, g, b
Revealed pixel
h=r, g, b,
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0 or 1
Last significant bit
XOR
Without using
\
pr
pg
pb

## Slide 23: Experimental Results
http://blog.toggl.com/wp-content/uploads/sites/5/2014/10/programmer-at-work.jpg

## Slide 24: Experimental Results - Mandrill
Original image
Shadow image1
Shadow image2
Shadow image3
Shadow image4
Shadow image5
Revealed image

## Slide 25: Experimental Results - Lenna
Original image
Shadow image1
Shadow image2
Shadow image3
Shadow image4
Shadow image5
Revealed image

## Slide 26: Experimental Results - Peppers
Original image
Shadow image1
Shadow image2
Shadow image3
Shadow image4
Shadow image5
Revealed image

## Slide 27: Experimental Results
Sharing time and revealing time of three secret images
 | Sharing time (sec.) | Revealing time (sec.)
Baboon | 6.37 | 4.10
Lenna | 6.57 | 4.13
Peppers | 6.31 | 3.93

## Slide 28: Conclusion
http://www.oldinsuranceguy.com/wp-content/uploads/2013/12/conclusion-diagram-in-blank.jpg

## Slide 29: Conclusion
Based on Ulutas’s scheme, we proposed a secret image sharing method which uses color image as secret image and Chinese remainder theorem to reveal the secret image.
In our method, we can only reveal a distortion image. Generally speaking, naked eyes cannot distinguish the difference between the secret image and distortion image with only the difference of the least significant bit.