## Slide 1: CS4101 嵌入式系統概論 MQX GPIO, Timer, ISR
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Materials from www.freescale.com)

## Slide 2
MQX GPIO

## Slide 3: Recall the Code for Using LED
GPIO_PIN_STRUCT pin_led1[] = {
BSP_LED1,
GPIO_LIST_END
};
MQX_FILE_PTR port_file_led1;
port_file_led1 = fopen("gpio:write", (char *) NULL);
ioctl(port_file_led1, GPIO_IOCTL_ADD_PINS, &pin_led1 );
ioctl(port_file_led1, GPIO_IOCTL_WRITE_LOG0, NULL );
What do they mean?

## Slide 4: GPIO Driver
GPIO drivers create a hardware abstraction layer for application to use input or output pins.
To access GPIO pins, need to open GPIO device with a parameter specifying set of pins to be used, e.g.,
  file = fopen(“gpio:read”, &pin_table);
  The pin_table is an array of GPIO_PIN_STRUCT ended with GPIO_LIST_END.
  A pin is described as:
  <port_name>|<pin_#>|<additional_flags>
(MQX RTOS I/O Drivers User’s Guide)

## Slide 5: GPIO Driver
Example of pin_table initialization structure:
  const GPIO_PIN_STRUCT pin_table[] = {
  GPIO_PORT_NQ | GPIO_PIN5 | GPIO_PIN_IRQ,
  GPIO_PORT_TC | GPIO_PIN3,
  GPIO_LIST_END
  };

## Slide 6: Some GPIO Control Parameters
GPIO_IOCTL_ADD_PINS
  Adds pins to the device file. The parameter is GPIO_PIN_STRUCT array.
GPIO_IOCTL_WRITE_LOG1
  Sets output pins. If the parameter is GPIO_PIN_STRUCT array, the driver sets all pins specified
GPIO_IOCTL_WRITE
  Sets or clears output pins according to GPIO_PIN_STRUCT array.
GPIO_IOCTL_READ
  Reads status of input pins and update the GPIO_PIN_STRUCT array.
GPIO_IOCTL_SET_IRQ_FUNCTION
  Sets the callback function which is invoked for any IRQ event coming from any file pin.
GPIO_IOCTL_ENABLE_IRQ
  Enables IRQ functionality for all IRQ pins in the file.

## Slide 7: Example of Using IOCTL Command
Set all pins attached to the GPIO device file:
  ioctl(file, GPIO_IOCTL_WRITE_LOG1, NULL);
Read pin status to read_pin_table:
  if(ioctl(file, GPIO_IOCTL_READ,
  &read_pin_table) == IO_OK)
  {
  if((read_pin_table[0]& GPIO_PIN_STATUS)
  == GPIO_PIN_STATUS_1)
  {// first pin in the table is set}
  }

## Slide 8
MQX Timer

## Slide 9: MQX Time
Kept as a 64-bit count of the number of tick interrupts since MQX started to run
  If tick rate is 1/nsec, MQX time rolls over for 584 years
Time component:
  Elapsed time (amount of time since MQX started) and absolute time (time since the reference date of 0:00:00 January 1, 1970)
  Time unit: seconds/milliseconds, ticks, date format
Time resolution:
  Define how often MQX updates time, duration of a tick
  Normally 200 ticks per second or five milliseconds
  Can get elapsed time in nsec resolution
(MQX RTOS User’s Guide)

## Slide 10: Timers
An application can use timers:
  To cause notification function to run at specific time
    When MQX creates the timer component, it starts Timer task, which maintains timers and application-defined notification functions. When a timer expires, Timer task calls the appropriate notification function.
  To communicate that a time period has expired
A task can start a timer at a specific time or at some specific time after the current time
Types of timers:
  One-shot timer: expire once
  Periodic timer: expire repeatedly at specified interval

## Slide 11: Timers
Create timer component:
  A timer component and associated Timer task can be explicitly created by calling _timer_create_component() with the priority and stack size for Timer task.
  Timer task manages timer queues and provides a context for notification functions.
Start timers:
  Start a timer with calls such as _timer_start_periodic_at() _timer_start_oneshot_after_ticks()
  MQX then inserts a timer request into the queue of outstanding timers.
  When the timer expires, the notification function runs.

## Slide 12: Example of Timers
Simulate a LED being turned on and off every second
  One timer turns the LED on, and another turns it off.
  Each timer has a period of 2 seconds with an offset of 1 second between them.
  Task runs for 6 seconds.

## Slide 13: Example of Timers (1/3)
#include <mqx.h> #include <bsp.h> #include <fio.h> #include <timer.h> #define TIMER_TASK_PRIORITY 2 #define TIMER_STACK_SIZE 2000 #define MAIN_TASK 10 extern void main_task(uint_32); const TASK_TEMPLATE_STRUCT MQX_template_list[] = { /* Task Index, Function, Stack, Priority, Name, Attributes, Param, Time Slice */ { MAIN_TASK, main_task, 2000, 8, "Main", MQX_AUTO_START_TASK, 0, 0 }, { 0 } };
Notes: 12
12

## Slide 14: Example of Timers (2/3)
static void LED_on(_timer_id id, pointer data_ptr, MQX_TICK_STRUCT_PTR tick_ptr) { /* turn on LED */ } static void LED_off(_timer_id id, pointer data_ptr, MQX_TICK_STRUCT_PTR tick_ptr) { /* turn off LED */ } void main_task(uint_32 initial_data) { MQX_TICK_STRUCT ticks, dticks; _timer_id on_timer, off_timer; uint_8 time = 6; // total running time in seconds _timer_create_component(TIMER_TASK_PRIORITY, TIMER_STACK_SIZE);
Notes: 13
13

## Slide 15: Example of Timers (3/3)
_time_init_ticks(&dticks, 0); _time_add_sec_to_ticks(&dticks, 2); // 2 seconds _time_get_elapsed_ticks(&ticks); _time_add_sec_to_ticks(&ticks, 1); // cur time + 1s on_timer = _timer_start_periodic_at_ticks(LED_on, 0, TIMER_ELAPSED_TIME_MODE, &ticks, &dticks); _time_add_sec_to_ticks(&ticks, 1); // cur time + 2s off_timer = _timer_start_periodic_at_ticks(LED_off, 0, TIMER_ELAPSED_TIME_MODE, &ticks, &dticks); _time_delay(time * 100); // wait 6 seconds _timer_cancel(on_timer); _timer_cancel(off_timer); _task_block(); }
Notes: 14
14

## Slide 16: Timer Example Explained
Data structure of ticks:
  typedef struct mqx_tick_struct{
  _mqx_uint TICKS[MQX_NUM_TICK_FIELDS];
  uint_32 HW_TICKS;
  } MQX_TICK_STRUCT;
_time_init_ticks()
  Initializes a tick-time structure with a specified number of ticks
_time_get_elapsed_ticks()
  Gets the tick time that has elapsed, since the application started on this processor

## Slide 17: Timer Example Explained
_timer_start_periodic_at_ticks
  Starts a periodic timer at a specific time (in tick)
  _timer_id _timer_start_periodic_at_ticks(
  void (_CODE_PTR_ notification_function)
  (_timer_id id, pointer data_ptr,
  MQX_TICK_STRUCT_PTR tick_time_ptr),
  pointer notification_data_ptr,
  _mqx_uint mode,
  MQX_TICK_STRUCT_PTR tick_time_start_ptr,
  MQX_TICK_STRUCT_PTR tick_time_wait_ptr)
Start time
Period
Pointer to the data that MQX passes to the notification function

## Slide 18
MQX Interrupts

## Slide 19: Handling Interrupts
An MQX ISR is not a task. It is a small routine that reacts to hardware interrupts or exceptions
  When MQX calls an ISR, it passes a parameter that application defines, when application installs the ISR
  ISR usually causes a task to become ready
There is a kernel ISR (_int_kernel_isr()) that runs before any other ISR:
  It saves the context of the active task.
  It switches to the interrupt stack.
  It calls the appropriate ISR.
  After the ISR has returned, it restores the context of the highest-priority ready task
(MQX RTOS User’s Guide)

## Slide 20: Handling Interrupts
When the ISR returns to the kernel ISR, the kernel ISR performs a task dispatch operation if the ISR readied a task that is of higher priority, than the one that was active at the time of the interrupt.

## Slide 21: Initializing Interrupt Handling
When the MQX starts, it initializes its ISR table, which has an entry for each interrupt number:
  A pointer to the ISR to call.
  Data to pass as a parameter to the ISR.
  A pointer to an exception handler for that ISR.
Initially, the ISR for each entry is the default ISR _int_default_isr(), which blocks the active task.
  An application can replace an ISR with an application-defined, interrupt-specific ISR using _int_install_isr()

## Slide 22: Initializing Interrupt Handling
Application can replace the ISR with an application-defined, interrupt-specific ISR with _int_install_isr()
  interrupt number
  pointer to the ISR function
  Pointer to data to be passed as first parameter to the ISR
An application-defined ISR usually signals a task using mechanisms such as event or semaphore
  The will then be dequeued from a task queue and put in the task’s ready queue

## Slide 23: Example of Button Interrupt
void Main_task(uint_32 initial_data) { //gpio sw1 port_file_btn1 = fopen("gpio:read", (char_ptr) &pin_btn1 ); ioctl(port_file_btn1, GPIO_IOCTL_SET_IRQ_FUNCTION, (pointer)btn_1_INT_callback); } #if defined BSP_BUTTON1 #define PIN_BTN1 GPIO_PIN_STRUCT pin_btn1[] = { BSP_BUTTON1 ¦ GPIO_PIN_IRQ_FALLING, GPIO_LIST_END}; #endif void btn_1_INT_callback(void) { printf("BTN_1\n"); }

## Slide 24: Button Interrupt Example Explained
GPIO_IOCTL_SET_IRQ_FUNCTION
  Sets the callback function which is invoked for any IRQ event coming from any file pin.
GPIO_IOCTL_ENABLE_IRQ
  Enables IRQ functionality for all IRQ pins in the file.
GPIO_PIN_IRQ_FALLING
  For the gpio:input device, enables the pin status change interrupt callback function, which is set by PIO_IOCTL_SET_IRQ_FUNCTION, and allows the interrupt callback function being called when the falling edge occurs.

## Slide 25: Example of Interrupts (1/3)
Install an ISR that will call the previous ISR, which is the BSP-provided periodic timer ISR.
#include <mqx.h> #include <bsp.h> #define MAIN_TASK 10 extern void main_task(uint_32); extern void new_tick_isr(pointer); const TASK_TEMPLATE_STRUCT MQX_template_list[] = { /* Task Index, Function, Stack, Priority, Name, Attributes, Param, Time Slice */ { MAIN_TASK, main_task, 2000, 8, "Main", MQX_AUTO_START_TASK, 0, 0 }, { 0 } };

## Slide 26: Example of Interrupts (2/3)
typedef struct my_isr_struct { pointer OLD_ISR_DATA; void (_CODE_PTR_ OLD_ISR)(pointer); _mqx_uint TICK_COUNT; } MY_ISR_STRUCT, _PTR_ MY_ISR_STRUCT_PTR; void new_tick_isr(pointer user_isr_ptr) { MY_ISR_STRUCT_PTR isr_ptr; isr_ptr = (MY_ISR_STRUCT_PTR)user_isr_ptr; isr_ptr->TICK_COUNT++; /* Chain to the previous notifier */ (*isr_ptr->OLD_ISR)(isr_ptr->OLD_ISR_DATA); }
Notes: 25
25

## Slide 27: Example of Interrupts (3/3)
void main_task(uint_32 initial_data) { MY_ISR_STRUCT_PTR isr_ptr; isr_ptr = _mem_alloc_zero((_mem_size)sizeof(MY_ISR_STRUCT)); isr_ptr->TICK_COUNT = 0; isr_ptr->OLD_ISR_DATA = _int_get_isr_data(BSP_TIMER_INTERRUPT_VECTOR); isr_ptr->OLD_ISR = _int_get_isr(BSP_TIMER_INTERRUPT_VECTOR); _int_install_isr(BSP_TIMER_INTERRUPT_VECTOR, new_tick_isr, isr_ptr); _time_delay_ticks(200); printf("\nTick count = %d\n", isr_ptr->TICK_COUNT); _task_block(); }
Notes: 26
26

## Slide 28: Interrupt Example Explained
_int_get_isr
  Get the current ISR for the vector number
_int_get_isr_data
  Get the data associated with the vector number
_int_install_isr
  vector: vector number of the interrupt
  isr_ptr: pointer to the ISR
  isr_data: pointer to the data to be passed as the first parameter to the ISR