## Slide 1: CS4101 嵌入式系統概論 Sensor Accessing in MQX
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Materials from www.freescale.com, Prof. P. Marwedel of Univ. Dortmund)

## Slide 2: Recall Our TWR-K60D100M
PK60DN512VMD10
Kinetis MCU
LED/Touch Buttons
D7,D8,D9,
D11
SW1
SW2
Power/OSJTAG
Mini-B USB
Connector
Secondary
Connector
Primary
Connector
SW3(Reset)
MMA8451Q
Accelerometer

## Slide 3: Outline
Introduction to sensors
  Focusing on 3-axis accelerometer
Accessing sensors in MQX through I2C serial communication

## Slide 4: What Are Sensors?
A sensor is a device that detects either an absolute value or a change in a physical or electrical quantity, and converts that change into a useful input signal (often analog signals) for a decision making center
Data Processing,
Control, Connectivity
Sensor
Input
Actuator
or
Output
Notes: What is a Sensor?
A Sensor is a device that detects a physical or electrical quantity and converts this characteristic into a value for a decision making center such as an MCU. From this the MCU can decide on events, and trigger an additional output.
Some examples of physical quantities that our sensors measure include:
Temperature
Pressure
Flow rate
Acceleration
Vibration
Tilt
Touch

## Slide 5: Sensors
For capturing physical data
Sensors can be designed for virtually every physical and chemical stimulus
  Heat, light, sound, weight, velocity, acceleration, electrical current, voltage, pressure, …
  chemical compounds
Many physical effects can be used for constructing sensors
  Law of induction (generation of voltages in an electric field), light-electric effects. …

## Slide 6: Sensor Applications
Touch
Touch detection
Appliance control panels
Touch panels
Pressure
Medical
Barometer/altimeter
Engine control/tire pressure
HVAC applications
Water level
Acceleration
Gesture detection
Tilt to control
Tap detection
Position detection
Orientation
Multiple sensors working together for next generation applications…
Gyroscopic
Magnetic
Ambient light sensing
Temperature/humidity
Motion detection
Notes: Freescale has a diverse Sensor Portifolio . Traditionally we started in the Automotive field, and have branched into the Consumer and Industrial space. This includes some medical application space.
Freescale has many different sensors, including Inertial Accelerometers, Pressure Sensors and Touch Sensors.
Accelerometers include measurements of Gesture detection, Tilt, Tap and Orientation.
Pressure sensors measure Automotive engine control parameters, medical health monitoring, and have lots of industrial applications.
Touch sensors can be utilized in button replacement and be designed for custom applications.

## Slide 7: Accelerometers
Devices that are used to measure acceleration
Common accelerometer types
  Resistive: strain gauge, piezoresistive, thin-film
  Capacitive, fiber optic, servo or force balance, vibrating quartz, piezoelectric
MEMS accelerometers:
  MEMS (Micro ElectroMechanical Systems): small silicon devices that perform the same function as larger mechanical systems
There is always 1 g downward due to gravity

## Slide 8: Accelerometer Types
Capacitive: utilizes frequency modulation technique through varying capacitor bridge
Power
Signal
Ground
Mass
Sensing Capacitor #1
Built-In Electronics
Fixed Capacitors
~
Sensing Capacitor #2
Flexure
Insulator
Insulator

## Slide 9: Accelerometer Types
8
Piezoelectric:
  Force on self-generating crystal provides charge output proportional to acceleration
Signal/Power
Ground
Base
Voltage or Charge Amplifier
Preload Ring
Mass
Piezoelectric Crystal
F
F
+
-
Piezoelectric Material
+
+
+
+
+
+
-
-
-
-
-
-
Notes: 壓電材料

## Slide 10: MEMS Accelerometer
9
Substrate with circuitry
Proof mass
Suspension arms
Axis of response

## Slide 11: Accelerometer at Work: X, Y, Z Movement
X-axis
Y-axis
Z-axis
Notes: Notice how the g-cell moves in X, Y and Z axes. The change in the distance between the plates or fingers determines the capacitance. This relates to the acceleration in each axis. Silicon has no fatigue, so can repetitively move back and forth for extended periods. Bump stops are used to control maximum movement.

## Slide 12: MMA8451Q Accelerometer
Low-power, 3-axis, capacitive micromachined accelerometer with 14 bits of resolution

## Slide 13: MMA8451Q Accelerometer
Operation modes

## Slide 14: MMA8451Q Features
Measured acceleration data stored in OUT_X (Y, Z)_MSB, OUT_X (Y, Z)_LSB, registers as 2’s complement 14-bit numbers
  If only 8-bit results needed, can use OUT_X (Y, Z)_MSB
Resolution
  When the full-scale is set to 2g, the measurement range is -2g to +1.99975g, and each count corresponds to 1g/4096 (0.25 mg) at 14-bits resolution.
  When 8g, range is -8g to +7.999g, and each count is 1g/1024 (0.98 mg) at 14-bits resolution.
Provide a large number of data and control registers, data buffer, interrupt, I2C communication

## Slide 15: Control Register: CTRL_REG1
Configure MMA8451Q:
write_I2C(I2C_ACCELEROMETER_ADDRESS,0x2A,0x03);
Notes: F_Read bit selects between normal and Fast Read mode. When selected, the auto increment counter will skip over the LSB data
bytes. Data read from the FIFO will skip over the LSB data, reducing the acquisition time. Note F_READ can only be changed
when FMODE = 00. The F_READ bit applies for both the output registers and the FIFO.

## Slide 16: Outline
Introduction to sensors
  With emphasis on 3-axis accelerometer
Accessing sensors through I2C serial communication

## Slide 17: I2C Serial Communication
I2C: Inter Integrated Circuit Bus
  Two-wire serial multimaster-slave bus protocol by Philips in the 1980s
  Enables peripheral ICs to communicate using simple communication hardware
  7-bit or 10-bit address space
  Data transfer rate: 100 kbits/s (standard mode), 400 kbits/s (fast mode), 3.4M bits/s (high speed mode)
  Common devices capable of interfacing to I2C bus:
    EPROMS, Flash, and some RAM memory, real-time clocks, watchdog timers, and microcontrollers

## Slide 18: I2C Bus Structure
2 signal lines: SCL (serial clock), SDA (serial data)
Every device connected to the I2C bus has a unique address and can act as a receiver or a transmitter
I2C is a multi master bus.
  Bus master is established at the time of communication

## Slide 19: I2C Protocol
Transfers are byte oriented, MSB first
Quiescent state for SCL, SDA is HIGH
Start: Master sends SDA low while keeps SCL high
Master sends address of slave (7-bits) on next 7 clocks
Master sends read/write request bit
  0 (write to slave), 1 (read from slave)
Slave ACKs by pulling SDA low on next clock

## Slide 20: I2C Protocol
Master transfers one-byte of data to slave on next 8 clock pulses
  Clock is controlled by master
Data receipt is ACKed by slave on 9th pulse by pulling SDA low
When slave releases, SDA master can send next byte
At the end of transmission, Master sets a Stop condition by making a low to high transition on SDA with SCL is high

## Slide 21: Timing Diagram of I2C Protocol
Data transfer initiated with a START bit (S) signaled by SDA being pulled low while SCL stays high.
SDA sets 1st data bit level, keeping SCL low (blue)
Data is sampled (received) when SCL rises (green)
This process repeats: SDA transitioning while SCL is low, and data being read while SCL is high
A STOP bit (P) is signaled when SDA is pulled high while SCL is high
(wikipedia)

## Slide 22: I2C Transaction
Transmitter/receiver differs from master/slave
  Master initiates transactions
  Slave responds
Transmitter sets data on SDA line, slave acks
  For a read, slave is transmitter and master acks
  For a write, master is transmitter, and slave acks

## Slide 23: Arbitration
Two transmitters may start transmission at about the same time  need arbitration
  If one transmitter sets SDA to 1 (not driving a signal) and a second transmitter sets it to 0 (pull to ground), the result is that the line is low.
  The first transmitter observes that the level of the line is different from that expected. It concludes that another node is transmitting and it loses arbitration
  In the meantime, the other node has not noticed any difference between the expected and actual levels on SDA, and therefore continues transmission

## Slide 24: Accessing MMA8451Q with I2C
The registers embedded inside the MMA8451Q are accessed through the I2C serial interface
Single byte read
  MCU first addresses MMA8451Q ($1D) and then transmits the address of the register to read
  MCU transmits a repeated start condition (SR) and then addresses MMA8451Q with R/W bit = 1 for a read
  MMA8451Q acks and transmits data from requested register

## Slide 25: Accessing MMA8451Q with I2C
Multiple byte read
  After following the steps of a single byte read, multiple bytes of data can be read from sequential registers after each MMA8451Q acknowledgment (AK) is received until a no acknowledge (NAK) occurs from the Master followed by a stop condition (SP) signaling an end of transmission.

## Slide 26
Sample code next week