## Slide 1: CS4101 Introduction to Embedded Systems Lab 10: Timer and Interrupt
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Introduction
In this lab, we will learn
  Timer and interrupt of MQX

## Slide 3: Timers
Create timer component:
  A timer component and associated Timer task can be explicitly created by calling _timer_create_component() with the priority and stack size for Timer task.
  Timer task manages timer queues and provides a context for notification functions.
Start timers:
  Start a timer with calls such as _timer_start_periodic_at() _timer_start_oneshot_after_ticks()
  MQX then inserts a timer request into the queue of outstanding timers.
  When the timer expires, the notification function runs.

## Slide 4: Example of Timers
Simulate a LED being turned on and off every second
  One timer turns the LED on, and another turns it off.
  Each timer has a period of 2 seconds with an offset of 1 second between them.
  Task runs for 6 seconds.

## Slide 5: Example of Timers (1/3)
#include <mqx.h> #include <bsp.h> #include <fio.h> #include <timer.h> #define TIMER_TASK_PRIORITY 2 #define TIMER_STACK_SIZE 2000 #define MAIN_TASK 10 MQX_FILE_PTR port_file_btn1; extern void main_task(uint32_t); void btn_1_INT_callback(void); const TASK_TEMPLATE_STRUCT MQX_template_list[] = { /* Task Index, Function, Stack, Priority, Name, Attributes, Param, Time Slice */ { MAIN_TASK, main_task, 2000, 8, "Main", MQX_AUTO_START_TASK, 0, 0 }, { 0 } };
Notes: 4
4

## Slide 6: Example of Timers (2/3)
static void LED_on(_timer_id id, void* data_ptr, MQX_TICK_STRUCT_PTR tick_ptr) { /* turn on LED */ } static void LED_off(_timer_id id, void* data_ptr, MQX_TICK_STRUCT_PTR tick_ptr) { /* turn off LED */ } void main_task(uint32_t initial_data) { MQX_TICK_STRUCT ticks, dticks; _timer_id on_timer, off_timer; uint_8 time = 6; // total running time in seconds _timer_create_component(TIMER_TASK_PRIORITY, TIMER_STACK_SIZE);
Notes: 5
5

## Slide 7: Example of Timers (3/3)
_time_init_ticks(&dticks, 0); _time_add_sec_to_ticks(&dticks, 2); // 2 seconds _time_get_elapsed_ticks(&ticks); _time_add_sec_to_ticks(&ticks, 1); // cur time + 1s on_timer = _timer_start_periodic_at_ticks(LED_on, 0, TIMER_ELAPSED_TIME_MODE, &ticks, &dticks); _time_add_sec_to_ticks(&ticks, 1); // cur time + 2s off_timer = _timer_start_periodic_at_ticks(LED_off, 0, TIMER_ELAPSED_TIME_MODE, &ticks, &dticks); _time_delay(time * 100); // wait 6 seconds _timer_cancel(on_timer); _timer_cancel(off_timer); _task_block(); }
Notes: 6
6

## Slide 8: MQX Interrupts
An MQX ISR is not a task. It is a small routine that reacts to hardware interrupts or exceptions
There is a kernel ISR (_int_kernel_isr()) that runs before any other ISR
(MQX RTOS User’s Guide)

## Slide 9: Initializing Interrupt Handling
Application can replace the ISR with an application-defined, interrupt-specific ISR with _int_install_isr()
  interrupt number
  pointer to the ISR function
  Pointer to data to be passed as first parameter to the ISR
An application-defined ISR usually signals a task using mechanisms such as event or semaphore
  The will then be dequeued from a task queue and put in the task’s ready queue

## Slide 10: Example of Button Interrupt
#if defined BSP_BUTTON1 #define PIN_BTN1 GPIO_PIN_STRUCT pin_btn1[] = { BSP_BUTTON1 ¦ GPIO_PIN_IRQ_FALLING, GPIO_LIST_END}; #endif void Main_task(uint32_t initial_data) { //gpio sw1 port_file_btn1 = fopen("gpio:read", (char*) &pin_btn1 ); ioctl(port_file_btn1, GPIO_IOCTL_SET_IRQ_FUNCTION, (void*)btn_1_INT_callback); } void btn_1_INT_callback(void) { printf("BTN_1\n"); }

## Slide 11: Example of Interrupts (1/3)
Install an ISR that will call the previous ISR, which is the BSP-provided periodic timer ISR.
#include <mqx.h> #include <bsp.h> #define MAIN_TASK 10 extern void main_task(uint_32); extern void new_tick_isr(pointer); const TASK_TEMPLATE_STRUCT MQX_template_list[] = { /* Task Index, Function, Stack, Priority, Name, Attributes, Param, Time Slice */ { MAIN_TASK, main_task, 2000, 8, "Main", MQX_AUTO_START_TASK, 0, 0 }, { 0 } };

## Slide 12: Example of Interrupts (2/3)
typedef struct my_isr_struct { pointer OLD_ISR_DATA; void (_CODE_PTR_ OLD_ISR)(pointer); _mqx_uint TICK_COUNT; } MY_ISR_STRUCT, _PTR_ MY_ISR_STRUCT_PTR; void new_tick_isr(pointer user_isr_ptr) { MY_ISR_STRUCT_PTR isr_ptr; isr_ptr = (MY_ISR_STRUCT_PTR)user_isr_ptr; isr_ptr->TICK_COUNT++; /* Chain to the previous notifier */ (*isr_ptr->OLD_ISR)(isr_ptr->OLD_ISR_DATA); }
Notes: 11
11

## Slide 13: Example of Interrupts (3/3)
void main_task(uint_32 initial_data) { MY_ISR_STRUCT_PTR isr_ptr; isr_ptr = _mem_alloc_zero((_mem_size)sizeof(MY_ISR_STRUCT)); isr_ptr->TICK_COUNT = 0; isr_ptr->OLD_ISR_DATA = _int_get_isr_data(BSP_TIMER_INTERRUPT_VECTOR); isr_ptr->OLD_ISR = _int_get_isr(BSP_TIMER_INTERRUPT_VECTOR); _int_install_isr(BSP_TIMER_INTERRUPT_VECTOR, new_tick_isr, isr_ptr); _time_delay_ticks(200); printf("\nTick count = %d\n", isr_ptr->TICK_COUNT); _task_block(); }
Notes: 12
12

## Slide 14: Basic Lab
Create a print task, which print “Hello, World!” every second continuously.
Use interrupt to monitor button1 and button2.
  When button1 is pressed, flash the red LED (ON 0.3 sec and OFF 0.7 sec). Turn off the LED when it is released.
  When button2 is pressed, flash the green LED (ON 0.5 sec and OFF 0.5 sec). Turn off the LED when it is released.
Note that the print task must print “Hello, World!” even when the buttons are pressed.
Hint1: create one task to handle one event and make all events interrupt-driven
Hint2: add in user_config.h →#define MQX_USE_TIMER 1

## Slide 15: Bonus Lab
Implement a game to measure your responsiveness
  The Tower system flashes green LED at 1 sec
  You press button1 to stop LED flashing and start a new run of the game
  The Tower system waits for a random time to turn on the red LED. When you see the red LED is on, press button2
  If the interval from LED on to button2 press is smaller than a threshold, both red and green LED flash at 1 sec. Otherwise, red LED flash at 0.5 sec. Your response time is also printed on the screen.
  After 5 sec, return to flashing green LED at 1 sec and wait for next run