## Slide 1: CS4101 Introduction to Embedded Systems Lab 12: Device Drivers
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Introduction
In this lab, we will learn
  Basics of device drivers of MQX
  To create and install a null IO driver
  To develop a driver for the 3-axis accelerometer

## Slide 3: Basics of I/O Device Drivers

## Slide 4: I/O Device Drivers
Dynamically installed software packages that provide a direct interface to hardware
Driver installation:
  Each device driver has a driver-specific installation function, io_device_install(), which is called in init_bsp.c under “mqx\source\bsp\” directory.
  The installation function then calls _io_dev_install() to register the device with MQX.
  To install a new device driver, the init_bsp.c needs to be modified and the BSP rebuilt

## Slide 5: I/O Device Drivers
Device names
  Device name must end with “:”, e.g. _io_mfs_install("mfs1:" ...)
  Characters following “:” are information passed to device driver by fopen() call, e.g., fopen("mfs1:bob.txt") opens file bob.txt on device mfs1:
I/O device drivers must provide following services:
  _io_device_open: required
  _io_device_close: required
  _io_device_read: optional
  _io_device_write: optional
  _io_device_ioctl: optional

## Slide 6: Null Driver
The null device driver is an I/O device that functions as a device driver but does not perform any work.
  Code at “mqx\source\io\io_null\”

## Slide 7: Null Driver
_mqx_uint _io_my_null_install(char_ptr identifier) /* “idetifier” identifies the device for fopen */ { _mqx_uint result; result = _io_dev_install(identifier, _io_my_null_open, _io_my_null_close, _io_my_null_read, _io_my_null_write, _io_my_null_ioctl, NULL); return result; }
Notes: 6
6

## Slide 8: Null Driver
/* This function is called when the user calls fopen. It prepares the driver for subsequent read, write, and ioctl operations.*/ _mqx_int _io_my_null_open(MQX_FILE_PTR fd_ptr, char_ptr open_name_ptr, char_ptr flags) { /* Nothing to do */ return(MQX_OK); }
Notes: 7
7

## Slide 9: Null Driver
_mqx_int _io_my_null_read(MQX_FILE_PTR fd_ptr, char_ptr data_ptr, _mqx_int num) { /* Body */ return(0); } /* Endbody */ _mqx_int _io_my_null_ioctl(MQX_FILE_PTR fd_ptr, _mqx_uint cmd, pointer param_ptr) { /* Body */ return IO_ERROR_INVALID_IOCTL_CMD; } /* Endbody */ ...
Notes: 8
8

## Slide 10: Using Null Driver
#include <my_null_io.h> #define MY_TASK 5 extern void my_task(uint_32); TASK_TEMPLATE_STRUCT MQX_template_list[] = { {MY_TASK, my_task, 1500, 9, "null_test", MQX_AUTO_START_TASK, 0, 0}, {0} }; void my_task(uint_32 initial_data) { FILE_PTR null_file; uint_8 data[10]; if (IO_OK != _io_my_null_install("null:")) { printf("Error opening Null\n"); }
Notes: 9
9

## Slide 11: Using Null Driver
if (NULL == (null_file = fopen("null:", NULL ))) { printf("Opening NULL device driver failed.\n"); _mqx_exit(-1); } if (write(null_file, data, 4 ) != 4) { printf("Writing to NULL driver failed.\n"); _mqx_exit(-1); } fclose(null_file); printf ("NULL driver working\n"); _mqx_exit(0); }
Notes: 10
10

## Slide 12: Installing a Null Device Driver
The Freescale MQX software solution includes several I/O device drivers that can be used as a reference to develop your own.
These drivers are located in your default installation folder (referred to in this document as “<MQX_folder>”) inside the following path:
<MQX_folder>\mqx\source\io

## Slide 13
Under <mqx folder>/mqx/source/io, create a folder called “my_null_io” to contain your device driver.

## Slide 14
Under the “my_null_io” folder, put the following 3 files: ionulprv.h, my_null_io.c, my_null_io.h

## Slide 15
Drag-and-drop
Drag-and-drop the whole my_null_io folder to your Codewarrior project inside the IO Drivers folder.
bsp_twrk60d100m/Peripheral IO Drivers

## Slide 16
When you finish the drag-and-drop action, you will see the following.

## Slide 17
The projects will execute a .bat file, which, among other things, copies header files to the output directory. This file is located at: <mqx folder>\mqx\build\bat\bsp_twrk60d100m

## Slide 18
Add the following line to the file：
copy "%ROOTDIR%\mqx\source\io\my_null_io\my_null_io.h" "%OUTPUTDIR%\my_null_io.h" /Y

## Slide 19: Basic Lab I
Test the Null Driver
This device driver can be used by adding the following header to your application:
#include <my_null_io.h>
New a mqx project and add #include <my_null_io.h> to see if it can be built successfully or not.

## Slide 20: Basic Lab II
Create a driver for the 3-axis accelerometer by providing the five driver services.
  The read service should return the 6 bytes of data
  There is no need to provide the write service
  The control service can set to catch 8-bit or 14-bit data from the 3-axis accelerometer
Create a new project to print the 3-axis value by calling the 3-axis accelerometer driver.

## Slide 23
Write_I2C(I2C_ACCELEROMETER_ADDRESS,0x2A,0x03);
On 0x03 mode, the MSB value of 3-axis is meaningful.
So you need to catch the MSB data of 3-axis when reading the accelerometer.

## Slide 24: 3-axis Original Value
The measured acceleration data are stored in the OUT_X_MSB, OUT_Y_MSB, OUT_Z_MSB registers as 2’s complement 8-bit numbers.
0
0
0
0
0
0
0
0
Sign bit
Data bit
Reference : http://en.wikipedia.org/wiki/Two%27s_complement

## Slide 25: Bonus
Use a button to toggle a flag that selects the return value from _io_null_read().
  If the flag is equal to 0, then return the value of the 3 axis- accelerometer as in Basic Lab.
  If the flag is 1, then return additionally the inclination, e.g., right, left, front, back.
  To do this, you have to add a control function using _io_null_ioctl(), which is called when the button is pushed.
X-axis
Y-axis
Z-axis
Regular gravity value will be between ±65