## Slide 1: CS4101 Introduction to Embedded Systems Lab 13: Task Synchronization
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Introduction
In this lab, we will learn
  To synchronize tasks using synchronization primitives of MQX

## Slide 3: Sample Code: Reader-Writer
NUM_BUFFERS buffers
NUM_WRITERS writer tasks:
  Read data from 3-axis accelerometer
  Fill the first empty buffer with the received data
1 reader task:
  Find the first filled buffer and empty it
Synchronization among writers and reader: each buffer is given three flags
  Assigned = 1: buffer is assigned to a writer task for writing
  Filled = 1: buffer is filled with data and is ready for read
  Emptied = 1: buffer is empty and is ready for write

## Slide 4: Tasks and Buffers
…
…
k writer tasks
(read 3-axis data)
1 reader task
n buffers
semaphore
(count = n)
Flags of buffers:
Assigned
Filled
Emptied
Suppose
k > n

## Slide 5: Writer and Reader Task
Writer task:
  Read data from 3-axis accelerometer
  Find the first unassigned buffer and mark it “assigned”
  Wait until the buffer is empty and mark it not “emptied”
  Fill the buffer with data
  Mark the buffer “filled” and “unassigned”
Reader task:
  Find the first “filled” buffer and mark it not “filled”
  Read the data from the buffer
  Mark the buffer “emptied”
Semaphore index_sem to control at most NUM_BUFFERS writer tasks in filling the buffers

## Slide 6: Sample Code: Main
#include <mqx.h> #include <bsp.h> #include <sem.h> #include <fio.h> uchar buffer[NUM_BUFFERS][ARRAY_SIZE]; int Assigned[NUM_BUFFERS]; int Filled[NUM_BUFFERS]; int Emptied[NUM_BUFFERS]; const TASK_TEMPLATE_STRUCT MQX_template_list[] = { { MAIN_TASK, main_task, 2000, 8, "main", MQX_AUTO_START_TASK, 0, 0 }, { WRITE_TASK, write_task, 2000, 8, "write", MQX_TIME_SLICE_TASK, 0, 10 }, { READ_TASK, read_task, 2000, 8, "read", MQX_TIME_SLICE_TASK, 0, 10 }, { 0 } };

## Slide 7: Sample Code: Main
void main_task(uint_32 initial_data) { _task_id task_id; /* Initialize the flags */ for (i = 0; i < NUM_BUFFERS; i++) { Assigned[i] = 0; Filled[i] = 0; Emptied[i] = 1; } /* Create the semaphores */ if(_sem_create_component(1,1,6) != MQX_OK) { ... } if(_sem_create("sem.index",NUM_BUFFERS,0)!= MQX_OK){} /* Create the tasks */ for (i = 0; i < NUM_WRITERS; i++) { task_id = _task_create(0, WRITE_TASK, (uint_32)i);} task_id = _task_create(0,READ_TASK, 0); _task_block(); }

## Slide 8: Sample Code: Writer
void void write_task(uint_32 initial_data){ pointer index_sem; if(_sem_open("sem.index",&index_sem) != MQX_OK) {...} while (TRUE) { if(_sem_wait(index_sem, 0) != MQX_OK) {...} for(i = 0; i < NUM_BUFFERS; i++){ if(Assigned[i] == 0) { Assigned[i] = 1; while(Emptied[i] == 0){ ... /* wait */ } Emptied[i] = 0; for(j = 0; j < ARRAY_SIZE; j++){ buffer[i][j] = ... /* fill the buffer */ } Assigned[i] = 0; Filled[i] = 1; break;} } _sem_post(index_sem); } }
CS

## Slide 9: Sample Code: Reader
void read_task(uint_32 initial_data) { pointer index_sem; int i; while (TRUE) { for(i = 0; i < NUM_BUFFERS; i++){ if(Filled[i] == 1){ Filled[i] = 0; ... /* read and empty the buffer */ Emptied[i] = 1; break; } } } }

## Slide 10: Semaphores & RoundRobin: user_config.h
#define MQX_USE_SEMAPHORES 1 #define MQX_HAS_TIME_SLICE 1
1. Add the definition in
bsp_twrk60d100m/twrk60d100m/user_config.h
2. Rebuild the bsp and psp library
1
2
2
Notes: 9
9

## Slide 11: Basic Lab
There is a race condition in the sample code. Use semaphores or mutex to protect the critical data structures.
  [Hint]: First check whether there is a race condition between writer and reader tasks by examining their common variables. Next, do the same between writer tasks.
Modify the writer code to minimize the time spend in the critical section, i.e., move all non-critical operations out of the critical section.

## Slide 12: Bonus Lab
In the original sample code, the writer task, after grabbing a buffer by finding the first unassigned buffer, waits for Emptied[i] == 1 using a while-loop. This is basically a spin-wait, which wastes CPU. Use Events to let the task blocked wait.