## Slide 1: CS4101 嵌入式系統概論 Introduction to LaunchPad
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
Materials from MSP430 Microcontroller Basics, John H. Davies, Newnes, 2008

## Slide 2: Outline
MSP430 LaunchPad
MSP430 Microcontroller
  Processor
  Memory
  I/O
First Program on LaunchPad
  C
  Assembly
LaunchPad Development Environment

## Slide 3: MSP430 LaunchPad Development Kit
LaunchPad development board
Mini-USB cable, 10-pin PCB connectors
2 MSP430 MCUs: MSP430G2553, MSP430G2452
Micro Crystal 32.768kHz Oscillator
Notes: 開發板: many peripherals, pins are linked to outside for easy connections
How to read the pin id of a chip?

## Slide 4: MSP430 Microcontroller
LaunchPad development board uses microcontroller such as MSP430G2553 and MSP430G2452
Microcontroller:
  A small computer on a single IC containing a processor core, memory, programmable I/O peripherals
MSP430 microcontroller:
  Incorporates a 16-bit RISC CPU, peripherals, and a flexible clock system that are interconnected using a von-Neumann common memory address bus (MAB) and memory data bus (MDB)
Notes: 比較前一頁的開發板, 上面的電路很簡單, 幾乎沒有其他元件

## Slide 5: MSP430 Microcontroller
MSP430G2553 outside view (pin-out):
  20-pin version
  VCC , VSS : supply voltage and ground
  P1.0~P1.7, P2.0~P2.7 are for digital input and output, grouped into ports P1 and P2
  TA0CLK, TA0.0, and TA0.1 are associated with Timer0_A

## Slide 6: MSP430 Microcontroller
MSP430G2553 outside view: (cont’d)
  A0~A7 inputs to the analog-to-digital (ADC) converter
  VREF is the reference voltage for the ADC converter
  ACLK and SMCLK are outputs for the microcontroller’s clock signals
  UCA0RXD and UCA0TXD are used for the universal serial interface
  XIN and XOUT are the connections for a crystal
  RST is an active low reset signal
  NMI is the non-maskable interrupt input

## Slide 7: MSP430G2553 Inside View
X
No P3 for 20-pin devices
Memory-mapped I/O
P1REN
…
P1IN
P1OUT
MOV.W #0x100,P1OUT
LED
Notes: Go through all the components once and explain their meanings

## Slide 8: MSP430 Instruction Set
Instruction set architecture:
  RISC with 51 instructions, 3 formats, and 7 addressing modes
Notes: Sample some of the entries

## Slide 9: MSP430 CPU Registers
Sixteen 16-bit registers
  R0, R1, R2, and R3: program counter, status registers, stack pointer, constant generator (provides six most used immediate values and reduces code size)
  R4 to R15 are working registers for general use
Notes: Ask the meanings of the special registers

## Slide 10: MSP430 Memory Organization
Memory:
  Word and byte addressing and instruction formats
  16-bit memory address bus (MAB) allows direct access and branching throughout entire memory range
  16-bit memory data bus (MDB) allows direct manipulation of word-wide arguments
  Direct memory-to-memory transfers without intermediate register holding

## Slide 11: MSP430 Memory Organization
Little-endian ordering: The low-order byte is stored at the lower address and the high-order byte at the higher address
Aligned words:
The address of a word is the address of the byte with the lower address, which must be even
16-bit addresses, addressing to bytes

## Slide 12: MSP430G2553 Memory Map
Information memory: A 256B block of flash memory that is intended for storage of nonvolatile data, including serial numbers to identify the equipment
Flash/ROM
(16 KB)
RAM
(512 bytes)
Flash/ROM
(256 bytes)
?
Notes: 11
Refer back to page 6 to see the blocks; Ask where the peripherals go?

## Slide 13: MSP430 Input/Output
Simple digital input and output of MSP430 (GPIO) takes place through sets of pins on the package of the IC called ports
  20-pin MSP430G2553 has two ports: P1 (8 bits: P1.0~P1.7), P2 (8 bits: P2.0~P2.7)
  Typical pins can be configured for either input or output and some inputs may generate interrupts when the voltage on the pin changes
  The ports appear to the CPU as registers (memory-mapped I/O ), where each bit corresponds to a pin and a port may be associated to many registers for different purposes (next page)

## Slide 14: Registers Associated with Port 1
Reg. | Addr. | Func. | Description
P1IN | 020h | Input from port 1 | The 8 bits of data from port P1
P1OUT | 021h | Output to port 1 | Outputs 8 bits of data to port P1
P1DIR | 022h | Direction of port 1 data transfer | Bits written as 1 (0) configure corresponding pin for output (input)
P1SEL | 026h | Select function for port 1 | Bits written as 1 configure the corresponding pin for use by the specialized peripheral; 0 configure general-purpose I/O
Notes: 13

## Slide 15: Outline
MSP430 LaunchPad
MSP430 Microcontroller
  Processor
  Memory
  I/O
First Program on LaunchPad
  C
  Assembly
LaunchPad Development Environment

## Slide 16: LaunchPad Development Board
Embedded Emulation
6-pin eZ430 Connector
Part and Socket
Crystal Pads
Power Connector
Reset Button
LEDs and Jumpers
P1.0 & P1.6
P1.3 Button
Chip Pinouts
USB Emulator Connection
Notes: Purpose of emulation

## Slide 17: LaunchPad Pinouts
On-board features of LaunchPad are pinned in the following fashion:
  LED1 (red) = P1.0
  LED2 (green) = P1.6
  Switch1 = P1.3
  Switch2 = Reset
  Timer UART Transmit = P1.1
  Timer UART Receive = P1.2
In order to blink the Red and Green LEDs, we have to set Ports 1.0 and 1.6 as outputs, and toggle them

## Slide 18: Sample Code (msp430g2xx3_1.c)
#include <msp430x2553.h> void main(void) { WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer P1DIR ¦= 0x41; // set P1.0 & P1.6 to outputs //(red & green LEDs) for(;;) { volatile unsigned int i; P1OUT ^= 0x41; // Toggle P1.0 & P1.6 with XOR i = 50000; // Delay do (i--); while (i != 0); } }
Notes: 17

## Slide 19: Sample Code (cont’d)
Configure the LED connected to the GPIO line
  The green and red LED are located on Port 1 Bit 0 and Bit 6  make these pins to be output  P1DIR set to 0x41 = 01000001
To turn on/off LED, set bit in register to 1/0
  Use XOR to toggle P1OUT
P1OUT ^= 0x41; // toggle P1.0 & 6 on/off
WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer P1DIR ¦= 0x41; // P1.0 & 6 outputs
0100 0001
Notes: 18

## Slide 20: Characteristics of Sample Code
No printf(), no GUI operations
Do not end
Do I/O mainly
  More on control of peripherals through their special registers  details of individual bits, bytes, words are important  manipulations of bits, bytes, words
Complete ownership of CPU
No OS

## Slide 21: Notes of Sample Code
volatile variable:
  volatile unsigned int i;
  The variable may appear to change “spontaneously,” with no direct action by the user’s program  may be due to memory-mapped I/O devices
  Compiler must be careful in optimizing it
    Ex.: should not keep a copy of the variable in a register for efficiency; should not assume the variable remains constant when optimizing the structure of the program, e.g., rearranging loops
  The peripheral registers associated with the input ports should be declared as volatile

## Slide 22: Notes of Sample Code
Example from wikipedia:
  Optimizing compiler will think that foo is never changed and will optimize the code into
static int foo; void bar(void) { foo = 0; while (foo != 255) ; }
static int foo; void bar(void) { foo = 0; while (true) ; }
The volatile keyword in declaration of foo prevents this optimization

## Slide 23: Notes of Sample Code
Bit manipulation:
  Important ISA feature for embedded processors
  Bit mask: set a bit P1OUT = P1OUT | BIT3 clear a bit P1OUT &= ~BIT3 toggle a bit P1OUT ˆ= BIT3
  Bit field: struct { unsigned short TAIFG:1; unsigned short TAIE:2; unsigned short TACLR:5; } TACTL_bit;
Set with TACTL_bit.TAIFG = 1

## Slide 24: Other Aspects of Embedded C
Programs for small embedded systems tend not to contain a lot of complicated manipulation of complex data objects
  Much code is usually devoted to the control of peripherals through their special registers
  Details of individual bits, bytes, words are important
Important operations
  Shifting and rotating bits
  Bit-level Boolean logic (A && B) and bitwise operator (A & B)
  Bit mask for testing and modifying individual bits

## Slide 25: Other Aspects of Embedded C
Union for manipulating individual bits or the whole byte/word as a unit
  union {
  unsigned short TACTL; // Timer_A Control
  struct {
  unsigned short TAIFG : 1; // Timer_A counter interrupt flag
  unsigned short TAIE : 1; // Timer_A counter interrupt enable
  unsigned short TACLR : 1; // Timer_A counter clear
  unsigned short : 1;
  unsigned short TAMC : 2; // Timer_A mode control
  unsigned short TAID : 2; // Timer_A clock input divider
  unsigned short TASSEL : 2; // Timer_A clock source select
  unsigned short : 6;
  } TACTL_bit;
  } TimerA;
bit 0

## Slide 26: Sample C Code: Blinking Only Red LED
#include <msp430x2553.h> int main(void) { WDTCTL = WDTPW ¦ WDTHOLD; // Stop watchdog timer P1DIR ¦= 0x01; // Set P1.0 as output for(;;) { volatile unsigned int i; // prevent optimization P1OUT ^= 0x01; // Toggle P1.0 using XOR i = 10000; // SW Delay do i--; while(i != 0); } return 0; }

## Slide 27: Assembly Code: Blinking Only Red LED
ORG 0F800h ; Program Toggle Toggle mov.w #0280h,SP ; Initialize SP StopWDT mov.w #WDTPW+WDTHOLD,&WDTCTL ; Stop WDT SetupP1 bis.b #001h,&P1DIR ; P1.0 output Mainloop xor.b #001h,&P1OUT ; Toggle P1.0 Wait mov.w #050000,R15 ; Delay to R15 L1 dec.w R15 ; Decrement R15 jnz L1 ; Delay over? jmp Mainloop ; Again ; Interrupt Vectors ORG 0FFFEh ; MSP430 RESET Vector DW Toggle END
Notes: Load the program starting 0F800h (flash memory) and upward
Initialize SP to 0400h, just above RAM; stack grow downward (refer to page 11)
bis.b = bit set on a byte
Interrupt vector at 0FFFEh
P1DIR = 022h, P1OUT = 021h, P2IN = 020h, P1SEL = 026h
26

## Slide 28: Notes of Assembly Code
Where to store the program in memory?
  The code should go into the flash ROM and variables should be allocated in RAM
   code at start of flash: 0F800h
   stack at end of RAM: 0280h (grow downward)
Where should execution of the program start?
  Address of the first instruction to be executed is stored at a specific location in flash, called reset vector, which occupies the 2 bytes at 0FFFEh:0FFFFh
  Use an ORG 0xFFFE directive to tell the assembler where to store the reset vector
  The DW directive (“define word”) tells the assembler to store the following word (2 bytes) in memory

## Slide 29: Notes of Assembly Code
The style of program shown above is known as absolute assembly because the memory addresses are given explicitly in the source using ORG directives
An alternative is to rely on the linker/loader to determine the address, which is called relocatable assembly
  The program must not contain absolute addresses, e.g., jump to a 16-bit address, only relative addresses, e.g., relative to current program counter

## Slide 30: Machine Code: Blinking Only Red LED
23 int main(void) { c05e: 8321 DECD.W SP WDTCTL = WDTPW ¦ WDTHOLD; c060: 40B2 5A80 0120 MOV.W #0x5a80,&Watchdog_Timer_WDTCTL P1DIR ¦= 0x01; c066: D3D2 0022 BIS.B #1,&Port_1_2_P1DIR 31 P1OUT ^= 0x01; $C$L1: c06a: E3D2 0021 XOR.B #1,&Port_1_2_P1OUT i = 10000; c06e: 40B1 2710 0000 MOV.W #0x2710,0x0000(SP) 34 do i--; $C$L2: c074: 8391 0000 DEC.W 0x0000(SP) 36 } c078: 9381 0000 TST.W 0x0000(SP) c07c: 27F6 JEQ ($C$L1) ......

## Slide 31: Outline
MSP430 LaunchPad
MSP430 Microcontroller
  Processor
  Memory
  I/O
First Program on LaunchPad
  C
  Assembly
LaunchPad Development Environment

## Slide 32: Code Composer Studio (CCS)
An Integrated Development Environment (IDE) based on Eclipse
Integrated “Debugger” and “Editor” – IDE
  Edit and Debug have the own “perspectives” (menus, windows)
Contains all development tools – compilers, TI-RTOS kernel and includes one target – the Simulator

## Slide 33: Code Composer Studio (CCS)
Compiler
Asm
.c
.asm
.obj
.asm
Edit
Debug
Standard Runtime Libraries
.out
.lib
.map
User.cmd
TI-RTOS
Libraries
TI-RTOS
Config
(.cfg)
Bios.cmd
Launch Pad
EVM
Stand Alone Emulator (MSP430 FET)
Target Cfg File
.ccxml
Link

## Slide 34: CCS GUI – EDIT Perspective
Project Explorer
Project(s)
Source Files
Source EDIT’ing
Tabbed windows
Color-coded text
Outline View
Declarations and functions
Menus & Buttons
Specific actions related to EDIT’ing
Perspectives
EDIT and DEBUG

## Slide 35: CCS GUI – DEBUG Perspective
DEBUG Windows
Watch Variables
Memory Browser
PC execution point
Console Window
Menus & Buttons
Related to DEBUG’ing
Play, Pause, Terminate
Connection Type
Specified in Target Cfg file
What options do users have when connecting to a target?
This window also provides a “call” stack

## Slide 36: Notes on Code Composer Studio
Download code to LaunchPad from CCS
  After application program is entered and all the changes are made, we can download this code to the MSP430 MCU plugged into LaunchPad’s DIP target socket
  Make sure LaunchPad is plugged in to your PC
  Next, click the “Debug” button, which will check the code and load it into the MSP430 device
  When the code successfully loads, we will enter the Debug view of CCS. We can execute the code by clicking the green “Run” arrow and start debugging

## Slide 37: Summary
Basic structure of MSP430 LaunchPad:
  MSP430 CPU and memory
  MSP430 I/O ports and LaunchPad I/O connections
First MSP430 program
  C and assembly
  Importance of bit/byte manipulation
  Management and allocation of memory