## Slide 1: CS4101 嵌入式系統概論 General Purpose IO
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
Materials from MSP430 Microcontroller Basics, John H. Davies, Newnes, 2008

## Slide 2: LaunchPad Development Board
Part and Socket
Crystal Pads
Power Connector
Reset Button
P1.3 Button
Chip Pinouts
USB Emulator Connection
LEDs P1.0 & P1.6
6-pin eZ430 Connector
Embedded Emulation

## Slide 3: Recall: Sample Code for Output
#include <msp430x2553.h> void main(void) { WDTCTL = WDTPW + WDTHOLD; // Stop watchdog P1DIR ¦= 0x41; // set P1.0 & 6 to outputs for(;;) { volatile unsigned int i; P1OUT ^= 0x41; // Toggle P1.0 & P1.6 i = 50000; // Delay do (i--); while (i != 0); } }

## Slide 4: Recall: Memory-Mapped I/O
X
No P3 for 20-pin devices
P1REN
…
P1IN
P1OUT
MOV.W #0x100,P1OUT
LED
Notes: Go through all the components once and explain their meanings

## Slide 5: Configuring the I/O Ports
Registers (Mem Addr) | Functions | Descriptions
P1IN (0x0020) | Port 1 input | This is a read-only register that reflects the current state of the port's pins.
P1OUT (0x0021) | Port 1 output | The values written to this read/write register are driven out to corresponding pins when they are configured to output.
P1DIR (0x0022) | Port 1 data direction | Bits written as 1 (0) configure the corresponding pins for output (input).
P1SEL (0x0026) | Port 1 function select | Bits written as 1 (0) configure corresponding pins for use by the specialized peripheral (for general-purpose I/O).
P1REN (0x0027) | Port 1 resistor enable | Bits set in this register enable pull-up/down resistors on the corresponding I/O pins.

## Slide 6: MSP430 GPIO
GPIO = General Purpose Bit Input/Output
8-bit I/O ports
Each pin is individually controllable
Controlled by memory-mapped registers
 | P1.7 | P1.6 | P1.5 | P1.4 | P1.3 | P1.2 | P1.1 | P1.0
I/O Port 1 | Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0

## Slide 7: PxDIR (Pin Direction): Input or Output
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
P1IN |  |  |  |  |  |  |  | 
P1OUT |  |  |  |  |  |  |  | 
P1DIR | 1 |  |  |  |  |  |  | 1
P1IN.7
P1OUT.7
P1DIR.7
“1”
PxDIR.y: 0 = input 1 = output
Register example: P1DIR &= 0x81;

## Slide 8: GPIO Output
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
P1IN | X |  |  |  |  |  |  | 
P1OUT | 1 |  |  |  |  |  |  | 
P1DIR | 1 |  |  |  |  |  |  | 
P1IN.7
P1OUT.7
P1DIR.7
“1”
“1”
“1”
PxOUT.y: 0 = low 1 = high
Register example: P1OUT &= 0x80;

## Slide 9: Sample Code for Input (MSP430g2553)
#include <msp430g2553.h> #define LED1 BIT0 //P1.0 to red LED #define B1 BIT3 //P1.3 to button void main(void){ WDTCTL = WDTPW + WDTHOLD; //Stop watchdog timer P1OUT ¦= LED1 + B1; P1DIR = LED1; //Set pin with LED1 to output P1REN = B1; //Set pin to use pull-up resistor for(;;){ //Loop forever if((P1IN & B1) ==0){ //Is button down? P1OUT &= ~LED1; // Yes, turn LED1 off } else{ P1OUT ¦= LED1; // No, turn LED1 on } } }
Notes: P1OUT is not initialized and must be written before configuring the pin for output.
Assume button is active low (0  pressed; 1  depressed)

## Slide 10: Problem with Input Using a Button
When the button is pressed down (closed), MSP430 will detect a 0 from the pin.
When the button is up (open), what will MSP430 detect?
Ans.: random value
 Floating

## Slide 11: Typical Way of Connecting a Button
The pull-up resistor Rpull holds input at logic 1 (voltage VCC) while button is up and logic 0 or VSS when button is down  active low
  A wasted current flows through Rpull to ground when button is down
  This is reduced by making Rpull large enough, typically 33 k

## Slide 12: Typical Way of Connecting a Button
MSP430 offers internal pull-up/down
PxREN register selects whether this resistor is used (1 to enable, 0 to disable)
  When enabled, the corresponding bit of PxOUT register selects whether the resistor pulls the input up to VCC (1) or down to VSS (0)

## Slide 13: GPIO Input
Enable resistor
 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
P1IN | x |  |  |  |  |  |  | 
P1OUT | 1 |  |  |  |  |  |  | 
P1DIR | 0 |  |  |  |  |  |  | 
P1REN | 1 |  |  |  |  |  |  | 
P1IN.7
P1OUT.7
P1DIR.7
P1REN.7
Input pins are held in high-impedance (Hi-Z) state, so they can react to 0 or 1
When not driven, Hi-Z inputs may float up/down … prevent this with pullup/pulldown resistors
PxREN enables resistors PxOUT selects pull-up (1) or -down (0)
Lower cost devices may not provide up/down resistors for all ports
up/down