## Slide 1: CS4101 嵌入式系統概論 Analog-to-Digital Converter
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
Materials from MSP430 Microcontroller Basics, John H. Davies, Newnes, 2008

## Slide 2: Recall the Container Thermometer
Container thermometer: monitor the temperature of the interior of a container
  Monitor the temperature every 5 minutes
  Flash LED alarm at 1 Hz
  If the temperature rises above a threshold, flash the LED alarm at 3 Hz and notify backend server
  If the temperature drops below a threshold, return the LED alarm to normal and notify the server
Need to know the temperature!

## Slide 3: Digitizing Temperature
Temperature is a nature phenomena, whose value vary continuously
To make it feasible for computer to handle, we need to convert it into digital signals
To transform an analog signal into a digital one, the analog-to-digital converter (ADC) samples the input at fixed interval and do the conversion
Analog signal
Digital signal
Notes: The ADC10CLK is used both as the conversion clock and to generate the sampling period. The ADC10
source clock is selected using the ADC10SSELx bits and can be divided from 1-8 using the ADC10DIVx
bits. Possible ADC10CLK sources are SMCLK, MCLK, ACLK and an internal oscillator ADC10OSC .
The ADC10OSC, generated internally, is in the 5-MHz range, but varies with individual devices, supply
voltage, and temperature. See the device-specific data sheet for the ADC10OSC specification.
The user must ensure that the clock chosen for ADC10CLK remains active until the end of a conversion. If
the clock is removed during a conversion, the operation will not complete, and any result will be invalid.
2

## Slide 4: We Have Learned …
IO
Clock System
Timer System
ADC

## Slide 5: Outline
Introduction to analog-to-digital conversion
ADC of MSP430
Sample code of using ADC10 in MSP430

## Slide 6: Analog Signals
A signal representing continuous things, e.g.
  Fluctuations in air pressure (i.e. sound) strike the diaphragm of a microphone, which causes corresponding fluctuations in a voltage or the current in an electric circuit
  The voltage or current is an "analog" of the sound
time
time
strength
voltage

## Slide 7: Analog-to-Digital Conversion
ADC: convert an analog input, e.g., a voltage V, into a binary value that the processor can handle
  The input V(t) is a continuous function, i.e., V can take any value within a permitted range and can change in any way as a function of time t
  The output V[n] is a sequence of binary values. Each has a fixed number of bits and can represent only a finite number of values
  Typically input is sampled regularly at intervals of T, so the continuous nature of time has also been lost
Of course, we also have DAC (digital-to-analog converter)!

## Slide 8: Analog-to-Digital Conversion
Digital representations of analog waveforms
Continuous time
Continuous values
Discrete time
Discrete values

## Slide 9: Sampling in Time
The value of the analog signal is measured at certain intervals in time. Each measurement is referred to as a sample
A series of “snapshots”

## Slide 10: Terminologies in Sampling
Sampling rate:
  How often analog signal is measured (samples per second, Hz), e.g. 44,100 Hz?
Sampling resolution:
  Number of bits to represent each sample (“sample word length,” “bit depth”), e.g. 16 bit
Analog Input
4 samples/cycle
8 samples/cycle
16 samples/cycle

## Slide 11: Encoding of Discrete Signals
If we use N bits to encode the magnitude of one of the discrete-time samples, we can capture 2N possible values

## Slide 12: Sampling Rate and Encoding Bits
1-bit
3-bit

## Slide 13: Outline
Introduction to analog-to-digital conversion
ADC of MSP430
Sample code of using ADC10 in MSP430

## Slide 14: Requirements of MSP430 for ADC
Provide continuous sampling of multiple analog inputs and store sampled data
ADC10AE0
INCH in ADC10CTL1

## Slide 15: Requirements of MSP430 for ADC
Provide continuous sampling of multiple analog inputs and store sampled data
SHS, ADC10SSEL, CONSEQ in ADC10CTL1

## Slide 16: Requirements of MSP430 for ADC
Provide continuous sampling of multiple analog inputs and store sampled data
Interrupt CPU on every word sampled from ADC
Use software (ISR run by the CPU) to move data from ADC (ADC10MEM) to memory

## Slide 17: Requirements of MSP430 for ADC
Provide continuous sampling of multiple analog inputs and store sampled data
Interrupt CPU when block transfer is
completed
Use hardware (Data Transfer Controller, DTC) to move data from ADC to memory
 DMA

## Slide 18: ADC in MSP430
MSP430 may contain one or more converters:
Comparator:
  Compare the voltages on its two input terminals and return 0 or 1, e.g., Comparator_A+
Successive-approximation ADC:
  Use binary search to determine the closest digital representation of the input signal, e.g., ADC10 and ADC12 to give 10 and 12 bits of output
Sigma-delta ADC:
  A more complicated ADC that gives higher resolution (more bits) but at a slower speed, e.g., SD16 and SD16_A, both of which give a 16-bit output

## Slide 19: Simplified Block Diagram of ADC10
Voltage reference
Clock sources
Conversion trigger

## Slide 20: Main Components of ADC10
Sample-and-Hold circuit:
  Vout = Vin when Vsample = 1
SAR (Successive-Approximation Register):
  10-bit
  Result written to ADC10MEM and raising ADC10IFG
Vin
Vout

## Slide 21: Successive-Approximation ADC
Generate internal analog signal VD/A by DAC
Compare VD/A with input signal Vin
Modify VD/A by D0D1D2…DN-1 until closest possible value to Vin is reached
Dr.-Ing. Frank Sill, Department of Electrical Engineering, Federal University of Minas Gerais, Brazil

## Slide 22: Successive-Approximation ADC
P. Fischer, VLSI-Design - ADC und DAC, Uni Mannheim, 2005

## Slide 23: Main Components of ADC10
Built-in voltage reference:
  Two selectable voltage levels, 2.5 V and 1.5 V
  Setting REFON in ADC10CTL0 register to 1 enables the internal reference
  Setting REF2_5V in ADC10CTL0 to 1 selects 2.5 V as the internal reference, otherwise 1.5 V
  After voltage reference is turned on, we must wait about 30µs for it to settle

## Slide 24: Main Components of ADC10
Triggering of sample-and-hold circuit:
  ADC10SC bit in ADC10CTL0 register, which can be set (and is thus triggered) by software, or
  OUTx from Timer_A: for periodic sampling
Capture/Compare Block 2
of Timer_A

## Slide 25: Data Transfer Controller (DTC)
Transfer conversion results from ADC10MEM to other on-chip memory locations
  Each load of ADC10MEM triggers a data transfer until a set amount
  During each DTC transfer, CPU is halted
Input channel
1.5V or 2.5V or Reference
ADC10MEM
Notes: @ userguide 22.2.1 10-Bit ADC Core ,Page 542
The eight external and four internal analog signals are selected as the channel for conversion by the analog input multiplexer.
The ADC core converts an analog input to its 10-bit digital representation and stores the result in the ADC10MEM register. The core uses two programmable/selectable voltage levels (VR+ and VR-) to define the upper and lower limits of the conversion. The digital output (NADC) is full scale (03FFh) when the input signal is equal to or higher than VR+, and zero when the input signal is equal to or lower than VR-. The input channel and the reference voltage levels (VR+ and VR-) are defined in the conversion-control memory. Conversion results may be in straight binary format or 2s-complement format.
The ADC10 core is configured by two control registers, ADC10CTL0 and ADC10CTL1. The core is enabled with the ADC10ON bit. With few exceptions the ADC10 control bits can only be modified when ENC = 0. ENC must be set to 1 before any conversion can take place.
SAR: successive approximation register
24

## Slide 26: ADC10 Interrupts
One interrupt and one interrupt vector
  When DTC is not used (ADC10DTC1 = 0), ADC10IFG is set when conversion results are loaded into ADC10MEM
  When DTC is used (ADC10DTC1 > 0), ADC10IFG is set when a block transfer completes
If both ADC10IE and GIE bits are set, then ADC10IFG generates an interrupt request
  ADC10IFG is automatically reset when interrupt request is serviced, or it may be reset by software

## Slide 27: Enabling Sampling and Conversion

## Slide 28: Steps for Single Conversion
(1) Configure ADC10, including the ADC10ON bit to enable the module.
  The ENC bit must be clear so that most bits in ADC10CTL0 and ADC10CTL1 can be changed.
(2) Set the ENC bit to enable a conversion.
  This cannot be done while the module is being configured in the previous step.
(3) Trigger the conversion.
This is done either by setting the ADC10SC bit or by an edge from Timer_A.
ADC10ON, ENC, ADC10SC are all in control register ADC10CTL0

## Slide 29: ADC10 Registers
Register | Short Form | Register Type | Addr. | Initial State
ADC10 input enable register 0 | ADC10AE0 | Read/write | 04Ah | Reset with POR
ADC10 input enable register 1 | ADC10AE1 | Read/write | 04Bh | Reset with POR
ADC10 control register 0 | ADC10CTL0 | Read/write | 01B0h | Reset with POR
ADC10 control register 1 | ADC10CTL1 | Read/write | 01B2h | Reset with POR
ADC10 memory | ADC10MEM | Read | 01B4h | Unchanged
ADC10 data transfer control register 0 | ADC10DTC0 | Read/write | 048h | Reset with POR
ADC10 data transfer control register 1 | ADC10DTC1 | Read/write | 049h | Reset with POR
ADC10 data transfer start address | ADC10SA | Read/write | 01BCh | 0200h with POR
Where the data is saved
Notes: power-on reset (PoR)
28

## Slide 30: ADC10CTL0
ideal for the temperature sensor
ideal for the temperature sensor
Notes: 29

## Slide 31: ADC10CTL0 cont’d
ADC10CTL0 = SREF_2 + ADC10SHT_1; // Reference range & SH time
Notes: The settling time for the internal reference is < 30µs. A value of 5 cycles would be 40µs.
We should allow thirteen ADC10CLK cycles before we read the conversion result.
Thirteen cycles of the 5MHz ADC10CLK is 2.6µs. Even a single cycle of the DCO/8 would be longer than that. We will leave the LED on and use the same delay so that we can see it with our eyes.
When the conversion is complete, the encoder and reference need to be turned off.
30

## Slide 32: ADC10CTL1
Notes: 31

## Slide 33: ADC10CTL1 cont’d
ADC10CTL1 = INCH_10 + ADC10DIV_0; // Temp Sensor ADC10CLK
Notes: 32

## Slide 34: Outline
Introduction to analog-to-digital conversion
ADC of MSP430
Sample code of using ADC10 in MSP430

## Slide 35: Sample Code 1 for ADC10
Repetitive single conversion:
  A single sample is made on A1 with reference to Vcc
  If A1 > 0.5*Vcc, P1.0 set, else reset.
  Software sets ADC10SC to start sample and conversion. ADC10SC automatically cleared at end of conversion.
  Use ADC10 internal oscillator to time the sample and conversion.

## Slide 36: Sample Code 1 for ADC10
#include "msp430.h" void main(void) { WDTCTL = WDTPW + WDTHOLD; // Stop WDT // H&S time 16x, interrupt enabled ADC10CTL0 = ADC10SHT_2 + ADC10ON + ADC10IE; ADC10CTL1 = INCH_1; // Input from A1 ADC10AE0 ¦= 0x02; // Enable pin A1 for analog in P1DIR ¦= 0x01; // Set P1.0 to output ADC10CTL0 ¦= ENC + ADC10SC; // Start sampling for (;;) { } } #pragma vector=ADC10_VECTOR __interrupt void ADC10_ISR(void) { if (ADC10MEM < 0x1FF) P1OUT &= ~0x01; else P1OUT ¦= 0x01; ADC10CTL0 ¦= ENC + ADC10SC; // enable sampling }
Notes: 35
Why not read ADC10MEM right after setting ADC10CTL0? While wait for interrupt?
Any one of the pins of Port 1 can be set to be an analog input. Thus up to 8 channels are available for separate ADC inputs.
Analog Enable control register ADC10AE0 will be use for enabling the corresponding input channels.
35

## Slide 37: Sample Code 2 for ADC10
Continuous sampling driven by Timer0_A
  A1 is sampled 16/second (ACLK/2048) with reference to 1.5V, where ACLK runs at 32 KHz driven by an external crystal.
  If A1 > 0.5Vcc, P1.0 is set, else reset.
  Timer0_A is run in up mode and its CCR1 is used to automatically trigger ADC10 conversion, while CCR0 defines the sampling period
  Use internal oscillator times sample (16x) and conversion (13x).

## Slide 38: Sample Code 2 for ADC10
#include "msp430.h“ int i=1; void main(void) { WDTCTL = WDTPW + WDTHOLD; // Stop WDT // TA1 trigger sample start ADC10CTL1 = SHS_1 + CONSEQ_2 + INCH_1; ADC10CTL0 = SREF_1 + ADC10SHT_2 + REFON + ADC10ON + ADC10IE; __enable_interrupt(); // Enable interrupts TA0CCR0 = 30; // Delay for Volt Ref to settle TA0CCTL0 ¦= CCIE; // Compare-mode interrupt TA0CTL = TASSEL_2 + MC_1; // SMCLK, Up mode while(i); // Wait for settle TA0CCTL0 &= ~CCIE; // Disable timer Interrupt __disable_interrupt();
Notes: 37
SHS_1: S&H triggering source  OUT1
CONSEQ_2: Conversion sequence mode select (Repeat-single-channel)
SREF_1: Select reference (VR+ = VREF+ and VR- = VSS)
ADC10SHT_2: Sample-and-hold time (6 × ADC10CLKs)
REFON: reference generator on
37

## Slide 39: Sample Code 2 for ADC10
ADC10CTL0 ¦= ENC; // ADC10 Enable ADC10AE0 ¦= 0x02; // P1.1 ADC10 option select P1DIR ¦= 0x01; // Set P1.0 output TA0CCR0 = 2048-1; // Sampling period TA0CCTL1 = OUTMOD_3; // TACCR1 set/reset TA0CCR1 = 2046; // TACCR1 OUT1 on time TA0CTL = TASSEL_1 + MC_1; // ACLK, up mode while(1); }
Timer0_A CCR1 out mode 3: The output (OUT1) is set when the timer counts to the TA0CCR1 value. It is reset when the timer counts to the TA0CCR0 value.
Notes: 38
38

## Slide 40: Sample Code 2 for ADC10
// ADC10 interrupt service routine #pragma vector=ADC10_VECTOR __interrupt void ADC10_ISR(void){ if (ADC10MEM < 0x155) // ADC10MEM = A1 > 0.5V? P1OUT &= ~0x01; // Clear P1.0 LED off else P1OUT ¦= 0x01; // Set P1.0 LED on } #pragma vector=TIMERA0_VECTOR __interrupt void ta0_isr(void){ TA0CTL = 0; i = 0 }
Notes: 39
39

## Slide 41: Summary
ADC: analog-to-digital conversion DAC: digital-to-analog conversion
  Conversions will necessarily introduce errors. Important to understand constraints and limitations
ADC10 in MSP430
  Convert an analog signal into 10-bit digitals
  Registers associated with ADC10
Sample program of ADC10
  Single conversion
  Continuous conversion driven by Timer_A