## Slide 1: CS4101 嵌入式系統概論 Low-Power Optimization
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Materials from MSP430 Microcontroller Basics, John H. Davies, Newnes, 2008)

## Slide 2: Introduction
Why low power?
  Portable and mobile devices are getting popular, which have limited power sources, e.g., battery
  Energy conservation for our planet
  Power generates heat  low carbon
Power optimization becomes a new dimension in system design, besides performance and cost
MSP430 provides many features for low-power operations, which will be discussed next

## Slide 3: Outline
Introduction to low-power optimizations
Low-power design in MSP430

## Slide 4: Energy and Power
Energy: ability to do work
  Most important in battery-powered systems
Power: energy per unit time
  Important even in wall-plug systems---power becomes heat
Power draw increases with…
  Vcc
  Clock speed
  Temperature

## Slide 5: Efforts for Low Power
Device/transistor level
  Development of low power devices
  Reducing power supply voltage
  Reducing threshold voltage
Circuit level
  Clock gating, frequency reduction, circuit turned off
  Asynchronous circuits
System level
  Compiler optimization for energy
  OS-directed power management
Application level
Notes: 4

## Slide 6: Power Consumption: Transistor Level
Switching consumes power  dynamic power
  Switching slower, consume less power
  Smaller sizes reduce power to operate
Leakage  static power

## Slide 7: Circuit Level
Power consumption of CMOS circuits (ignoring leakage):
Delay for CMOS circuits:
Decreasing Vdd reduces P quadratically, while the runtime of program is only linearly increased
Notes: 6

## Slide 8: Circuit Level
Clock gating for synchronous sequential logic:
  Disable the clock so that flip-flops will hold their states forever and the whole circuit will not switch
   no dynamic power consumed
clock
Still need static power to hold the states

## Slide 9: System Level: Compiler
Energy-aware code scheduling
Energy-aware instruction selection
Operator strength reduction: e.g. replace * by + and <<
Standard optimizations with energy as a cost function
e.g.: register pipelining:
for (i = 1; i < 10; i++) C = 2 * a[i] + a[i-1];
R2 = a[0]; for (i = 1; i < 10; i++) { R1 = a[i]; C = 2 * R1 + R2; R2 = R1; }
Notes: 8

## Slide 10: System Level: Compiler
First-order optimization:
  high performance = low energy (some exceptions)
Optimize memory access patterns
Use registers efficiently
Identify and eliminate cache conflicts
Moderate loop unrolling eliminates some loop overhead instructions
Eliminate pipeline stalls (e.g., software pipeline)
Inlining procedures may help: reduces linkage, but may increase cache thrashing

## Slide 11: System Level: OS
Idle base
  After idle for a period, switch system to sleep mode
Power-aware memory management
  e.g. OS can determine points during execution of an application where memory banks would remain idle, so they can be transitioned to low power modes
Power-aware buffer cache
  Collect disk operations in a cache until the hard drive is running or has enough data

## Slide 12: System Level: Cooperative I/O
Time
Idle
Idle
Idle
Idle
Idle
Idle
Standby
Standby
Idle
Standby
Time
Reduces power consumption by batching requests

## Slide 13: Outline
Introduction to low-power optimizations
Low-power design in MSP430

## Slide 14: General Strategies
Put the system in low-power modes and/or use low-power modules as much as possible
How?
  Provide clocks of different frequencies  frequency scaling
  Turn off clocks when no work to do  clock gating
  Use interrupts to wake up the CPU, return to sleep when done (another reason to use interrupts)
  Switched on peripherals only when needed
  Use low-power integrated peripheral modules in place of software, e.g., move data between modules

## Slide 15: MSP430 Low-Power Modes
Mode | CPU and Clocks
Active | CPU active; all enabled clocks active
LPM0 | CPU, MCLK disabled; SMCLK, ACLK active
LPM1 | CPU, MCLK disabled; DCO disabled if not for SMCLK; ACLK active
LPM2 | CPU, MCLK, SMCLK, DCO disabled; ACLK active
LPM3 | CPU, MCLK, SMCLK, DCO disabled; ACLK active
LPM4 | CPU and all clocks disabled

## Slide 16: MSP430 Low Power Modes
Active mode:
  MSP430 starts up in this mode, which must be used when the CPU is required, i.e., to run code
  An interrupt automatically switches MSP430 to active
  Current can be reduced by running at lowest supply voltage consistent with the frequency of MCLK, e.g. VCC to 1.8V for fDCO = 1MHz
LPM0:
  CPU and MCLK are disabled
  Used when CPU is not required but some modules require a fast clock from SMCLK and DCO
Notes: Low-power mode 2 or 3 is selected if bits CPUOff and SCG1 in the status register are set. Immediately after the bits are set, CPU, MCLK, and SMCLK operations halt and all internal bus activities stop until an interrupt request or reset occurs.
Peripherals that operate with the MCLK or SMCLK signal are inactive because the clock signals are inactive. Peripherals that operate with the ACLK signal are active or inactive according with the individual control registers and the module enable bits in the SFRs. All I/O port pins and the RAM/registers are unchanged. Wake up is possible byenabled interrupts coming from active peripherals or RST/NMI.

## Slide 17: MSP430 Low Power Modes
LPM3:
  Only ACLK remains active
  Standard low-power mode when MSP430 must wake itself at regular intervals and needs a (slow) clock
  Also required if MSP430 must maintain a real-time clock
LPM4:
  CPU and all clocks are disabled
  MSP430 can be wakened only by an external signal, e.g., RST/NMI, also called RAM retention mode

## Slide 18: Power Saving in MSP430
The most important factor for reducing power consumption is using the MSP430 clock system to maximize the time in LPM3
“Instant on” clock

## Slide 19: Controlling Low Power Modes
Through four bits in status register (SR) in CPU
  SCG0 (System clock generator 0): when set, turns off DCO, if DCOCLK is not used for MCLK or SMCLK
  SCG1 (System clock generator 1): when set, turns off the SMCLK
  OSCOFF (Oscillator off): when set, turns off LFXT1 crystal oscillator, when LFXT1CLK is not use for MCLK or SMCLK
  CPUOFF (CPU off): when set, turns off the CPU
  All are clear in active mode

## Slide 20: Controlling Low Power Modes
Status bits and low-power modes

## Slide 21: Entering/Exiting Low-Power Modes
Interrupt wakes MSP430 from low-power modes:
Enter ISR:
  PC and SR are stored on the stack
  CPUOFF, SCG1, OSCOFF bits are automatically reset  entering active mode
  MCLK must be started so CPU can handle interrupt
Options for returning from ISR:
  Original SR is popped from the stack, restoring the previous operating mode
  SR bits stored on stack can be modified within ISR to return to a different mode when RETI is executed
All done in hardware

## Slide 22: Sample Code (MSP430G2xx1 _ta_01)
void main(void) { //Toggle P1.0 every 50000 cycles WDTCTL = WDTPW + WDTHOLD; // Stop WDT P1DIR ¦= 0x01; // P1.0 output TA0CCTL0 = CCIE; // CCR0 interrupt enabled TA0CCR0 = 50000; TA0CTL = TASSEL_2 + MC_2; // SMCLK, contmode _BIS_SR(LPM0_bits + GIE); // LPM0 w/ interrupt } #pragma vector=TIMERA0_VECTOR __interrupt void Timer0_A (void) { P1OUT ^= 0x01; // Toggle P1.0 TA0CCR0 += 50000; // Add Offset to CCR0 }
Use _BIC_SR_IRQ(LPM0_bits)
to exit LPM0

## Slide 23: Issues to Discuss
Which saves more energy?
  Use a higher frequency to run a program faster so as to sleep longer
  Use a lower frequency to run a program to save power, but system may be active longer