## Slide 1: CS4101 嵌入式系統概論 Real-Time Operating System
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Materials from Prof. P. Marwedel of Univ. Dortmund, Richard Barry, and
http://www.eecs.umich.edu/eecs/courses/eecs373/Lec/RTOS2.pptx)

## Slide 2: Outline
Introduction to embedded operating systems
  Comparison with desktop operating systems
  Characteristics of embedded operating systems
Introduction to real-time systems and operating systems
  Overview of real-time systems
  Characteristics of real-time operating systems (RTOS)
Introduction to FreeRTOS
  Tasks

## Slide 3: Operating Systems
The collection of software that manages a system’s hardware resources
  Often include a file system module, a GUI and other components
Often times, a “kernel” is understood to be a subset of such a collection
Characteristics
  Resource management
  Interface between application and hardware
  Library of functions for the application
Notes: Resource management - e.g. memory, processor, hard disk, cd-rom, printer
Interface between application and hardware
Creation of an operating system-API for hardware - leads to a simple handling of the hardware for the programmer (minor knowledge of hardware)
Library of functions for application
Use:
The operating system has a big influence at software reliability, productivity, maintenance and service.
Allocation of resources (cpu, memory, etc) for the application
Deletion of conflict situations

## Slide 4: Embedded Operating Systems
Fusion of the application and the OS to one unit
Characteristics:
  Resource management
    Primary internal resources
  Less overhead
  Code of the OS and the application mostly reside in ROM
Notes: Resources management
Optimising to less memory requirement
Processor
Mostly no management of the ports and periphery (limitation to operating system kernel)
Less Overhead
Run time
Memory requirement (RAM, ROM)
Interface: Relation to the outside world (input.- and output signals)
Kind of operating system:
Single-/multi-user system
Timesharing (multi-access)
Multitasking
Batch

## Slide 5: Desktop vs Embedded OS
Desktop OS: applications are compiled separately from the OS
Embedded OS: application is compiled and linked together with the embedded OS
  On system start, application usually gets executed first, and it then starts the RTOS
  Typically only part of RTOS (services, routines, or functions) needed to support the embedded application system are configured and linked in
(Dr Jimmy To, EIE, POLYU)

## Slide 6: Characteristics of Embedded OS
Embedded OS need to be configurable:
  No single OS fit all needs  install only those needed
  e.g., conditional compilation using #if and #ifdef
Device drivers often not integrated into kernel
  Embedded systems often application-specific  specific devices  move devices out of OS to tasks
Embedded OS
Standard OS
kernel

## Slide 7: Characteristics of Embedded OS
Protection is often optional
  Embedded systems are typically designed for a single purpose, untested programs rarely loaded, and thus software is considered reliable
  Privileged I/O instructions not necessary and tasks can do their own I/O, e.g., switch is address of some switch Simply use
  load register, switch instead of OS call
Real-time capability
  Many embedded systems are real-time (RT) systems and, hence, the OS used in these systems must be real-time operating systems (RTOSs)

## Slide 8: Outline
Introduction to embedded operating systems
  Comparison with desktop operating systems
  Characteristics of embedded operating systems
Introduction to real-time systems and operating systems
  Overview of real-time systems
  Characteristics of real-time operating systems (RTOS)
Introduction to FreeRTOS
  Tasks

## Slide 9: What is a Real-Time System?
Real-time systems have been defined as: "those systems in which the correctness of the system depends not only on the logical result of the computation, but also on the time at which the results are produced"
  J. Stankovic, "Misconceptions about Real-Time Computing," IEEE Computer, 21(10), October 1988.

## Slide 10: Real-Time Characteristics
Pretty much typical embedded systems
  Sensors and actuators all controlled by a processor
  The big difference is timing constraints (deadlines)
Tasks can be broken into two categories1
  Periodic Tasks: time-driven, recurring at regular intervals
    A car checking for pedestrians every 0.1 second
    An air monitoring system taking a sample every 10 seconds
  Aperiodic: event-driven
    The airbag of a car having to react to an impact
    The loss of network connectivity
  1Sporadic tasks are sometimes considered as a third category. They are tasks similar to aperiodic tasks but activated with some known bounded rate, which is characterized by a minimum interval of time between two successive activations.

## Slide 11: Soft, Firm and Hard deadlines
The instant at which a result is needed is called a deadline
If the result has utility even after the deadline has passed, the deadline is classified as soft, otherwise it is firm
If a catastrophe could result if a firm deadline is missed, the deadline is hard

## Slide 12: Scheduling algorithms
A scheduling algorithm is a scheme that selects what job to run next
  Must be able to meet deadlines in all cases
  Can be preemptive or non-preemptive
  Dynamic or static priorities
Two representative RT scheduling algorithms
  Rate monotonic (RM): static priority, simple to implement, nice properties
  Earliest deadline first (EDF): dynamic priority, harder to implement, very nice properties

## Slide 13: Rate Monotonic Scheduling
RMS [Liu and Layland, 73]: widely-used, analyzable scheduling policy
Assumptions:
  All processes run periodically on single CPU
  Zero context switch time
  No data dependencies between processes
  Process execution time is constant
  Deadline is at end of respective period
  Highest-priority ready process runs
  Tasks can be preempted

## Slide 14: Rate Monotonic Scheduling
Optimal (fixed) priority assignment:
  Shortest-period process gets highest priority, i.e., priority inversely proportional to period
  Break ties arbitrarily
No fixed-priority scheme does better
  In terms of CPU utilization while ensuring all processes meet their deadlines

## Slide 15: RMS Example
Process Execution time Period
P1 1 4
P2 2 6
P3 3 12
time
0
6
2
4
12
8
10
P1
P2
P3
P1
P1
P2
P3
P3
Preempted
Resumed
Preempted
Resumed

## Slide 16: RMS Example
Process Execution time Period
P1 2 4
P2 3 6
P3 3 12
No feasible task assignment to satisfy deadlines:
  In 12 unit intervals, execute P1 3 times, P2 2 times, P3 1 times  (6+6+3)=15 unit intervals
  Let n be # of tasks, if total utilization < n(21/n-1), tasks are schedulable (at n=∞  69.3%)
  This means that RMS algorithm will work if the total CPU utilization is less than 2/3!

## Slide 17: Earliest-Deadline-First Scheduling (EDF)
Process closest to its deadline has highest priority
  Requires recalculating processes at every time unit
  Dynamic priority assignment: priority of a task is assigned as the task arrives
  Tasks do not have to be periodic
EDF is an optimal uniprocessor scheduling algorithm
  Can use 100% of CPU
  Scheduling cost is high and ready queue can reassign priority
  May fail to meet a deadline
  Cannot guarantee who will miss deadline, but RMS can guarantee that the lowest priority task miss deadline

## Slide 18: Example of EDF Algorithm
T1: period 2; execution time 0.9
T2: period 5; execution time 2.3
10
T2
5
2
4
6
8
T1
J1.1 is 2, J2.1 is 5
Priority: T1>T2
J1.2 is 4, J2.1 is 5
Priority: T1>T2
T1 preempts T2
J1.3 is 6, J2.1 is 5
Priority: T2>T1
At time 4.1, J2.1 completes, J1.3 starts to execute

## Slide 19: Outline
Introduction to embedded operating systems
  Comparison with desktop operating systems
  Characteristics of embedded operating systems
Introduction to real-time systems and operating systems
  Overview of real-time systems
  Characteristics of real-time operating systems (RTOS)
Introduction to FreeRTOS
  Tasks

## Slide 20: Goals of an RTOS
Manage to meet RT deadlines
Also like
  Deadlines met
    Ability to specify scheduling algorithm
    Interrupts are fast
    Interrupt prioritization easy to set
  Tasks stay out of each others way
    Normally through page protection
  Device drivers already written (and tested!) for us
  Portable—runs on a huge variety of systems
  Nearly no overhead so we can use a small device!
    That is a small memory and CPU footprint

## Slide 21: Requirements for RTOS
Predictability of timing behavior of the OS
  Upper bound on execution time for all OS services
  Scheduling policy must be deterministic
  Period in which interrupts are disabled must be short (to avoid unpredictable delays in processing critical events)
OS should manage timing and scheduling
  OS has to be aware of task deadlines (unless scheduling is done off-line)
  OS should provide precise time services with high resolution
    Important if internal processing of the embedded system is linked to an absolute time in the physical environment

## Slide 22: Functionality of RTOS Kernel
Processor management
Memory management
Timer management
Task management (resume, wait, etc.)
Inter-task communication
Task synchronization
resource management

## Slide 23: Outline
Introduction to embedded operating systems
  Comparison with desktop operating systems
  Characteristics of embedded operating systems
Introduction to real-time systems and operating systems
  Overview of real-time systems
  Characteristics of real-time operating systems (RTOS)
Introduction to FreeRTOS
  Tasks

## Slide 24: Three Main Areas in FreeRTOS
Tasks
  Almost half of FreeRTOS's core code deals with tasks (in task.c and task.h)
  Creating, scheduling, and maintaining tasks
Communication
  40% of FreeRTOS's core code deals with communication (in queue.c and queue.h)
  Tasks and interrupts use queues to send data to each other and to signal the use of critical resources
Hardware interface
  Most FreeRTOS code is hardware-independent. About 6% of code to interface to hardware-dependent code
(http://www.aosabook.org/en/freertos.html)

## Slide 25: Tasks
In FreeRTOS each thread of execution is called a task
  Tasks are implemented as C functions that must return void and take a void pointer parameter:
  void ATaskFunction(void *pvParameters);
  A task is a small program that has an entry point, will normally run forever within an infinite loop, will not exit
void ATaskFunction(void *pvParameters) {
/* Each instance of task will have its own copy of variable */
int iVariableExample = 0;
/* A task is normally implemented in infinite loop */
for( ;; ) { /* task functionality */ }
/* Should the code ever break out of the above loop
then the task must be deleted. */
vTaskDelete(NULL); /* NULL: this task */
}

## Slide 26: Task Creation
xTaskCreate( pvTaskCode, pcName, usStackDepth, pvParameters, uxPriority, pxCreatedTask )
  pvTaskCode: pointer to task entry function, implemented to never return
  pcName: a descriptive name for the task to facilitate debugging
  usStackDepth: size of task stack, specified as the number of variables that the stack can hold
  pvParameters: pointer to parameters for the task
  uxPriority: priority at which the task should run
  pvCreatedTask: pass back a handle by which the created task can be referenced

## Slide 27: Example: Creating a Task
int main(void) {
xTaskCreate(vTask1, /* Pointer to func. for the task */
"Task 1", /* Text name for the task */
1000, /* Stack depth */
NULL, /* NULL task parameter */
1, /* This task will run at priority 1 */
NULL ); /* Do not use the task handle */
xTaskCreate( vTask2, "Task 2", 1000, NULL, 1, NULL );
/* Start the scheduler so the tasks start executing */
vTaskStartScheduler();
/* If all is well then main() will never reach here as
scheduler will be running the tasks. If main() reaches
here then it is likely that insufficient heap memory
available for the idle task to be created */
for( ;; );
}

## Slide 28: Example: Creating a Task
void vTask1(void *pvParameters) {
const char *pcTaskName = "Task 1 is running\r\n";
volatile unsigned long ul;
for( ;; ) {
/* Print out the name of this task. */
vPrintString(pcTaskName);
/* Delay for a period. */
for( ul = 0; ul < mainDELAY_LOOP_COUNT; ul++ ) {
}
}
}

## Slide 29: vTaskStartScheduler
Starts the RTOS scheduler
  RTOS kernel has control over which tasks are executed and when
  Create an Idle task first preventing there is no task running
  The idle task has the lowest priority
  Only return if there is insufficient RTOS heap

## Slide 30: Task States in FreeRTOS
Running:
  Task is actually executing
  Only one task can exist in the Running state at any one time
Ready:
  Task is ready to execute but a task of equal or higher priority is Running.

## Slide 31: Task States in FreeRTOS
Blocked:
  Task is waiting for some event
    Time: if a task calls vTaskDelay() it will be blocked until the delay period has expired
    Resource: tasks can also block waiting for queue and semaphore events
Suspended:
  Much like blocked, but not waiting for anything
  Tasks will only enter or exit the suspended state when explicitly commanded to do so through the vTaskSuspend() and xTaskResume() API calls respectively