## Slide 1: CS4101 Introduction to Embedded Systems Lab 12: Task Synchronization
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Introduction
In this lab , we will learn
  How to implement interrupt-driven controls in FreeRTOS using binary semaphores
  How to use Mutex to ensure exclusive accesses to system resources
  How to use counting semaphores to communicate data between tasks

## Slide 3: Binary Semaphore Example
vSemaphoreHandle binary_sem; //Global handler void one_sec_isr(void){ // an ISR xSemaphoreGiveFromISR(binary_sem, NULL); } void sem_task(void *p){ while(1) if(xSemaphoreTake(binary_sem,999999)) puts("Tick!"); } int main(void){ vSemaphoreCreateBinary(binary_sem); xTaskCreate(sem_task, (signed char*)) "t1", 2048, NULL, 1, NULL); vTaskStartScheduler(); return 0; }

## Slide 4: Mutex Example (1/3)
Two tasks attempt to gain exclusive accesses to a precious resource
xSemaphoreHandle gatekeeper = 0; //Global handler int main(void){ gatekeeper = xSemaphoreCreateMutex(); /*Create tasks with priority 1 for both users*/ xTaskCreate(user_1, (signed char*)) "t1", 1024, NULL, 1, NULL); xTaskCreate(user_2, (signed char*)) "t2", 1024, NULL, 1, NULL); vTaskStartScheduler(); return 0; }

## Slide 5: Mutex Example (2/3)
void user_1(void *p){ while(1){ if(xSemaphoreTake(gatekeeper, 1000)){ puts("User 1 got access"); access_precious_resource(); // critical section xSemaphoreGive(gatekeeper); } else{ puts("User 1 failed to get access within 1000ms"); } vTaskDelay(1000); // or do other works /*Without delay, user 1 will get key immediately after releasing the key */ } }

## Slide 6: Mutex Example (3/3)
void user_2(void *p){ while(1){ if(xSemaphoreTake(gatekeeper, 1000)){ puts("User 2 got access"); access_precious_resource(); // critical section xSemaphoreGive(gatekeeper); } else{ puts("User 2 failed to get access within 1000ms"); } vTaskDelay(1000); /*Without delay, user 2 will get key immediately after releasing the key */ } }

## Slide 7: Counting Semaphore Example (1/2)
xSemaphoreHandle count_sem; //Global Handler int main(void){ /**parameter for uxMaxCount, uxInitialCount/ count_sem = xSemaphoreCreateCounting(2, 2); /*Create tasks with priority 1 for both users*/ xTaskCreate(task1, (signed char*)) “t1", 1024, NULL, 1, NULL); xTaskCreate(task2, (signed char*)) “t2", 1024, NULL, 1, NULL); vTaskStartScheduler(); return 0; }

## Slide 8: Counting Semaphore Example (2/2)
void task1(void *p){ while(1){ if(xSemaphoreTake(count_sem, portMAX_DELAY)){ xSemaphoreGive(count_sem); } vTaskDelay(3000); } } void task2(void *p){ while(1){ if(xSemaphoreTake(count_sem), portMAX_DELAY){ xSemaphoreGive(count_sem); } vTaskDelay(3000); } }

## Slide 9: Lab: Basic 1
Modify Basic 2 of Lab 11 so that Task 3 is interrupt-driven
  Whenever light changes (from bright to dark and vice versa) on NuMaker TRIO, an interrupt is triggered
  If the light changes from bright to dark, then a FreeRTOS task will print “Dark” on the display
  If the light changes from dark to bright, then a FreeRTOS task will print “Bright” on the display
  Remember to clear the display before you print

## Slide 10: Lab: Basic 2
Extend Basic 1 to allow exclusive accesses of the tasks to the LCD display
Create a Mutex to guard the LCD so that only one task can print texts to the LCD display at any time
Note:
  Texts should be displayed at the same position of the LCD
  You may like to delay the tasks for a while after they printed to the LCD so that the race condition is obvious
  What happen if the light is blocked very swiftly? Will your program miss the light change events?

## Slide 11: Lab: Basic 3
Create 3 sender tasks, 1 receiver task and 2 buffers
  Each buffer is an array that can hold 10 characters
  Sender task 1 will fill an empty buffer with “aaaaa” and “bbbbb” alternatively; sender task 2 with texts “ccccc” and “ddddd” alternatively; and sender task 3 with “eeeee” and “fffff” alternatively
  The receiver task will read the text from the filled buffer and print it on the LCD display
Use counting semaphores to allow data communicated between sender and receiver tasks