## Slide 1: CS4101 嵌入式系統概論 Introduction to LaunchPad
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
Materials from MSP430 Microcontroller Basics, John H. Davies, Newnes, 2008

## Slide 2: Outline
MSP430 LaunchPad
MSP430 Microcontroller
  Processor
  Memory
  I/O
LaunchPad and First Program
  C
  Assembly
LaunchPad Development Environment

## Slide 3: MSP430 LaunchPad Development Kit
LaunchPad development board
Mini-USB cable, 10-pin PCB connectors
2 MSP430 MCUs: MSP430G2553, MSP430G2452
Micro Crystal 32.768kHz Oscillator
Notes: 開發板: many peripherals, pins are linked to outside for easy connections
How to read the pin id of a chip?

## Slide 4: MSP430 Microcontroller
LaunchPad development board uses microcontroller such as MSP430G2553 and MSP430G2452
Microcontroller (MCU):
  A small computer on a single IC containing a processor core, memory, programmable I/O peripherals
MSP430 microcontroller:
  Incorporates a 16-bit RISC CPU, peripherals, and a flexible clock system that are interconnected using a von-Neumann common memory address bus (MAB) and memory data bus (MDB)
Notes: 比較前一頁的開發板, 上面的電路很簡單, 幾乎沒有其他元件

## Slide 5: MSP430 Microcontroller
MSP430G2553 outside view (pin-out):
  20-pin version
  VCC , VSS : supply voltage and ground
  P1.0~P1.7, P2.0~P2.7 are for digital input and output, grouped into ports P1 and P2
  TA0CLK, TA0.0, and TA0.1 are associated with Timer0_A

## Slide 6: MSP430 Microcontroller
MSP430G2553 outside view: (cont’d)
  A0~A7 inputs to the analog-to-digital (ADC) converter
  VREF is the reference voltage for the ADC converter
  ACLK and SMCLK are outputs for the microcontroller’s clock signals
  UCA0RXD and UCA0TXD are used for the universal serial interface
  XIN and XOUT are the connections for a crystal
  RST is an active low reset signal
  NMI is the non-maskable interrupt input

## Slide 7: MSP430G2553 Inside View
X
No P3 for 20-pin devices
Memory-mapped I/O
P1REN
…
P1IN
P1OUT
MOV.W #0x40,P1OUT
LED
Notes: Go through all the components once and explain their meanings

## Slide 8: MSP430 CPU Registers
Sixteen 16-bit registers
  R0, R1, R2, and R3: program counter, status registers, stack pointer, constant generator (provides six most used immediate values and reduces code size)
  R4 to R15 are working registers for general use
Notes: Ask the meanings of the special registers

## Slide 9: Status Register: SR (R2)
  C: SR(0)
  Z: SR(1)
  N: SR(2)
  V: SR(8)
  GIE (Global interrupt enable): SR(3)
  CPUOff: SR(4)
  OSCOff: SR(5)
  SCG1, SCG0: SR(7), SR(6)
result of last arithmetic/logical operation
put MCU into one of low-power modes
Notes: Alex Milenkovich
8

## Slide 10: MSP430 Instruction Set
Instruction set architecture:
  RISC with 51 instructions, 3 formats, and 7 addressing modes
Notes: Sample some of the entries

## Slide 11: Addressing Modes
Addressing modes: the ways in which operands can be specified
Four basic modes for the source and two for the destination in instructions with two operands
The combination of the basic addressing modes and the registers gives seven modes
  All 16 registers treated on an equal basis, including special-purpose registers PC, SP, SR/CG1, and CG2
An instruction fits into a single word of 16 bits, although it may be followed by further words to provide addresses or an immediate value

## Slide 12
Notes: Alex Milenkovich
11

## Slide 13: MSP430 Memory Organization
Memory:
  Word and byte addressing and instruction formats
  16-bit memory address bus (MAB) allows direct access and branching throughout entire memory range
  16-bit memory data bus (MDB) allows direct manipulation of word-wide arguments
  Direct memory-to-memory transfers without intermediate register holding

## Slide 14: MSP430 Memory Organization
Little-endian ordering: The low-order byte is stored at the lower address and high-order byte at higher address
Aligned words:
The address of a word is the address of the byte with the lower address, which must be even
16-bit addresses, addressing to bytes

## Slide 15: MSP430G2553 Memory Map
Information memory: A 256B block of flash memory that is intended for storage of nonvolatile data, including serial numbers to identify the equipment
Flash/ROM
(16 KB)
RAM
(512 bytes)
Flash/ROM
(256 bytes)
?
Notes: 14
Refer back to page 6 to see the blocks; Ask where the peripherals go?

## Slide 16: MSP430 Input/Output
Simple digital input and output of MSP430 (GPIO) takes place through sets of pins on the package of the IC called ports
  20-pin MSP430G2553 has two ports: P1 (8 bits: P1.0~P1.7), P2 (8 bits: P2.0~P2.7)
  Typical pins can be configured for either input or output and some inputs may generate interrupts when the voltage on the pin changes
  The ports appear to the CPU as registers (memory-mapped I/O ), where each bit corresponds to a pin and a port may be associated to many registers for different purposes (next page)

## Slide 17: Registers Associated with Port 1
Reg. | Addr. | Func. | Description
P1IN | 020h | Input from port 1 | The 8 bits of data from port P1
P1OUT | 021h | Output to port 1 | Outputs 8 bits of data to port P1
P1DIR | 022h | Direction of port 1 data transfer | Bits written as 1 (0) configure corresponding pin for output (input)
P1SEL | 026h | Select function for port 1 | Bits written as 1 configure the corresponding pin for use by the specialized peripheral; 0 configure general-purpose I/O
Notes: 16

## Slide 18: Outline
MSP430 LaunchPad
MSP430 Microcontroller
  Processor
  Memory
  I/O
LaunchPad and First Program
  C
  Assembly
LaunchPad Development Environment

## Slide 19: LaunchPad Development Board
Embedded Emulation
6-pin eZ430 Connector
Part and Socket
Crystal Pads
Power Connector
Reset Button
LEDs and Jumpers
P1.0 & P1.6
P1.3 Button
Chip Pinouts
USB Emulator Connection
Notes: Purpose of emulation

## Slide 20: LaunchPad Pinouts
On-board features of LaunchPad are pinned in the following fashion:
  LED1 (red) = P1.0
  LED2 (green) = P1.6
  Switch1 = P1.3
  Switch2 = Reset
  Timer UART Transmit = P1.1
  Timer UART Receive = P1.2
In order to blink the Red and Green LEDs, we have to set Ports 1.0 and 1.6 as outputs, and toggle them

## Slide 21: Sample Code
#include <msp430.h> void main(void) { WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer P1DIR ¦= 0x41; // set P1.0 & P1.6 to outputs //(red & green LEDs) for(;;) { volatile unsigned int i; P1OUT ^= 0x41; // Toggle P1.0 & P1.6 with XOR i = 50000; // Delay do (i--); while (i != 0); } }
Notes: 20

## Slide 22: Sample Code (cont’d)
Configure the LED connected to the GPIO line
  The green and red LED are located on Port 1 Bit 0 and Bit 6  make these pins to be output  P1DIR set to 0x41 = 0100 0001
To turn on/off LED, set bit in register to 1/0
  Use XOR to toggle P1OUT
P1OUT ^= 0x41; // toggle P1.0 & 6 on/off
WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer P1DIR ¦= 0x41; // P1.0 & 6 outputs
0100 0001
Notes: 21

## Slide 23: Characteristics of Sample Code
No printf(), no GUI operations
Do not end
Do I/O mainly
  More on control of peripherals through their special registers  details of individual bits, bytes, words are important  manipulations of bits, bytes, words
Complete ownership of CPU
  Device hangs if program goes wrong
  Watchdog timer
No OS

## Slide 24: Notes of Sample Code
volatile variable:
  volatile unsigned int i;
  The variable may appear to change “spontaneously,” with no direct action by the user’s program  may be due to memory-mapped I/O devices
  Compiler must be careful in optimizing it
    Ex.: should not keep a copy of the variable in a register for efficiency; should not assume the variable remains constant when optimizing the structure of the program, e.g., rearranging loops
  The peripheral registers associated with the input ports should be declared as volatile

## Slide 25: Notes of Sample Code
Example from wikipedia:
  Optimizing compiler will think that foo is never changed and will optimize the code into
static int foo; void bar(void) { foo = 0; while (foo != 255) ; }
static int foo; void bar(void) { foo = 0; while (true) ; }
The volatile keyword in declaration of foo prevents this optimization

## Slide 26: Notes of Sample Code
Bit manipulation:
  Important instruction set architecture (ISA) feature for embedded processors
  Bit mask: set a bit P1OUT = P1OUT | BIT3 clear a bit P1OUT &= ~BIT3 toggle a bit P1OUT ˆ= BIT3
  Bit field: struct { unsigned short TAIFG:1; unsigned short TAIE:2; unsigned short TACLR:5; } TACTL_bit;
Set with TACTL_bit.TAIFG = 1

## Slide 27: Other Aspects of Embedded C
Programs for small embedded systems tend not to contain a lot of complicated manipulation of complex data objects
  Much code is usually devoted to the control of peripherals through their special registers
  Details of individual bits, bytes, words are important
Important operations
  Shifting and rotating bits
  Bit-level Boolean logic (A && B) and bitwise operator (A & B)
  Bit mask for testing and modifying individual bits

## Slide 28: Other Aspects of Embedded C
Union for manipulating individual bits or the whole byte/word as a unit
  union {
  unsigned short TACTL; // Timer_A Control
  struct {
  unsigned short TAIFG : 1; // Timer_A counter interrupt flag
  unsigned short TAIE : 1; // Timer_A counter interrupt enable
  unsigned short TACLR : 1; // Timer_A counter clear
  unsigned short : 1;
  unsigned short TAMC : 2; // Timer_A mode control
  unsigned short TAID : 2; // Timer_A clock input divider
  unsigned short TASSEL : 2; // Timer_A clock source select
  unsigned short : 6;
  } TACTL_bit;
  } TimerA;
bit 0

## Slide 29: Sample C Code: Blinking Only Red LED
#include <msp430.h> int main(void) { WDTCTL = WDTPW ¦ WDTHOLD; // Stop watchdog timer P1DIR ¦= 0x01; // Set P1.0 as output for(;;) { volatile unsigned int i; // prevent optimization P1OUT ^= 0x01; // Toggle P1.0 using XOR i = 10000; // SW Delay do i--; while(i != 0); } return 0; }

## Slide 30: Machine Code: Blinking Only Red LED
23 int main(void) { c05e: 8321 DECD.W SP WDTCTL = WDTPW ¦ WDTHOLD; c060: 40B2 5A80 0120 MOV.W #0x5a80,&Watchdog_Timer_WDTCTL P1DIR ¦= 0x01; c066: D3D2 0022 BIS.B #1,&Port_1_2_P1DIR 31 P1OUT ^= 0x01; $C$L1: c06a: E3D2 0021 XOR.B #1,&Port_1_2_P1OUT i = 10000; c06e: 40B1 2710 0000 MOV.W #0x2710,0x0000(SP) 34 do i--; $C$L2: c074: 8391 0000 DEC.W 0x0000(SP) 36 } c078: 9381 0000 TST.W 0x0000(SP) c07c: 27F6 JEQ ($C$L1) ......
Notes: BIS(.B) src,dst: Set bits in destination src .or. dst → dst

## Slide 31: Assembly for Using volatile
23 int main(void) { c05e: 8321 DECD.W SP WDTCTL = WDTPW ¦ WDTHOLD; c060: 40B2 5A80 0120 MOV.W #0x5a80,&Watchdog_Timer_WDTCTL P1DIR ¦= 0x01; c066: D3D2 0022 BIS.B #1,&Port_1_2_P1DIR 31 P1OUT ^= 0x01; $C$L1: c06a: E3D2 0021 XOR.B #1,&Port_1_2_P1OUT i = 10000; c06e: 40B1 2710 0000 MOV.W #0x2710,0x0000(SP) 34 do i--; $C$L2: c074: 8391 0000 DEC.W 0x0000(SP) 36 } c078: 9381 0000 TST.W 0x0000(SP) c07c: 27F6 JEQ ($C$L1) c07e: 3FFA JMP ($C$L2)
Notes: “i” is allocated to top of stack  DECD.W SP

## Slide 32: Assembly for Not Using volatile
WDTCTL = WDTPW ¦ WDTHOLD; main(): c078: 40B2 5A80 0120 MOV.W #0x5a80,&Watchdog_Timer_WDTCTL P1DIR ¦= 0x01; c07e: D3D2 0022 BIS.B #1,&Port_1_2_P1DIR 31 P1OUT ^= 0x01; $C$L1: c082: E3D2 0021 XOR.B #1,&Port_1_2_P1OUT 34 do i--; c086: 3FFD JMP ($C$L1) 65 func_epilog_7: POP r4 __mspabi_func_epilog(), __mspabi_func_epilog_7(): c088: 4134 POP.W R4 66 func_epilog_6: POP r5 __mspabi_func_epilog_6(): c08a: 4135 POP.W R5
Notes: “i” is removed and not allocated at all!

## Slide 33: Outline
MSP430 LaunchPad
MSP430 Microcontroller
  Processor
  Memory
  I/O
LaunchPad and First Program
  C
  Assembly
LaunchPad Development Environment

## Slide 34: Hardware Setup
MSP430G2553
Please check the version of the MSP430 microcontroller and use the right header files in your programs

## Slide 35: Code Composer Studio (CCS)
An Integrated Development Environment (IDE) based on Eclipse
Integrated “Debugger” and “Editor” – IDE
  Edit and Debug have own “perspectives” (menus, windows)
Contains all development tools: compilers, TI-RTOS kernel, and includes one target: the Simulator
Other development tools also available:
  Energia
  CCS Cloud
  (http://www.ti.com/ww/en/launchpad/software.html)

## Slide 36: Code Composer Studio (CCS)
Compiler
Asm
.c
.asm
.obj
.asm
Edit
Debug
Standard Runtime Libraries
.out
.lib
.map
User.cmd
TI-RTOS
Libraries
TI-RTOS
Config
(.cfg)
Bios.cmd
Launch Pad
EVM
Stand Alone Emulator (MSP430 FET)
Target Cfg File
.ccxml
Link

## Slide 37: CCS GUI – EDIT Perspective
Project Explorer
Project(s)
Source Files
Source EDIT’ing
Tabbed windows
Color-coded text
Outline View
Declarations and functions
Menus & Buttons
Specific actions related to EDIT’ing
Perspectives
EDIT and DEBUG

## Slide 38: CCS GUI – DEBUG Perspective
DEBUG Windows
Watch variables
Memory browser
PC execution point
Console window
Menus & Buttons
Related to DEBUG’ing
Play, pause, terminate
Connection Type
Specified in Target Cfg file
What options do users have when connecting to a target?
This window also provides a “call” stack

## Slide 39: Create a New CCS Project
1

## Slide 40: Create a New CCS Project
Type 2553 to find MSP430G2553
Type the project name
2
3
4
5

## Slide 41: Build and Load the Project
Three buttons on the horizontal toolbar control code generation. You can move your mouse over each button to read their descriptions.
Click the “Build” button and watch the tools run in the Console window. Check for any errors in the Problems window.

## Slide 42: Build and Load the Project
CCS can automatically save modified source files, build the program, open the debug perspective view for debugging, download the program to the target, and run the program at the beginning of the main() function
  Click on the “Debug” button (green bug) or
  Click Target → Debug Active Project

## Slide 43: Debug Environment
The basic buttons that control the debug environment are located in the top of CCS:
At this point you should still be at the beginning of main(). Click the Run button to run the code.
  Notice that the LEDs are toggling, as expected.
RUN

## Slide 44: End Debug Session and Close Project
The Terminate All button will terminate the active debug session, close the debugger and return CCS to the “C/C++ Perspective” view
  Click Target → Terminate All or use the Terminate All button
Next, close the project by right-clicking on project-name in the C/C++ Projects window and select Close Project.

## Slide 45: Use Disassembly Window in Debug Mode

## Slide 46: Summary
Basic structure of MSP430 LaunchPad:
  MSP430 CPU and memory
  MSP430 I/O ports and LaunchPad I/O connections
First MSP430 program
  C and assembly
  Importance of bit/byte manipulation
  Management and allocation of memory
Development environment