## Slide 1: CS4101 嵌入式系統概論 Tasks and Scheduling
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Materials From Using the FreeRTOS Real Time Kernel, Richard Barry, Study of an operating system: FreeRTOS, Nicolas Melot, and
http://www.eecs.umich.edu/eecs/courses/eecs373/Lec/RTOS2.pptx)

## Slide 2: Outline
Tasks in FreeRTOS
  Task states
  Task creation and deletion
Task scheduler of FreeRTOS
  Priority and ticks
  Delaying a task
  Suspending and resuming a task
  Idle task hook
  Changing priority

## Slide 3: Tasks in FreeRTOS
In FreeRTOS, computations are organized around tasks, which are the most basic unit of scheduling
  A task is a thread
A task is a function that must return void and take a void pointer parameter:
  void ATaskFunction(void *pvParameters);
  A task normally runs in an infinite loop and must not return
You inform the scheduler of
  The task’s resource needs (stack space, priority)
  Any arguments the task needs

## Slide 4: Task States in FreeRTOS
Running:
  Task is actually executing
  Only one task can exist in Running state at any one time (assuming 1-core system)
Ready:
  Task is ready to execute but a task of equal or higher priority is Running

## Slide 5: Task States in FreeRTOS
Blocked:
  Task is waiting for some event
    Time: if a task calls vTaskDelay() it will be blocked until the delay period has expired
    Resource: tasks can also block waiting for queue and semaphore events
Suspended:
  Much like blocked, but not waiting for anything
  Tasks will only enter or exit the suspended state when explicitly commanded to do so through the vTaskSuspend() and vTaskResume() API calls respectively

## Slide 6: Task Creation
xTaskCreate(pvTaskCode, pcName, usStackDepth, pvParameters, uxPriority, pxCreatedTask)
  pvTaskCode: pointer to task entry function, implemented to never return
  pcName: a descriptive name for the task to facilitate debugging
  usStackDepth: size of task stack, specified as the number of variables that the stack can hold
  pvParameters: pointer to parameters for the task
  uxPriority: priority at which the task should run; low numeric priority values denote low priority
  pvCreatedTask: pass back a handle to reference the task

## Slide 7: Task Deletion
A created task commonly runs in an infinite loop, but it may invoke vTaskDestroy(NULL) to end
void vTaskDelete(TaskHandle_t xTask);
  xTask: handle of the task to be deleted; NULL to cause the calling task to be deleted
  Remove a task from the RTOS kernels management
void vOtherFunction(void) {
TaskHandle_t xHandle = NULL;
// Create the task, storing the handle.
xTaskCreate(vTaskCode, "NAME", STACK_SIZE, NULL,
tskIDLE_PRIORITY, &xHandle);
// Use the handle to delete the task.
if(xHandle != NULL) vTaskDelete(xHandle);
}
Notes: Memory allocated by the task code is not automatically freed, and should be freed before the task is deleted.

## Slide 8: Outline
Tasks in FreeRTOS
  Task states
  Task creation and deletion
Task scheduler of FreeRTOS
  Priority and ticks
  Delaying a task
  Suspending and resuming a task
  Idle task hook
  Changing priority

## Slide 9: Scheduler of FreeRTOS
Task scheduling: decide which task in “Ready” state has to be run at a given time
RTOS scheduler is started by calling
  void vTaskStartScheduler(void);
  RTOS kernel now has control over which tasks are executed and when (Arduino invokes it automatically)
An Idle task is automatically created by scheduler when vTaskStartScheduler() is called
  Because CPU always needs something to execute  must always be one task that can enter Running state
  The idle task has lowest priority (priority 0) to never prevent a higher priority task from running

## Slide 10: Task Priority
FreeRTOS only uses the priorities of tasks to decide which task to run next
The uxPriority parameter of xTaskCreate() assigns an initial priority to the task being created
  Can be changed using vTaskPrioritySet()
  Low numeric priority values denote low priority tasks
Scheduler always selects the highest priority task that is able to run
  When more than one task of the same priority is able to run, the scheduler uses round-robin

## Slide 11: Ticks
To select the next task to run, the scheduler has to be executed periodically
  By a periodic interrupt called the tick interrupt
FreeRTOS API calls always specify time in tick interrupts (or just ‘ticks’)
‘Tick count’ is the total number of tick interrupts that have occurred since the scheduler was started

## Slide 12: Sample Code for Task Priority
static const char *pcTextForTask1 = “T1 running\r\n”;
static const char *pcTextForTask2 = “T2 running\t\n”;
int main(void) {
/* Create the first task at priority 1. */
xTaskCreate(vTaskFunction, "Task 1", 1000,
(void*)pcTextForTask1, 1, NULL);
/* Create the second task at priority 2. */
xTaskCreate(vTaskFunction, "Task 2", 1000,
(void*)pcTextForTask2, 2, NULL);
/* Start scheduler so the tasks start executing. */
vTaskStartScheduler();
return 0;
}

## Slide 13: Running Multiple Periodic Tasks
It is inconvenient to run multiple periodic jobs using a single Arduino loop, e.g.
  Measure the light using the photoresistor at 1 Hz
  Measure the sound intensity using microphone at 2.5 Hz
  Measure the distance of an object using the ultrasonic sensor at 0.4 Hz
Even if we run each job in a FreeRTOS task, we still need a way to schedule the tasks at specified time
Use blocked state with vTaskDelay()

## Slide 14: Delaying a Task
void vTaskDelay(const TickType_t xTicksToDelay)
  Places the calling task into the Blocked state for a fixed number of tick interrupts
  While in the Blocked state, the task will not use any processing time  equivalent to timer interrupt
  Note: Frequency of the periodic task depends on the path of the code, as well as other tasks and interrupt activities
void vTaskFunction(void * pvParameters) {
const TickType_t xDelay = 500/portTICK_PERIOD_MS;
for( ;; ) {
vToggleLED();
vTaskDelay(xDelay); /* Block for 500ms. */
}
}
Notes: The constant portTICK_PERIOD_MS can be used to calculate real time from the tick rate - with the resolution of one tick period.

## Slide 15: Delaying a Task
void vTaskDelayUntil(TickType_t *pxPreviousWakeTime, const TickType_t xTimeIncrement);
  Delay a task until a specified time  to ensure a constant execution frequency
    vTaskDelay() specifies a time at which the task wishes to unblock relative to the time at which vTaskDelay() is called
    vTaskDelayUntil() specifies an absolute time to unblock the task
  pxPreviousWakeTime: the time that task last left Blocked state
    This time is used as a reference point to calculate the time at which the task should next leave the Blocked state
  xTimeIncrement: frequency of the periodic task in ‘ticks’
  vTaskDelayUntil() will return immediately without blocking if the specified wake time is already in the past

## Slide 16: Sample Code for Periodic Tasks
void vTaskFunction(void * pvParameters){
// Perform an action every 10 ticks
TickType_t xLastWakeTime;
const TickType_t xFrequency = 10;
// Initialize the xLastWakeTime variable with the current time.
xLastWakeTime = xTaskGetTickCount();
for( ;; )
{
// Wait for the next period.
vTaskDelayUntil(&xLastWakeTime, xFrequency);
// Perform action here.
}
}
Notes: volatile TickType_t xTaskGetTickCount( void );
Returns: The count of ticks since vTaskStartScheduler was called.

## Slide 17: Suspending and Resuming a Task
void vTaskSuspend(TaskHandle_t xTaskToSuspend)
  Suspend any task
  Task will never get any microcontroller processing time, no matter what its priority
  Calls to vTaskSuspend() are not accumulative, i.e. calling vTaskSuspend () twice on the same task still only requires one call to vTaskResume () to ready the suspended task
void vTaskResume(TaskHandle_t xTaskToResume)
  Resumes a suspended task
  A task that has been suspended by one or more calls to vTaskSuspend () will be made available for running again by a single call to vTaskResume ()

## Slide 18: Sample Code for Suspending a Task
void vAFunction(void) {
TaskHandle_t xHandle;
// Create a task, storing the handle. xTaskCreate(vTaskCode, "NAME", STACK_SIZE, NULL, tskIDLE_PRIORITY, &xHandle);
// ...
// Use the handle to suspend the created task vTaskSuspend(xHandle);
// ...
// Created task will not run during this period
// ...
// Resume the suspended task ourselves.
vTaskResume(xHandle);
}

## Slide 19: Idle Task Hook
Recall:
  An Idle task is created when vTaskStartScheduler() is called so that there is at least always a task to run
Can add special functionality into the idle task through an idle hook (or call-back) function
  void vApplicationIdleHook(void);
  A function that is automatically called by the idle task once per iteration of the idle task loop
Common uses for the Idle task hook include:
  Executing low priority, background or continuous task
  Measuring the amount of spare processing capacity
  Placing the processor into a low power mode
Notes: The idle task will only run when all the other tasks have no work to perform, so measuring the amount of processing time allocated to the idle task provides a clear indication of how much processing time is spare.

## Slide 20: Changing the Priority of a Task
void vTaskPrioritySet(TaskHandle_t pxTask, UBaseType_t uxNewPriority);
  Set the priority of any task
  pxTask: handle of the task whose priority is being modified (NULL for itself)
  uxNewPriority: the priority to which the task is to be set
    Capped to the maximum available priority of (configMAX_PRIORITIES – 1), where configMAX_PRIORITIES is a compile time option set in the FreeRTOSConfig.h header file
  A context switch will occur before the function returns if the priority being set is higher than the currently executing task
unsigned portBASE_TYPE uxTaskPriorityGet(xTaskHandle pxTask);

## Slide 21: Sample Code for Changing Priority
void vTask1(void *pvParameters) {
unsigned portBASE_TYPE uxPriority;
uxPriority = uxTaskPriorityGet(NULL); // my priority
for( ;; ) {
vPrintString(“Task1 raises Task2’s priority\r\n" );
vTaskPrioritySet(xTask2Handle, (uxPriority + 1));
/* For Task1 to reach this point Task2 must
set its priority back down to below Task1. */ }
}
void vTask2(void *pvParameters) {
unsigned portBASE_TYPE uxPriority;
uxPriority = uxTaskPriorityGet(NULL);
for( ;; ) {
vPrintString(“Task2 lower its priority\r\n");
vTaskPrioritySet(NULL, (uxPriority - 2)); }
}

## Slide 22: Sample Code for Changing Priority
xTaskHandle xTask2Handle;
int main(void) {
// Create Task1 at priority 2
xTaskCreate(vTask1, "Task 1", 1000, NULL, 2, NULL);
// Create Task2 at priority 1
xTaskCreate(vTask2, "Task 2", 1000, NULL, 1,
&xTask2Handle);
// Start the scheduler
vTaskStartScheduler();
/* If all is well, then main() will never reach here
as the scheduler will now be running the tasks.
If main() does reach here, then it is likely that
there was insufficient heap memory available for
the idle task to be created.*/
for( ;; );
}

## Slide 23: Summary
FreeRTOS runs Fixed Priority Preemptive Scheduling
  Each task is assigned a priority
  Each task can exist in one of several states
  Only one task can exist in Running state at any one time
  The scheduler will always select the highest priority Ready state task to enter the Running state
  Scheduling is made at each tick interrupt
Notes: ‘Fixed Priority’ because each
task is assigned a priority that is not altered by the kernel itself (only tasks can change priorities).
‘Preemptive’ because a task entering the Ready state or having its priority altered will always pre-empt
the Running state task if the Running state task has a lower priority.