## Slide 1: CS4101 嵌入式系統概論 RT Scheduling & Synchronization
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Materials from Prof. Insup Lee, Prof. Frank Drews, MQX User Guide, Using the FreeRTOS Real Time Kernel, Study of an Operating System: FreeRTOS)

## Slide 2: Outline
Real-time task scheduling
Introduction to task synchronization
Queues of FreeRTOS
Semaphores and mutexs of FreeRTOS

## Slide 3: What is a Real-Time System?
Real-time systems have been defined as: "those systems in which the correctness of the system depends not only on the logical result of the computation, but also on the time at which the results are produced"
  J. Stankovic, "Misconceptions about Real-Time Computing," IEEE Computer, 21(10), October 1988.
Performance measure
  Timeliness on timing constraints (deadlines)
Key property
  Predictability on timing constraints

## Slide 4: Real-Time Characteristics
Fundamental design issues:
  To specify the timing constraints of real-time systems
  To achieve predictability on satisfying their timing constraints with the existence of other real-time systems
Tasks can be broken into two categories1
  Periodic Tasks: time-driven, recurring at regular intervals
    A car checking for pedestrians every 0.1 second
    An air monitoring system taking a sample every 10 seconds
  Aperiodic: event-driven
    The airbag of a car having to react to an impact
    The loss of network connectivity
  1Sporadic tasks are sometimes considered as a third category. They are tasks similar to aperiodic tasks but activated with some known bounded rate, which is characterized by a minimum interval of time between two successive activations.

## Slide 5: Real-Time Tasks
Periodic task (p,e)
  It is invoked repetitively in a regular interval  sampling
  Period p = time between sampling (0 < p)
  Execution time e = maximum execution time (0 < e < p)
  Utilization U = e/p
  Deadline: the instant at which a result is needed
5
10
15
0
period
deadline

## Slide 6: Types of Deadlines
Hard deadline:
  Disastrous or very serious consequences may occur if the deadline is missed
  Validation is essential: can all the deadlines be met, even under worst-case scenario?
  Deterministic guarantees
Soft deadline
  Ideally, deadline should be met for the result to be useful (e.g. good performance), but, even if the deadline is missed, the result still has some uses (degraded perf.)
  Best effort approaches

## Slide 7: Schedulability
A property indicating whether a set of real-time tasks (a real-time system) can meet their deadlines
(4,1)
(5,2)
(7,2)

## Slide 8: Real-Time Scheduling
Determines the order of real-time task executions
  Must meet deadlines in all cases
Variations:
  Preemptive or non-preemptive
  Dynamic priority or static priority
Two representative RT scheduling algorithms
  Rate monotonic (RM): static priority, simple to implement, nice properties
  Earliest deadline first (EDF): dynamic priority, harder to implement, very nice properties

## Slide 9: Rate Monotonic Scheduling
RMS [Liu and Layland, 73]: widely-used, analyzable scheduling policy
Assumptions:
  All processes run periodically on single CPU
  Zero context switch time
  No data dependencies between processes
  Process execution time is constant
  Deadline is at end of respective period
  Highest-priority ready process runs
  Tasks can be preempted
Liu & Layland, “Scheduling algorithms for multi-programming in a hard-real-time environment”, Journal of ACM, 1973.

## Slide 10: Rate Monotonic Scheduling
Optimal static priority assignment:
  Shortest-period task gets highest priority
  Break ties arbitrarily
No static-priority scheme does better
  In terms of CPU utilization
0
5
10
15
Deadline missed!
response time of T3

## Slide 11: Rate Monotonic Scheduling
Let n be # of tasks, if total utilization < n(21/n-1), tasks are schedulable (at n=∞  69.3%)
This means that RMS algorithm will work if the total CPU utilization is less than 2/3!
0
5
10
15

## Slide 12: Another RMS Example
Process Execution time Period
P1 1 4
P2 2 6
P3 3 12
time
0
6
2
4
12
8
10
P1
P2
P3
P1
P1
P2
P3
P3
Preempted
Resumed
Preempted
Resumed
Utilization = 0.5

## Slide 13: Earliest-Deadline-First Scheduling (EDF)
Task closest to its deadline has highest priority
  Requires recalculating priority of tasks at every time unit
  Dynamic priority assignment: priority of a task is assigned as the task arrives
  Tasks do not have to be periodic
EDF is an optimal uniprocessor scheduling algorithm
  Can use 100% of CPU
  Scheduling cost is high and ready queue can reassign priority
  May fail to meet a deadline
  Cannot guarantee who will miss deadline, but RMS can guarantee that the lowest priority task misses deadline

## Slide 14: Earliest-Deadline-First Scheduling (EDF)
Executes the task with the earliest deadline
Optimal scheduling algorithm
  if there is a schedule for a set of real-time tasks, EDF can schedule it
0
5
10
15

## Slide 15: Outline
Real-time task scheduling
Introduction to task synchronization
Queues of FreeRTOS
Semaphores and mutexs of FreeRTOS

## Slide 16: Why Synchronization?
Synchronization may be used to solve:
  Mutual exclusion
  Control flow
  Data flow
Synchronization mechanisms include:
  Message queues
  Semaphores
  Mutexs
  Events
Correct synchronization mechanism depends on the synchronization issue being addressed
EF
M

## Slide 17: Mutual Exclusion
Problem: multiple tasks may “simultaneously” need to access the same resource
  Resource may be code, data, peripheral, etc.
  Need to allow the shared resource exclusively accessible to only one task at a time
How to do?
  Allowing only one task to lock the resource and the rest have to wait for the resource to be unlocked
  Common mechanisms: lock/unlock, mutex, semaphore

## Slide 18: Control Flow Synchronization
Problem: a task or ISR may need to resume the execution of one or more other tasks, so that tasks execute in an application-controlled order
  Mutual exclusion is used to prevent another task from running, while control flow is used to allow another task to run, often specific tasks
How to do?
  Common mechanisms: post/wait, signal, event

## Slide 19: Data Flow Synchronization
Problem: a task or ISR may need to pass some data to one or more other specific tasks, so that data may be processed in an application-specified order
How to do?
  May be accomplished indirectly through control flow synchronization
  Common mechanisms: queues, signal, post/wait

## Slide 20: Outline
Real-time task scheduling
Introduction to task synchronization
Queues of FreeRTOS
Semaphores and mutexs of FreeRTOS

## Slide 21: FreeRTOS Queues
Queues are the primary form of inter-task communications in FreeRTOS
  A queue can hold a finite number of fixed size data items.
  In most cases, used as thread safe FIFO (First In First Out) buffers with new data being sent to the back of the queue, and removed from the front
  Can be used to send messages between tasks, and between interrupts and tasks

## Slide 22: FreeRTOS Queues
Queues store a finite number of fixed-size data
  May be read and written by different tasks, but do not belong to any task
  # of items and item size determined at queue create time
  Sending/receiving items are by copy not reference
Queue functions
  Create queues: xQueueCreate(), vQueueDelete()
  Send/receive data to/from queues: xQueueSend(), xQueueSendToBack(), xQueueReceive(), xQueueReceiveFromISR()
  Queue management/number of items in a queue
  Blocking on a queue/effect of priority

## Slide 23: Blocking on Queues
Queue APIs permit a block time to be specified
When read from an empty queue,
  Task will be placed into the Blocked state
  Until data is available on the queue or block time expires
When write to a full queue,
  Task will be placed into the Blocked state
  Until space is available in the queue, or block time expires
If more than one task block on the same queue, then the task with the highest priority will be the task that is unblocked first
  If the blocked tasks have equal priority, the task that has been waiting for data the longest will be unblocked

## Slide 24: Queue Creation
QueueHandle_t xQueueCreate(
UBaseType_t uxQueueLength,
UBaseType_t uxItemSize);
Creates a new queue instance
  Allocates queue storage and returns a handle
  uxQueueLength: maximum number of items that the queue can contain
  uxItemSize: number of bytes that each item in the queue will require
    Items are queued by copy, not by reference, so this is the number of bytes that will be copied for each posted item
  Each item on the queue must be the same size

## Slide 25: Send Data through Queues
BaseType_t xQueueSend(QueueHandle_t xQueue,
const void * pvItemToQueue,
TickType_t xTicksToWait);
Post an item on a queue
  The item is queued by copy, not by reference
  Must not be called from an interrupt service routine
  xQueue: queue handle to which the item is to be posted
  pvItemToQueue: pointer to item to be placed on queue
  xTicksToWait: max. time (in ticks) that task should block waiting for space to become available, should it is full
  If INCLUDE_vTaskSuspend is set to '1‘, then specifying the block time as portMAX_DELAY will block task indefinitely

## Slide 26: Receive Data through Queues
BaseType_t xQueueReceive(
QueueHandle_t xQueue, void *pvBuffer,
TickType_t xTicksToWait);
Receive an item from a queue
  The item is received by copy so a buffer of adequate size must be provided
  Must not be used in an interrupt service routine
  xQueue: queue handle from which to receive item
  pvBuffer: pointer to the buffer into which the received item will be copied.
  xTicksToWait: max. amount of time the task should block waiting for an item should the queue be empty

## Slide 27: Other Functions for Queues
portBASE_TYPE xQueuePeek(
xQueueHandle xQueue,
const void * pvBuffer,
portTickType xTicksToWait);
Receive an item from the head of the queue without the item being removed from the queue
unsigned portBASE_TYPE uxQueueMEssagesWaiting(
xQueueHandle xQueue);
Query the number of items currently in a queue

## Slide 28: Example of Queues (1/3): sender_task
QueueHandle_t Global_Queue_Handle = 0; //Global Handler void sender_task(void *p){ int i=0; while(1){ Serial.println("sent a value:"); Serial.println(i); if(!xQueueSend(Global_Queue_Handle, &i, 1000)) Serial.println("Failed to send to queue"); i++; vTaskDelay(3000/portTICK_PERIOD_MS); //delay 3 sec } }
Notes: 27
27

## Slide 29: Example of Queues (2/3): receiver_task
void receiver_task(void *p){ int rx_int = 0; while(1){ if(xQueueReceive(Global_Queue_Handle,&rx_int,1000)) { Serial.println("receive a value:"); Serial.println(rx_int); } else Serial.println("Failed to receive from queue"); } }
Notes: 28
28

## Slide 30: Example of Queues (3/3): setup
void setup() { Serial.begin(9600); Global_Queue_Handle = xQueueCreate(3, sizeof(int)); // create a queue of 3 int // Create tasks with priority 1 // xTaskCreate(sender_task,(const portCHAR *)"sx", 128, NULL, 1, NULL); xTaskCreate(receiver_task,(const portCHAR *)"rx", 128, NULL, 1, NULL); vTaskStartScheduler(); }
Notes: 29
29

## Slide 31: Outline
Real-time task scheduling
Introduction to task synchronization
Queues of FreeRTOS
Semaphores and mutexs of FreeRTOS
  Binary semaphores
  Counting semaphores
  Mutex

## Slide 32: Semaphores
Semaphores are used to:
  Control access to a shared resource (mutual exclusion)
  Signal the occurrence of an event
  Allow two tasks to synchronize their activities
Basic idea
  A semaphore contains a number of tokens. The code needs to acquire one in order to continue execution
  If all the tokens of the semaphore are used, the requesting task is suspended until some tokens are released by their current owners

## Slide 33: How Semaphores Work?
A semaphore has:
  Counter: maximum number of concurrent accesses
  Queue: for tasks that wait for access
If a task requests (waits for) a semaphore
  if counter > 0, then (1) the counter is decremented by 1, and (2) task gets the semaphore and proceed to do work
  Else task is blocked and put in the queue
If a task releases (posts) a semaphore
  if there are tasks in the semaphore queue, then appropriate task is readied, according to queuing policy
  Else counter is incremented by 1
Notes: 32
This should be a quick review from the basic RTOS section earlier
Mutex is special case where the count =1 so only one task can hold it at a time

## Slide 34: Binary Semaphores
Semaphores with counter = 1, used for mutual exclusion and synchronization
For synchronization purpose, a binary semaphore can be think of as a queue that only holds one item
  The queue can only be empty or full (hence binary)
  Tasks using the queue don't care what the queue holds, only want to know if the queue is empty or full
  If more than one task blocks on the same semaphore, then the task with the highest priority will be the task that is unblocked the next time the semaphore becomes available

## Slide 35: Binary Semaphores and Interrupts
The best way to handle complex events triggered by interrupts is to not do the code in the ISR
  Create a task that is blocking on a binary semaphore
  When the interrupt happens, the ISR just sets (gives) the semaphore and exits
  Task can now be scheduled like any other
    No need to worry about nesting interrupts and interrupt priority
This is called Deferred Interrupt Processing

## Slide 36: Binary Semaphores and Interrupts
Figure from Using the FreeRTOS Real Time Kernel (a pdf book), fair use claimed.

## Slide 37: Create a Binary Semaphore
SemaphoreHandle_t xSemaphoreCreateBinary(void);
Function to create a binary semaphore
  The semaphore is created in the 'empty' state
  A binary semaphore need not be given back once obtained, so task synchronization can be implemented by one task/interrupt continuously 'giving' the semaphore while another continuously 'takes' the semaphore
  Binary semaphores are assigned to variables of type SemaphoreHandle_t and can be used in any API function that takes a parameter of this type

## Slide 38: Set a Binary Semaphore
xSemaphoreGiveFromISR(
SemaphoreHandle_t xSemaphore,
signed BaseType_t *pxHigherPriorityTaskWoken)
Set (give) a semaphore
  Can be used from an ISR
  xSemaphore: handle to the semaphore being released
  pxHigherPriorityTaskWoken: set to pdTRUE if giving the semaphore caused a task of a higher priority to unblock, causing a context switch

## Slide 39: Reset a Binary Semaphore
xSemaphoreTake( xSemaphoreHandle xSemaphore,
portTickType xBlockTime)
Reset (take) a semaphore
  xSemaphore: handle to the semaphore being taken
  xBlockTime: time in ticks to wait for the semaphore to become available
    A block time of zero can be used to poll the semaphore

## Slide 40: Example of Binary Semaphores
vSemaphoreHandle binary_sem; //Global handler void one_sec_isr(void){ // an ISR xSemaphoreGiveFromISR(binary_sem, NULL); } void sem_task(void *p){ while(1) if(xSemaphoreTake(binary_sem,999999)) puts("Tick!"); } int main(void){ vSemaphoreCreateBinary(binary_sem); xTaskCreate(sem_task, (signed char*)) "t1", 2048, NULL, 1, NULL); vTaskStartScheduler(); return 0; }
Notes: 39
39

## Slide 41: Counting Semaphores
Typically used for two things:
Counting events:
  An event handler will 'give' a semaphore each time an event occurs, and a handler task will 'take' a semaphore each time it processes an event
Resource management:
  The count value indicates number of available resources
  To get a resource, a task must obtain (take) a semaphore
  When a task finishes with the resource, it 'gives' the semaphore back
SemaphoreHandle_t xSemaphoreCreateCounting( UBaseType_t uxMaxCount, UBaseType_t uxInitialCount)

## Slide 42: Example of Counting Semaphore (1/2)
xSemaphoreHandle count_sem; //Global Handler int main(void){ /**parameter for uxMaxCount, uxInitialCount/ count_sem = xSemaphoreCreateCounting(2, 2); /*Create tasks with priority 1 for both users*/ xTaskCreate(task1, (signed char*)) “t1", 1024, NULL, 1, NULL); xTaskCreate(task2, (signed char*)) “t2", 1024, NULL, 1, NULL); vTaskStartScheduler(); return 0; }

## Slide 43: Example of Counting Semaphore (2/2)
void task1(void *p){ while(1){ if(xSemaphoreTake(count_sem, portMAX_DELAY)){ xSemaphoreGive(count_sem); } vTaskDelay(3000); } } void task2(void *p){ while(1){ if(xSemaphoreTake(count_sem), portMAX_DELAY){ xSemaphoreGive(count_sem); } vTaskDelay(3000); } }

## Slide 44: Mutex
Mutexes are used for mutual exclusion, so that only one task at a time uses a shared resource, e.g., file, data, device, ...
  To access the shared resource, a task locks the mutex associated with the resource
  The task owns the mutex, until it unlocks the utex

## Slide 45: Mutex
Mutex acts like a token used to guard a resource
  When a task wishes to access the resource, it must first obtain ('take') the token
  When the task has finished with the resource it must 'give' the token back - allowing other tasks the opportunity to access the same resource
Mutex may cause a high priority task to be waiting on a lower priority one
  Even worse, a medium priority task might be running and cause the high priority task to not meet its deadline!
  Priority inversion problem

## Slide 46: Priority Inversion: Case 1
Assume priority of T1 > priority of T9
  If T9 has exclusive access, T1 has to wait until T9 releases resource  inverting priority  can raise priority of T9
T1 has higher priority and preempts T9
Critical section
(critical section)

## Slide 47: Priority Inversion: Case 2
A medium-priority task preempts a lower-priority task which is using a shared resource on which a higher priority task is blocked
  If the higher-priority task would be otherwise ready to run, but a medium-priority task is currently running instead, a priority inversion is occurred

## Slide 48: Solving Priority Inversion
Priority inheritance
  If a high priority task blocks while attempting to obtain a mutex (token) that is currently held by a lower priority task, then the priority of the task holding the token is temporarily raised to that of the blocking task

## Slide 49: Example of Mutex (1/3)
include <semphr.h> SemaphoreHandle_t gatekeeper = 0; //Global handler void user_1(void *p){ while(1){ if(xSemaphoreTake(gatekeeper, 100)){ Serial.println("User 1 got access"); // enter critical section vTaskDelay(200); //stay in C.S. for 200 ticks xSemaphoreGive(gatekeeper); // release semaphore, exit critical section } else{ Serial.println(“User 1 cannot access in 1000 ms"); } vTaskDelay(100); // or do other works // Without delay, user 1 will get key immediately// } }
Notes: 48
48

## Slide 50: Example of Mutex (2/3)
void user_2(void *p){ while(1){ if(xSemaphoreTake(gatekeeper, 100)){ Serial.println("User 2 got access"); //critical section xSemaphoreGive(gatekeeper); //release semaphore, exit critical section } else{//fail to get the semaphore Serial.println("User 2 cannot access in 1000 ms"); } vTaskDelay(100); // or do other works // Without delay, user 2 will get key immediately after releasing the key // } }
Notes: 49
49

## Slide 51: Example of Mutex (3/3)
void setup(){ Serial.begin(9600); gatekeeper = xSemaphoreCreateMutex(); // Create tasks with priority 1 for both users // xTaskCreate(user_1, (const portCHAR*)"t1", 128, NULL, 1, NULL); xTaskCreate(user_2, (const portCHAR*)"t2", 128, NULL, 2, NULL); Serial.println("test"); vTaskStartScheduler(); } void loop() { ... }
Notes: 50
50