## Slide 1: CS4101 Introduction to Embedded Systems Lab 1: General Purpose IO
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Introduction
In this lab, we will learn the basic GPIO of MSP430 LaunchPad
  Configure the I/O port of LaunchPad for input and output
  Run the debugger for basic debugging

## Slide 3: Sample Code 1 for Input
#include <msp430.h> #define LED1 BIT0 //P1.0 to red LED #define B1 BIT3 //P1.3 to button void main(void){ WDTCTL = WDTPW + WDTHOLD; //Stop watchdog timer P1OUT ¦= LED1 + B1; P1DIR = LED1; //Set pin with LED1 to output P1REN = B1; //Set pin to use pull-up resistor for(;;){ //Loop forever if((P1IN & B1) ==0){ //Is button down? P1OUT &= ~LED1; // Yes, turn LED1 off } else{ P1OUT ¦= LED1; // No, turn LED1 on } } }
Notes: Whenever button is down, turn LED off. Whenever button is up, turn LED on.
P1OUT is not initialized and must be written before configuring the pin for output.
Assume button is active low (0  pressed; 1  depressed)

## Slide 4: Sample Code 2 for Debugger
#include <msp430.h> #define LED1 BIT6 // P1.0 to green LED #define B1 BIT3 // P1.3 to button volatile unsigned int i, j; void main(void){ WDTCTL = WDTPW + WDTHOLD; // Stop watchdog timer P1OUT ¦= LED1 + B1; P1DIR = LED1; // Set pin with LED1 to output P1REN = B1; // Set pin to use pull-up resistor for(;;){ while((P1IN & B1) != 0){ // Loop on button up i = P1IN; j = P1OUT; } P1OUT &= ~LED1; // Turn LED1 off while((P1IN & B1) == 0){ // Loop on button down i = P1IN; j = P1OUT; } P1OUT ¦= LED1; // Turn LED1 on } }
Notes: On button down, turn LED off. On button up, turn LED on.

## Slide 5: How to Debug?
In the code line containing:
  i = P1IN;
  j = P1OUT;
Add new expression from Expressions window
  Right-click on the appropriate line of code and set the Breakpoint
  When the code runs, it will hit the breakpoint and stop
  You can now observe the value

## Slide 6: Debugger Output
1111 1110
01001000
00000110
00001000
No need to care about other bits!

## Slide 7: Lab 1
Basic 1:
  Flash the red and green LED alternatively whenever the button is pressed and released once. The LEDs change right after the button is released.
  Run the debugger to show the content of P1IN whenever the LEDs change.
Basic 2:
  When the button is down, only flash the green LED. But if the button is pressed “long” enough, flash only the red LED instead.
  When the button is released, neither of the LEDs is on.