## Slide 1: CS4101 Introduction to Embedded Systems Lab 3: Interrupt
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Lab 3
Basic 1:
  Flash the red and green LED alternatively on interrupt from the button, whenever the button is pressed and released once. The LEDs change right after the button is released. The LEDs flash at 1 Hz (0.3 sec on and 0.7 sec off) by interrupt from Timer0_A3, which is driven by ACLK sourced from VLO (running at 12 KHz).
  Note: There are two interrupts to handle: timer up and button down and up.
  Note: Since TAR register is 16-bit (0~65535) long, you should be careful of its overflow.

## Slide 3: Lab 3
Basic 2:
  When the button is up, neither of the LEDs is on.
  When the button is down, only flash the green LED according to the settings in Basic 1. The event, “button down”, must be detected by interrupts.
  Furthermore, if the button is pressed for more than 3 seconds, flash only the red LED instead (on for 0.2 sec and off for 0.8 sec), which is controlled by interrupts from Timer1_A3 driven by SMCLK sourced by DCO. The event, “more than 3 seconds”, should be implemented by interrupts.