## Slide 1: CS4101 Introduction to Embedded Systems Lab 4: Analog-to-Digital Converter
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Sample Code 1 for ADC10
Repetitive single conversion:
  Repetitively perform single samples on A1 (pin P1.1) with reference to Vcc
  If A1 > 0.5*Vcc, P1.0 set, else reset.
  Set ADC10SC to start sample and conversion
    But ADC10SC automatically cleared at end of conversion.
  Enable the next conversion in ISR of ADC10 and iterate
  Use ADC10 internal oscillator to time the sample and conversion

## Slide 3: Sample Code 1 for ADC10
void main(void) { WDTCTL = WDTPW + WDTHOLD; // Stop WDT // H&S time 16x, interrupt enabled ADC10CTL0 = ADC10SHT_2 + ADC10ON + ADC10IE; ADC10CTL1 = INCH_1; // Input from A1 ADC10AE0 ¦= 0x02; // Enable pin A1 for analog in P1DIR ¦= 0x01; // Set P1.0 to output ADC10CTL0 ¦= ENC + ADC10SC; // Start sampling for (;;) { } } #pragma vector=ADC10_VECTOR __interrupt void ADC10_ISR(void) { if (ADC10MEM < 0x1FF) P1OUT &= ~0x01; else P1OUT ¦= 0x01; ADC10CTL0 ¦= ENC + ADC10SC; // enable sampling }
Notes: 2
Why not read ADC10MEM right after setting ADC10CTL0? While wait for interrupt? What is the time to go through one iteration?
Any one of the pins of Port 1 can be set to be an analog input. Thus up to 8 channels are available for separate ADC inputs.
Analog Enable control register ADC10AE0 will be use for enabling the corresponding input channels.
2

## Slide 4: Sample Code 2 for ADC10
Continuous sampling driven by Timer0_A3
  A1 is sampled 16/second with reference to 1.5V, where ACLK runs at 32 KHz driven by an external crystal (2048 ACLK cycles give 1/16 second (ACLK/2048))
  If A1 > 0.5V, P1.0 is set, else reset.
  Timer0_A3 is run in up mode with CCR0 defining the sampling period (2048 cycles)
  Use CCR1 to automatically trigger ADC10 conversion

## Slide 5: Sample Code 2 for ADC10
#include “msp430.h” int i=1; void main(void) { WDTCTL = WDTPW + WDTHOLD; // Stop WDT // TA1 trigger sample start ADC10CTL1 = SHS_1 + CONSEQ_2 + INCH_1; ADC10CTL0 = SREF_1 + ADC10SHT_2 + REFON + ADC10ON + ADC10IE; __enable_interrupt(); // Enable interrupts TA0CCR0 = 30; // Delay for Volt Ref to settle TA0CCTL0 ¦= CCIE; // Compare-mode interrupt TA0CTL = TASSEL_2 + MC_1; // SMCLK, Up mode while(i); // Wait for settle TA0CCTL0 &= ~CCIE; // Disable timer Interrupt __disable_interrupt();
How to break?
Notes: 4
SHS_1: S&H triggering source  OUT1
CONSEQ_2: Conversion sequence mode select (Repeat-single-channel)
SREF_1: Select reference (VR+ = VREF+ and VR- = VSS)
ADC10SHT_2: Sample-and-hold time (6 × ADC10CLKs)
REFON: internal reference generator on
The settling time for the internal reference is < 30µs. If DCOCLK is 1 MHz, then 1 cycle takes 6µs and 30 cycles gives long enough delay for the internal reference voltage to settle down.
4

## Slide 6: Sample Code 2 for ADC10
ADC10CTL0 ¦= ENC; // ADC10 Enable ADC10AE0 ¦= 0x02; // P1.1 ADC10 option select P1DIR ¦= 0x01; // Set P1.0 output TA0CCR0 = 2048-1; // Sampling period TA0CCTL1 = OUTMOD_3; // TACCR1 set/reset TA0CCR1 = 2046; // TACCR1 OUT1 on time TA0CTL = TASSEL_1 + MC_1; // ACLK, up mode while(1); }
Timer0_A CCR1 out mode 3: The output (OUT1) is set when the timer counts to the TA0CCR1 value and is reset when the timer counts to the TA0CCR0 value.
Notes: 5
5

## Slide 7: Sample Code 2 for ADC10
// ADC10 interrupt service routine #pragma vector=ADC10_VECTOR __interrupt void ADC10_ISR(void){ if (ADC10MEM < 0x155) // ADC10MEM = A1 > 0.5V? P1OUT &= ~0x01; // Clear P1.0 LED off else P1OUT ¦= 0x01; // Set P1.0 LED on } #pragma vector=TIMERA0_VECTOR __interrupt void ta0_isr(void){ TA0CTL = 0; i = 0; }
Break the while loop in main() that waits for the internal voltage reference to settle
Notes: 6
Where do these two ISRs return to?
6

## Slide 8: Lab 4
Basic 1:
  Flash the red and green LED alternatively on interrupts from button releases. The LEDs flash at 1 Hz (0.3 sec on and 0.7 sec off) by interrupts (ACLK sourced from VLO).
  Every time the button is pushed, measure the temperature once, convert it to Celsius and store in a variable. Show the value of the variable in the debug mode of CCS.
    Use 1.5V voltage reference, the single-channel-single-conversion mode, and the triggering source of ADC10SC.
    Hint: V = 0.00355 * C + 0.986, where V is Voltage and C is Celsius
  If voltage >= 1.125V, change LED flash frequency to 2 Hz (0.3 sec on and 0.2 sec off); otherwise, back to 1 Hz.

## Slide 9: Lab 4
Basic 2:
  When the button is up, neither of the LEDs is on.
  When the button is down, only flash the green LED at 1 Hz (0.3 sec on and 0.7 sec off) with ACLK sourced from VLO.
  While the button is pressed, measure the temperature every 0.5 sec, using repeat-single-conversion mode triggered continuously by Timer0_A3.
  If the average temperature of the last second rises, then flash the red LED instead (on for 0.2 sec and off for 0.8 sec), which is controlled by Timer1_A3 driven by SMCLK sourced by DCO. Otherwise, flash the green LED as specified above.
  All events must be detected and handled by interrupts.