## Slide 1: CS4101 Introduction to Embedded Systems Lab 6: Serial Communication
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan

## Slide 2: Lab 6
Write a function flash(char id, int on, int off) to flash the LEDs by interrupts using Timer1_A3 driven by ACLK sourced from VLO, where
  id = 0 for red LED; 1 for green LED
  on/off = time (in ms) for the LED to be on/off
  CPU enters LPM3 between interrupts
Write a function temp(int interval, int times) to measure the temperature using repeat-single-conversion mode triggered by Timer0_A3
  interval: the interval (in ms) between measurements
  times: the number of times to measure
  Results are stored in a global integer array Temp[64]

## Slide 3: Lab 6
Normal:
  Use flash() to flash the green LED at 0.5 Hz (0.5 sec on and 1.5 sec off) by interrupts (ACLK sourced from VLO
  Use temp() to measure the temperature at 1 Hz continuously (Hint: must reuse Temp[])
Special:
  If the average temperature of the last 2 seconds is higher than 737 (voltage), then flash the red LED at 2 Hz (0.2 sec on and 0.3 sec off) and send a string “Hot!” to PC every second using 7-E-1 (7-bit data, even parity, 1 stop bit). You must use 7-E-1 to get the full credit!

## Slide 4: Lab 6
Special: (cont.)
  Whenever PC receives the string “Hot!”, it displays the string and waits for user’s input.
  When user enters a string, PC transmits the string to the LaunchPad using 7-E-1
  If the string is “Ack!”, then the LaunchPad goes back to the normal state (i.e. flash the green LED at 0.5 Hz with 0.5 sec on and 1.5 sec off). Otherwise, the LaunchPad ignores the string and keeps flashing the red LED at 2 Hz.