## Slide 1: CS5100 Advanced Computer Architecture Advanced Branch Prediction
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. Hsien-Hsin Lee, Prof. Yasun Hsu, Prof. Onur Mutlu)

## Slide 2: About This Lecture
1
Goal:
  To understand the techniques for reducing the cost of branches
Outline:
  Reducing branch cost with advanced branch prediction (Sec. 3.3)
    Prediction of branch direction: static, dynamic, branch correlation
    Prediction of branch target

## Slide 3: Control Speculation with Branch Prediction
Modern processors have deep pipelines
  Branch penalty limits performance of deep pipelines
Want to execute instructions beyond a branch even before that branch is resolved  use speculative execution
  Branch prediction: dynamic vs. static
What to predict?

## Slide 4: What to Predict?
Direction (1-bit)
  Single direction for unconditional jumps and calls/returns
  Binary for conditional branches
Target (32-bit or 64-bit addresses)
  Some are easy
    One address: uni-directional jumps
    Two: addresses: fall through (not taken) vs. taken
  Many: function pointer or indirect jump (e.g. jr r31)
Ideally, one predictor for direction and one predictor for target for each branch in the code

## Slide 5: Static Branch Prediction for Direction
Uni-directional: always predict taken (or not taken)
  Always-not-taken: easy (does not need branch target address), not effective for loops
  Always-taken: branch target address needs to be computed before the instruction flow can continue (may take extra cycles)
Backward taken, forward not taken
  Check sign of branch displacement: taken if negative, not-taken if positive  no extra hardware needed
  Good for, e.g., loops
  Do not require HW support since the sign of target displacement is already encoded in the branch instruction

## Slide 6: Static Branch Prediction for Direction
Compiler hints with branch annotation
  Run instrumented program with sample input data
  Collect info on branch direction (profiling)
  Use this profile info for prediction
  Use a bit in branch instruction
    Set to 1 if taken
    Set to 0 if un-taken
  Bits set by compiler or user
  Once set, same behavior every time

## Slide 7: Dynamic Branch Prediction for Direction
Predict branch based on past history of branch
One-bit Branch History Table (BHT)
PC
.
.
.
.
.
2N entries
Prediction
N bits
FSM
Update
Logic
Table update
Actual outcome
BHT: a cache of recent branches
Each entry stores last direction that the indexed branch went (1 bit to encode taken/not-taken)
No need to decode to know if it is a branch, just look at instr. address
Hash
Notes: Branch History Table (BHT)
Indexed by PC (or fraction of it)
Each entry stores last direction that the indexed branch went (1 bit to encode taken/not-taken)
Table is a cache of recent branches
Buffer size of 4096 entries are common (track 4K different branches)
When branch direction is resolved, go back into the table and update entry: 0 if not taken, 1 if taken

## Slide 8: Problems with the Simple Predictor
Aliasing:
  Two branches may be hashed to the same entry  branch prediction history is polluted
  Solution: make the table bigger, apply other cache optimization strategies
Always mispredict twice for a loop, e.g.,
  for (i=0; i<4; i++) { … }
0
Pred
Actual
T
T

1
1

T
T

1
1
NT
0


T
1

T

1

T
T

1
1
NT
0

T
1


## Slide 9: 2-bit Counter
2-bit saturating up/down counter predictor
Not Taken
Taken
Predict Not taken
Predict taken
ST: Strongly Taken
WT: Weakly Taken
WN: Weakly Not Taken
SN: Strongly Not Taken
01/
WN
00/
SN
10/
WT
11/
ST
Give inertial in responding external changes

## Slide 10: For More Advanced Branch Prediction …
Hypothesis: recent branches are correlated; that is, behavior of recently executed branches affects prediction of current branch
Two possibilities: current branch depends on
  Local behavior: Last m outcomes of the same branch (local branch predictor), e.g., a loop of 3 iterations is executed repetitively  a history record of the loop branch of the last 6 iterations should be able to predict the direction of that branch correctly
  Global behavior: Last m most recently executed branches  because branches are often correlated!
BHT predicts this

## Slide 11: Branches Are Correlated!
Branch direction of multiple branches
  Not independent but correlated to the path taken
Example: path 1-1 of b3 can be known beforehand
if (aa==2) // b1
aa = 0;
if (bb==2) // b2
bb = 0;
if (aa!=bb) {// b3
……
}
b1
b2
b2
b3
b3
b3
1 (T)
1
1
0 (NT)
0
b3
0
Path: A:1-1
B:1-0
C:0-1
D:0-0
aa=0
bb=0
aa=0
bb2
aa2
bb=0
aa2
bb2
How to capture global behavior?

## Slide 12: Capturing Global Branch Correlation
Idea: associate branch outcomes with global T/NT history of “all” branches
  Make a prediction based on outcome of the branch the last time the same global branch history was encountered
Implementation:
  Keep track of the “global T/NT history” of all branches in a register  Global History Register (GHR)
  Use GHR to index into a table that records the outcome that was seen for each GHR value in the recent past  Pattern History Table (table of 2-bit counters)
Global history/branch predictor
  Uses two levels of history (GHR + history at that GHR)

## Slide 13: Two Level Global Branch Prediction
1st level: Global Branch History Register (N bits)
  The direction of last N branches
2nd level: Table of saturating counters for each history entry
1
1
. . . . .
1
0
00…..00
00…..01
00…..10
11…..11
11…..10
Branch History Pattern
Pattern History Table (PHT)
Prediction
Rc-k
Rc-1
Actual branch outcome
FSM Update
Logic
Branch History Register (BHR)
(Shift left when update)
N
2N entries
Current state
PHT update

## Slide 14: How Does the Global Predictor Work?
Branch b1 tests i & last 3 branches test j.
 History: TTN
Predict taken for i  Next history: TNT
(shift in last outcome)
BHR
for(i=0; i<100; i++) {
for(j=1; j<3; j++) {
...
} // b2
...
} // b1
Outcome of b1 at i=7
b2 at i=7, j=1
b2 at i=7, j=2
b2 at i=7, j=3
b1 at i=8
Outcome of b2 at i=6, j=3
Notes: Start with j=3, last iteration that is not taken…

## Slide 15: Differentiating Per Branch Behavior
Two different branches may have the same global branch history but behave differently
Global
BHR
Global PHT
GAg
Global
BHR
..
Addr(B)
Per-addr PHTs
(PPHTs)
GAp
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 16: Capturing Local Correlation
But, we still want to capture the behavior of the same branch
for(i=0; i<100; i++)
for(j=0; j<3; j++) {
if (aa==2) aa = 0;
if (bb==2) bb = 0;
if (aa!=bb) {...}
}
Idea: have a per-branch history register
Addr(B)
Per-addr
PHTs (PPHTs)
PAp
.
.
.
Addr(B)
Per-addr
BHT (PBHT)
..
.
.
.
.
.
.
.
.
.

## Slide 17: Hybrid Branch Predictor
Some branches correlated to global history, some correlated to local history
  Use more than one type of predictors and select “best”
P0
P1
.
.
.
Choice (or Meta) Predictor
Branch PC
Final Prediction

## Slide 18: Tradeoff between Cost and Precision
Idea: add more context infor. to the global predictor to take into account which branch is being predicted (local predictor)
  Gshare: GHR hashed with the Branch PC
  + Better utilization of PHT
  -- Increases access latency

## Slide 19: Outline
Prediction of branch direction:
  Static
  Dynamic
  Branch correlation
Prediction of branch target

## Slide 20: Prediction of Branch Targets
Need target address at same time as prediction
  Branch Target Buffer (BTB): use PC to access I$ and simultaneously look up BTB to get prediction AND branch address (if taken)
Branch PC
Predicted PC
=?
PC of instruction
Fetch
Yes: instruction is branch and use predicted PC as next PC
No: branch not predicted, proceed normally
Branch predicted
taken or untaken

## Slide 21: How about Subroutine Returns?
Different call sites make return address hard to predict
  printf() may be called by many callers
  Target of “return” instruction in printf() is a moving target
But return address is actually easy to predict
  It is the address after the last call instruction that have not returned from yet
  Can use a Return Address Stack (RAS)
RAS:
  Call will push return address on the stack
  Return uses the prediction of top-of-stack

## Slide 22: Return Address Stack
+
4
Call PC
Push
Return
Address
BTB
Return PC
BTB
Return?
May not know if it is a return instruction prior to decoding
  Rely on BTB for speculation
  Fix once recognize Return

## Slide 23: Outline
Prediction of branch direction:
  Static
  Dynamic
  Branch correlation
Prediction of branch target
Predicated execution

## Slide 24: Predicated Execution
Idea: compiler converts control dependence into data dependence  branch is eliminated
  Each instr. has a predicate bit set based on the predicate computation
  Only instr. with TRUE predicates are committed (others become NOPs)
if (cond) {
b = 0;
}
else {
b = 1;
}
D
B
C
D
A
(predicated code)
A
B
C
p1 = (cond)
(!p1) mov b, 1
(p1) mov b, 0
add x, b, 1
D
(normal branch code)
C
B
D
A
T
N
p1 = (cond)
branch p1, TARGET
mov b, 1
jmp JOIN
TARGET: mov b, 0
A
B
C
add x, b, 1

## Slide 25: Conditional Move Operations
Very limited form of predicated execution
CMOV R1  R2
  R1 = (ConditionCode == true) ? R2 : R1
  Employed in most modern ISAs (x86, Alpha)
  if (a == 5) {b = 4;} else {b = 3;}
  CMPEQ condition, a, 5;
  CMOV condition, b  4;
  CMOV !condition, b  3;

## Slide 26: Recap
Branch History Table: 2 bits for loop accuracy
Correlation: recently executed branches correlated with next branch.
  Either different branches
  Or different executions of same branches
2-level predictor
  Branch history and pattern history
Branch Target Buffer: include branch address and prediction
Return address stack for return address of calls