## Slide 1: CS5100 Advanced Computer Architecture Advanced Techniques for ILP
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. Hsien-Hsin Lee, Prof. Yasun Hsu)

## Slide 2: So Far, Focus on ILP for Pipelines
Branch prediction
  Shorten branch decision time  reduce impact of control dependence
Dynamic scheduling and out-of-order execution:
  Do not allow a long-latency instruction to block the execution of following independent instructions
ROB and speculative execution
1
PC Fetch
Rename
Dispatch
Reg File
Exec
Commit
Br
PC Fetch
Rename
Dispatch
Reg File
Exec
Commit
ROB

## Slide 3: Pipelining Delivers CPI = 1 at Best
How to get CPI < 1?
  Issuing and completing multiple instructions/cycle
  Challenge: checking and resolving dependences among the instructions issued at the same cycle
Lecture outline:
  Multiple issue and static scheduling (Sec. 3.7)
  Dynamic scheduling, multiple issue, and speculation (Sec. 3.8)
  Multithreading: exploiting thread-level parallelism to improve uniprocessor throughput (Sec. 3.12)
  Advanced techniques for instruction delivery and speculation (Sec. 3.9)

## Slide 4: Dependences in Multiple Issue
If DIVD is to be issued at the same cycle as SUBD, how to know and resolve the RAW hazard between them?

## Slide 5: Strategies for Multiple Issue
Superscalar: varying number of instructions/cycle (1 to 8), scheduled by compiler (static) or by HW (dynamic)
  IBM PowerPC, Sun UltraSparc, DEC Alpha, Pentium 4, i7
Very Long Instruction Words (VLIW): fixed number of instructions (4-16) in a long instruction or a fixed instruction packet, scheduled statically by compiler
  Intel architecture-64 (IA-64) 64-bit address (renamed: “Explicitly Parallel Instruction Computer (EPIC)”)

## Slide 6: Strategies for Multiple Issue
Superscalar: fetch and issue multiple instructions at the same cycle

## Slide 7: Strategies for Multiple Issue
VLIW (Very Long Instruction Word):
  Use multiple independent functional units
  Multiple operations packaged into a very long instruction
  Compiler responsible for ensuring hazard-free

## Slide 8: Issuing Multiple Instructions/Cycle
Static multiple issue
  Compiler handles data and control hazards and decides what instructions can be issued in the same cycle
  Often restrict mix of instructions can be initiated in a clock
  Recompilation required for machines with diff. pipelines
Dynamic multiple Issue
  Fetch, decode, and commit multiple instructions
  Use dynamic pipeline scheduling, HW-based speculation and recovery
  Always beneficial if compiler can help, but recompiling not required for new machines

## Slide 9: Comparing Multiple-Issue Processors

## Slide 10: The VLIW Approach
High HW cost for checking parallelism, so …
VLIW: tradeoff for simple decoding
  A VLIW instruction has many fields for many operations, e.g., 2 INT, 2 FP, 2 memory, 1 branch  16--24 bits/field, or 112--168 bits wide
  Compiler packs multiple independent operations into one very long instruction  HW performs minimal check
  In general, operations that compiler puts in instruction word can execute in parallel, but can indicate otherwise
  Need compiler to schedule across basic blocks  e.g., loop unrolling, trace scheduling, software pipeline

## Slide 11: VLIW Processor
Register File
Op
Rd
Ra
Rb
Op
Rd
Ra
Rb
Op
Rd
Ra
Rb
Instruction Cache
PC
Instruction word consists of several conventional 3-operand instructions, one for each FU
Register file has 3N ports to feed N FUs

## Slide 12: The VLIW Approach
Rely on compiler for instruction scheduling
  HW designs are simpler or superfluous
  Higher possible clock rate due to reduced complexity
  Extra memory space and bandwidth
Compiler takes full responsibility for detection and removal of control, data, and resource dependences
  Compiler has to know the detailed characteristics of processor and memory, such as number and type of execution units, latencies and repetition rates, memory load-use delay, etc.
Sensitivity of compiler to architecture makes it harder to use same compiler for different VLIW lines

## Slide 13: The Superscalar Approach
Modern microarchitectures normally include dynamic scheduling + multiple issue + speculation
Two approaches:
  Assign reservation stations and update pipeline control tables in half clock cycles  superpipelining
    Only supports 2 instructions/clock
  Design logic to handle some or all possible dependencies between the instructions
  Hybrid approaches are possible
Issue logic can become bottleneck

## Slide 14: Operations for Multiple Issue
Limit the number of instructions of a given class that can be issued in a “bundle”
  i.e. one FP, one integer, one load, one store
Assign a RS and a ROB for every instruction that might be issued in the next issue bundle
Examine all the dependencies among the instructions in the bundle
If dependencies exist in bundle, use assigned ROB to update RS
Also need multiple completion/commit

## Slide 15: Superscalar vs. VLIW
Smaller code size
More complex issue logic
  check dependencies
  check structural hazards
  issue variable number of instructions (0-N)
Run existing binaries
Datapath identical
Branch prediction and dynamic memory disambiguation
Precise exception
Larger window of instructions examined
Simplify HW
Higher possible clock rate
Extra memory space, BW
More registers, but simple
Lockstep execution (static schedule)
  Sensitive to long latency operations (cache misses)
Poor code ‘density’
Must recompile sources
Implementation visible

## Slide 16: Limits to Multi-Issue Processors
Inherent limitations of ILP
  1 branch in 5: How to keep a 5-way VLIW busy?
  Need about Pipeline Depth x No. Functional Units of independent operations to keep all pipelines busy
  Difficulties in building HW
    Easy: more instruction bandwidth, duplicate FUs
    Hard: increase ports to RF and memory (bandwidth)
Most techniques for increasing performance also increase power consumption
  Growing gap between peak issue rates and sustained performance  performance gain is not linearly proportional to power increase

## Slide 17: How to Find More Parallelism?
Hardware?
Compiler?
Runtime environment, e.g., virtual machine?
The key is to find independent instructions
But, our attentions are focused mainly on the current thread of execution  why not from other programs or threads?  the instructions are completely independent
Programmer may need to be involved
  Parallel programming, program annotations, ...

## Slide 18: Use Multithreading to Help ILP
One idea: allow instructions from different threads to be mixed and executed together in the pipeline
  Original: pipeline with internal forwarding
  Multithreaded pipeline:
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
T1: LW r1, 0(r2)
<bubble>
T1: SUB r5, r1, r4
T1: AND r4, r1, r3
T1: SW 0(r7), r5
t9
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
T1: LW r1, 0(r2)
T2: ADD r7, r1, r4
T3: XORI r5, r4, #12
T4: SW 0(r7), r5
T1: SUB r5, r1, r4
t9
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
No need for internal forwarding

## Slide 19: Outline
Multiple issue and static scheduling (Sec. 3.7)
Dynamic scheduling, multiple issue, and speculation (Sec. 3.8)
Multithreading: exploiting thread-level parallelism to improve uniprocessor throughput (Sec. 3.12)
Advanced techniques for instruction delivery and speculation (Sec. 3.9)
18

## Slide 20: Hardware Multithreading
Exploiting thread-level parallelism (TLP)
  TLP from multiprogramming (from indep. sequential jobs)
  TLP from multithreaded applications
Need to maintain for each thread its own context (prog. state)  multiple register files
  PC, general purpose registers, virtual-memory page-table-base register, exception-handling registers, stack, …
Strategies for executing instructions from different threads in the same pipeline
  Mixed execution of instructions from different threads
  Thread context switch every cycle (we have just seen it)
  Thread context switch on long-latency events (traditional)

## Slide 21: Strategies for Multithreaded Execution
Time (processor cycle)
Superscalar
Fine-Grained
Coarse-Grained
Simultaneous
Multithreading
Thread 1
Thread 2
Thread 3
Thread 4
Thread 5
Idle slot
Instruction Issue capability

## Slide 22: Fine-Grained Multithreading
Interleave execution of instructions from different program threads on same pipeline
F
D
X
M
W
t0
t1
t2
t3
t4
t5
t6
t7
t8
T1: LW r1, 0(r2)
T2: ADD r7, r1, r4
T3: XORI r5, r4, #12
T4: SW 0(r7), r5
T1: SUB r5, r1, r4
t9
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
F
D
X
M
W
Interleave 4 threads, T1-T4, 5-stage pipe, no internal forwarding
Prior instruction in a thread always completes write-back before next instruction in same thread reads register file

## Slide 23: Fine-Grained Multithreading
Advantage:
  Hide both short and long stalls, e.g., latency of memory operations, dependent instructions, branch resolution, etc., since instructions from other threads executed when one thread stalls  latency hiding
  Utilize processing resources more efficiently
Disadvantage:
  Slow down execution of individual threads, since a thread ready to execute without stalls will be delayed by instructions from other threads
  Must have enough threads available

## Slide 24: Fine-Grained Multithreading Pipeline
Carry thread-select down pipeline to ensure correct state bits read/written at each pipe stage
  Appears to software (including OS) as multiple, albeit slower, CPUs
+1
2
Thread select
PC
1
PC
1
PC
1
PC
1
I$
IR
GPR1
GPR1
GPR1
GPR1
X
Y
2
D$

## Slide 25: Coarse-Grained Multithreading
Switches threads only on costly stalls, such as L2 cache misses or when an explicit context switch instruction is encountered
  Instructions from one thread use the pipeline for a certain period of time  Switch-on-event multithreading
  Can hide the latency
Possible stall events
  Cache misses
  Synchronization events (e.g., load an empty location)
  FP operations
Issue width
Time

## Slide 26: Coarse-Grained Multithreading
Advantages:
  Relieve the need to have very fast thread-switching
  Do not slow down thread, since context-switch only when the thread encounters a costly stall
  Priority may be given to critical thread
Disadvantages:
  Instructions must be drained and refilled on a context switch  bad for long pipeline, good only for costly stalls
  Fairness: a low cache miss thread gets to use pipeline longer and other threads may starve
    Possible solution: low miss thread may be preempted after a time slice expires, forcing a thread switch

## Slide 27: Simultaneous Multithreading (SMT)
Interleave multiple threads to multiple issue slots with no restrictions
  Dispatch instructions from multiple threads in the same cycle (to keep multiple execution units utilized)
  Allow better resource utilization within pipeline stage
Issue width
Time
[Tullsen, Eggers, Levy, UW, 1995]

## Slide 28: SMT Adapts to Parallelism Type
Issue width
Time
Issue width
Time
For regions with high thread level parallelism (TLP), entire machine width is shared by all threads
For regions with low TLP, entire machine width is available for instruction level parallelism (ILP)

## Slide 29: Resources in Typical SMT
Per thread:
  State for hardware context (separate PC, arch register file, rename mapping table, reorder buffer, L/S queues, etc.)
  Instruction commit/retirement, exception, subroutine return stack
  Per thread id in TLB
  BTB may be shared or have separate thread id (optional)
  Ability to fetch instructions for multiple threads (I cache port)
Shared
  Physical register, cache hierarchy, TLB (with TID), branch predictor and branch target buffer, functional units

## Slide 30: SMT Fetch
Duplicate fetch logic
Cycle-multiplexed fetch logic
I$
fetch
fetch
fetch
Decode, Rename, Issue
PC0
PC1
PC2
RS
I$
PC0
PC1
PC2
cycle % N
Round robin
fetch
Decode, etc.
RS

## Slide 31: Early Design: Alpha 21464 4-way SMT
SMT with 4 threads. Each thread appears to the outside world as executed sequentially
Fetch
Decode/Map
Queue
Reg Read
Execute
Dcache/Store Buffer
Reg Write
Retire
Icache
Dcache
PC
Register Map
Regs
Regs

## Slide 32: Observations on SMT
Higher throughput
  May be useful for server
May incur longer latency for a single thread
  Instruction fetch complexity
  Increase associativity of TLB and L1 cache
  Larger L2 cache, etc., to handle multiple threads
  May increase cache misses/conflicts
  Complexity in branch prediction and committing multiple threads simultaneously
  More registers (per thread RF, rename mapping table)
  Stretch hardware design and may affect cycle time

## Slide 33: Effects of SMT on Cache
Cache thrashing
I$
D$
Thread0 just fits in
the Level-1 Caches
Executes
reasonably
quickly due
to high cache
hit rates
Context switch to Thread1
I$
D$
Thread1 also fits
nicely in the caches
I$
D$
Caches were just big enough
to hold one thread’s data, but
not two thread’s worth
L2
Now both threads have
significantly higher cache
miss rates

## Slide 34: Outline
Multiple issue and static scheduling (Sec. 3.7)
Dynamic scheduling, multiple issue, and speculation (Sec. 3.8)
Multithreading: exploiting thread-level parallelism to improve uniprocessor throughput (Sec. 3.12)
Advanced techniques for instruction delivery and speculation (Sec. 3.9)
33

## Slide 35: Instruction Supply Issues
Fetch throughput defines max performance that can be achieved in later stages
  Superscalar processors need to supply more than one instruction per cycle
Instruction supply limited by
  Misalignment of multiple instructions in a fetch group
  Change of flow (interrupting instruction supply)
  Memory latency and bandwidth
Instruction
fetch unit
Execution
core
Instruction buffer

## Slide 36: Instruction Supply
Objective: fetch N instructions per machine cycle based on PC
  Imply each row of I-cache stores at least N instructions and the entire row can be accessed at a time
  The N instructions that are specified by this PC + the next N-1 sequential addresses form a fetch group
Challenges:
  Misalignment: not all N instructions in same row. Fetch group crosses row boundary  require extra row access  aligned access?
  The presence of branches in the fetch group
Instruction cache
PC
4 instructions to be fetched (fetch group)

## Slide 37: Multiple Branch Prediction (MBP)
Fetch address could be retrieved from BTB
Predicted path: BB1  BB2  BB5 (next page)
How to fetch BB2 and BB5 from BTB?
  Can’t! Branch PCs of br1 and br2 not available when MBP made
  Use a branch address cache (BAC) design
BB1
br1
BB2
br2
BB3
BB4
BB5
BB6
BB7
T (2nd)
F
T
T
F (3rd)
F
Fetch address
(br0 primary prediction)
BTB entry

## Slide 38: Multiple Branch Predictor [YehMarrPatt ICS’93]
Pattern History Table (PHT) to support MBP
Based on global history only
Branch History Register (BHR)
Pattern History Table (PHT)
bk
……
b1
Primary prediction
Secondary prediction
Tertiary prediction
p1
p2
p1
p2
update

## Slide 39: Branch Address Cache (BAC)
Keep 6 possible fetch addresses for two more predictions
  br: 2 bits for branch type (cond, uncond, return)
  V: 1 valid bit (to indicate if hits a branch in the sequence)
Tag
23 bits
Taken
Target Address
Not-Taken Target Address
T-T Address
T-N Address
N-T Address
N-N Address
30 bits
30 bits
V
br
V
br
V
br
212 bits per fetch address entry
1
2
Fetch Addr (from BTB)

## Slide 40: Fetch from Non-Consecutive Basic Blocks
Requirement: high fetch bandwidth + low latency
BB2
BB1
BB3
BB4
BB5
Fetch in conventional instruction cache
BB2
BB1
BB3
BB4
BB5
Fetch from linear memory location

## Slide 41: Fetch from Multiple Basic Blocks
Trace cache: pack multiple non-contiguous basic blocks into one contiguous trace cache line
  Single fetch brings in multiple basic blocks
  Used in Intel Pentium-4 processor to hold decoded micro operations
BR
BR
BR
BR
BR
BR
Trace cache

## Slide 42: Integrated Instruction Fetch Unit
Multiple issue processors demand issuing multiple instructions per cycle
  Fetch unit must fetch multiple instructions, while branches arrive faster in N-issued processor
Desirable to have a separate, autonomous fetch unit that feeds instructions to rest of pipe, which includes
  Integrated branch prediction to constantly predicting branches to drive fetch pipeline
  Instruction prefetch: prefetch from taken branch location
  Instruction memory access and buffering: multiple outstanding cache misses, prefetching to deal with crossing cache lines

## Slide 43: Recap
Multiple issue processor:
  Superscalar vs VLIW
  Static vs dynamic
TLP explicitly uses multiple threads of execution that are inherently parallel
  Fine-grained
  Coarse-grained
  Simultaneous multithreading
Handling branches for instruction fetch
  Instruction alignment
  Handling multiple branches: trace cache