## Slide 1: CS5100 Advanced Computer Architecture Graphics Processing Units
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. O. Mutlu, D. Sanchez, J. Emer, P. Cozzi, D. Luebke, T. Thorne,
http://www.es.ele.tue.nl/~heco/courses/EmbeddedComputerArchitecture/GPU.ppt)

## Slide 2: Outline
Introduction to parallel processing and data-level parallelism (Sec. 4.1)
Vector architecture (Sec. 4.2)
SIMD instruction set extensions (Sec. 4.3)
Graphics processing units (Sec. 4.4)
  Introduction to graphics pipeline
  CUDA programming model
  GPU architectures
Detecting and enhancing loop-level parallelism (Sec. 4.5)

## Slide 3: Computer Graphics Processing
Computer graphics require many stages of processing, which can be implemented as a pipeline
Computer graphics concern with the pixels drawn on the screen and thus are data parallel in nature
Geometric objects (in triangles)
Properties: color, textual, …
Move camera and objects around
Frame Buffer
Pixels
Graphics pipeline

## Slide 4: A High-Level View of Graphics Pipeline
GPU
CPU
Application Processing
Geometry Processing
Rasterization
(Vertex pipeline)
(Pixel pipeline or fragment pipeline)

## Slide 5: Application Stage
Read data
  3D models from world geometry database
    Commonly represented as triangles in 3D with attributes, e.g. color, normal vector, texture, transparency
    Vertices of triangles are the primary data to operate on
  User’s input by mouse, sensing gloves, …  changes the view or scene

## Slide 6: Geometry Stage
Transforming objects
  Model and view transformation
Illumination and shading (for vertices)
Model and View Transformation
Loaded 3D Models
Shading: reflection and lighting
Projection Transformation
Hidden Surface Elimination

## Slide 7: Geometry Stage: Model Transformation
Put objects into the scene to required position, size, orientation by applying translation, scaling, rotation
  Locations of all vertices are updated

## Slide 8: Geometry Stage: View Transformation
Transforming the scene such that the view point is at the origin, viewing direction is aligned with the negative Z axis and the view-up vector is aligned with the positive Y axis
  Uses rotation and translation

## Slide 9: Geometry Stage: Perspective Projection
Create a picture of scene viewed from the camera
  Apply a perspective transformation to convert the 3D coordinates to 2D coordinates of the screen
  Objects far away appear smaller, closer objects bigger
X
Y
-Z
near
far

## Slide 10: Geometry Stage: Hidden Surface Removal
Objects hidden by other objects must NOT be drawn
Clipping
  Not everything should be visible on the screen
  Any vertices that lie outside of the viewing volume are clipped

## Slide 11: Geometry Stage: Shading
Decide the colour of each vertex of object taking into account the object’s colour, lighting condition and the camera position
Object
point light source

## Slide 12: Geometry Stage: Coloring and Lighting
Objects coloured based on its own colour and the lighting condition
One colour for one face
Lighting calculation per vertex

## Slide 13: Geometry Stage: Coloring and Lighting
Light reflected in a mirror-like way

## Slide 14: Rasterization Stage
Rasterization and Sampling
Texture Mapping
Image Composition
Intensity and Colour Quantization
Geometry
Frame Buffer/Display
Pipeline

## Slide 15: Rasterization Stage: Rasterization
Converts the vertex information output by the geometry pipeline into pixel information needed by the video display
  Generating pixels in the scan (horizontal) line order (top to bottom, left to right)
Pixel + associated data: color, depth, stencil, etc.
  Interpolate per-vertex quantities across pixels

## Slide 16: Rasterization Stage: Texture Mapping
Add other effects, e.g., reflections, shadows

## Slide 17: Putting it Together
Vertex processing: convert each vertex into a 2D screen position, apply lighting for its color
Primitive assembly and triangle setup: collect vertices and convert them into triangles
Rasterization: fill triangles with pixels known as "fragments“
Occlusion culling: removes pixels that are hidden by other objects in the scene
Parameter interpolation: compute values for each pixel that were rasterized based on color, fog, texture, etc.
Pixel shader: adds textures and final colors to the fragments
Pixel engines: combine final pixel color, its coverage and degree of transparency
http://www.pcmag.com/encyclopedia/term/43933/graphics-pipeline

## Slide 18: GPU Evolution
Till mid-90s
  VGA controllers used to accelerate some display functions
Mid-90s to mid-2000s
  Fixed-function accelerators for OpenGL and DirectX APIs
  3D graphics: triangle setup and rasterization, texture mapping, shading
Modern GPUs
  Programmable multiprocessors optimized for data-parallelism for both geometric and rasterization
  OpenGL/DirectX and general purpose languages (CUDA, OpenCL, …)
  From GPU to GPGPU (general-purpose computing on GPU)

## Slide 19: Outline
Introduction to parallel processing and data-level parallelism (Sec. 4.1)
Vector architecture (Sec. 4.2)
SIMD instruction set extensions (Sec. 4.3)
Graphics processing units (Sec. 4.4)
  Introduction to graphics pipeline
  CUDA programming model
  GPU architectures
Detecting and enhancing loop-level parallelism (Sec. 4.5)

## Slide 20: Programming GPU
Need a programming model that can handle a large number of triangles and pixels, all are operated on by the same operations
A suitable programming abstraction is multithreading, one thread for each triangle/pixel
CUDA (Compute Uniform Device Architecture)
  Expresses DLP in terms of TLP
  Host (typically CPU) and device (typically GPU) interact through command buffer
CPU writes commands here
GPU reads commands from here
Pending GPU commands

## Slide 21: CUDA Program
Contains both host and device code
Device code is enclosed in C functions called kernels
Example: matrix addition
void MatAdd(float A[N][N],float B[N][N],float C[N][N]) {
for(int i = 0; i < N; i++)
for(int j = 0; j < N; j++)
C[i][j] = A[i][j] + B[i][j];
}
int main() {
...
MatAdd(A, B, C);
...
}
Sequential version

## Slide 22: Matrix Addition: CUDA Code
// Kernel definition
__global__ void MatAdd(float A[N][N], float B[N][N],
float C[N][N]) {
int i = threadIdx.x;
int j = threadIdx.y;
C[i][j] = A[i][j] + B[i][j];
}
int main() {
...
// Kernel invocation with 1 block of N*N*1 threads
int numBlocks = 1;
dim3 threadsPerBlock(N, N);
MatAdd<<<numBlocks, threadsPerBlock>>>(A, B, C);
...
}

## Slide 23: CUDA Programming Model
A kernel is executed by a grid of thread blocks
  A thread block is a set of threads that can cooperate with each other through shared memory
  All threads run the same code: extremely lightweight, very little creation overhead, fast switching  data parallel
  Each thread has an ID that it uses to compute memory addresses for data and make control decisions
  Hardware converts TLP into DLP at run time

## Slide 24: CUDA Programming Model
One kernel is executed at a time
Multidimensional thread organization:
  Block ID: 1D or 2D
  Thread ID: 1D, 2D, or 3D
  Specified by execution configuration: <<<BlocksPerGrid, threadsPerBlock>>>

## Slide 25: Thread Organization
Example: both grid and thread block have 2D index
kernelF<<<(2,2),(2,4)>>>(A);
__device__ kernelF(A){
i = blockDim.x * blockIdx.x
+ threadIdx.x;
j = blockDim.y * blockIdx.y
+ threadIdx.y;
A[i][j]++;
}
2  4

## Slide 26: Thread Block Scheduling
Thread blocks are executed independently
  Allows thread blocks to be scheduled in any order across any number of cores
Hardware is free to schedule thread blocks on any processor

## Slide 27: Outline
Introduction to parallel processing and data-level parallelism (Sec. 4.1)
Vector architecture (Sec. 4.2)
SIMD instruction set extensions (Sec. 4.3)
Graphics processing units (Sec. 4.4)
  Introduction to graphics pipeline
  CUDA programming model
  GPU architectures
Detecting and enhancing loop-level parallelism (Sec. 4.5)

## Slide 28: CUDA Multithreading
Basic programming model of CUDA: multithreading
  data parallel  one thread (same code) for one data
How to make use of the huge number of threads?
Latency hiding to simplify hardware:
  Granularity of thread interleaving (context switch time):
    100 cycles: hide off-chip memory latency
    10 cycles: + hide cache latency
    1 cycle: + hide branch latency, instruction dependency

## Slide 29: Hardware Support for Multithreading
Multiple thread contexts stored in HW registers
Register file supports zero overhead context switch between interleaved threads
Notes: The address assignment and translation is done dynamically by hardware.

## Slide 30: Data Lanes to Form Array Processing
Replicate to handle large number of triangles/pixels  array proc.
All PEs execute same instruction
PC 0
PC 1
...
PC n-1
Notes: From scalar to vector.

## Slide 31: With and Without Multithreading
Pros:
reduce cache size,
no branch predictor,
no OOO scheduler
Cons:
register pressure,
thread scheduler,
require huge parallelism
Very high computation density

## Slide 32: Multithreading in Array Processors
All PEs run same instruction but on different data (SIMD)
The m concurrent threads form a warp (in CUDA)
To hide memory latency, n warps are executed in an interleaved fashion
The mn threads form a thread block
Register values of all threads stay in register file
No OS context switching
Decode
R
F
R
F
R
F
A
L
U
A
L
U
A
L
U
D-Cache
Thread Warp 6
Thread Warp 1
Thread Warp 2
Data
All Hit?
Miss?
Warps accessing
memory hierarchy
Thread Warp 3
Thread Warp 8
Writeback
Warps available
for scheduling
Thread Warp 7
I-Fetch
SIMD Pipeline (PE)
Slide credit: Tor Aamodt
Notes: Warp can be grouped at run time by hardware. In this case it will be transparent to the programmer.
With a large number of shader threads multiplexed on the same execution resources, our architecture employs fine-grained multithreading, where individual threads are interleaved by the fetch unit to proactively hide the potential latency of stalls before they occur. As illustrated by Figure, warps are issued fairly in a round-robin queue. When a thread is blocked by a memory request, shader core simply removes that thread’s warp from the pool of “ready” warps and thereby allows other threads to proceed while the memory system processes its request.
With a large number of threads (1024 per shader core) interleaved on the same pipeline, FGMT effectively hides the latency of most memory operations since the pipeline is occupied with instructions from other threads while memory operations complete. also hides the pipeline latency so that data bypassing logic can potentially be omitted to save area with minimal impact on performance. simplify the dependency check logic design by restricting each thread to have at most one instruction running in the pipeline at any time.

## Slide 33: Array Processors in Multicore
Duplicate cores for multicore
Simplify thread scheduler
Stream Multiprocessor (SM) in CUDA terms
  SFU: Special Function Unit
Notes: The NVIDIA Fermi PE can do int and fp.

## Slide 34: Putting It Altogether
NVIDIA Fermi GTX 480 GPU
  16 SMs, executing a grid of thread blocks
  6 GDDR5 ports, each 64 bits, supporting up to 6 GB of capacity
  Host Interface: PCI Express 2.0
  Plus fixed graphics functions
Fig. 4.15

## Slide 35: Now You Know the Reasons Why …
Thread blocks must be independent
  Any possible interleaving of blocks should be valid
    presumed to run to completion without pre-emption
    can run in any order, concurrently OR sequentially
  Thread blocks may not synchronize
  Threads in different blocks cannot cooperate
Threads within a block may cooperate via shared memory, because they are allocated to the same SM
Several blocks can reside concurrently on one SM
  Number is limited by SM resources
  Registers are partitioned among all resident threads
  Shared memory is partitioned among all resident blocks
Notes: CUDA threads in a thread block may be scheduled to different warps by hardware and they may be executed in an interleaved fashion. However, they all can communicate with each other through shared memory.

## Slide 36: An Example Stream Multiprocessor (SM)
Called Multithreaded SIMD Processor in the textbook
  16 PEs (SIMD Lanes)
  48 threads of SIMD instructions
Fig. 4.14

## Slide 37: Thread Scheduling
Among SMs: Thread block scheduler (like a control processor) schedules thread blocks to SMs (multithreaded SIMD processors)
Inside a SM: SIMD thread scheduler uses scoreboard to track which SIMD thread is ready and dispatch those threads
  Can do flexible scheduling policies, from fine-grain to coarse-grain
For Fermi:
  Each 32-wide thread of SIMD instructions (a warp with 32 CUDA threads) is executed by 16 physical SIMD Lanes (PEs)  each SIMD instruction takes 2 cycles
Fig. 4.16

## Slide 38: Example Implementation
Notes: This example assumes the two warp schedulers are decoupled. It is possible that they are coupled together, at the cost of hardware complexity.

## Slide 39: Example
Program Address: Inst
0x0004: add r0, r1, r2
0x0008: sub r3, r4, r5
Assume warp 0 and warp 1 are scheduled for execution

## Slide 40: Read Src Op
Program Address: Inst
0x0004: add r0, r1, r2
0x0008: sub r3, r4, r5
Read source operands:
r1 for warp 0
r4 for warp 1
Notes: Assume the register file has one read port.
The register file may need two read port to support instructions with 3 source operands, e.g. the Fused Multiply Add (FMA).

## Slide 41: Buffer Src Op
Program Address: Inst
0x0004: add r0, r1, r2
0x0008: sub r3, r4, r5
Push ops to op collector:
r1 for warp 0
r4 for warp 1

## Slide 42: Read Src Op
Program Address: Inst
0x0004: add r0, r1, r2
0x0008: sub r3, r4, r5
Read source operands:
r2 for warp 0
r5 for warp 1

## Slide 43: Buffer Src Op
Program Address: Inst
0x0004: add r0, r1, r2
0x0008: sub r3, r4, r5
Push ops to op collector:
r2 for warp 0
r5 for warp 1

## Slide 44: Execute
Program Address: Inst
0x0004: add r0, r1, r2
0x0008: sub r3, r4, r5
Compute the first 16 threads in the warp

## Slide 45: Execute
Program Address: Inst
0x0004: add r0, r1, r2
0x0008: sub r3, r4, r5
Compute the last 16 threads in the warp

## Slide 46: Write back
Program Address: Inst
0x0004: add r0, r1, r2
0x0008: sub r3, r4, r5
Write back:
r0 for warp 0
r3 for warp 1

## Slide 47: Registers for Thread Contexts
Use the example Fermi
  16 physical lanes (PEs), each with 2048 registers  32768 32-bit registers in total  2 MB
  A SIMD thread (warp) operates on 32 CUDA threads  each lane must accommodate 2 CUDA threads
  Each SIMD thread is limited to 64 registers
  2048/64/2=16 SIMD threads (warps) can be interleaved
  In practice, physical registers are allocated to SIMD threads dynamically and thus more SIMD threads may be accommodated if they do not use up to 64 registers

## Slide 48: NVIDIA Instruction Set Architecture
PTX (Parallel Thread Execution)
  Use virtual registers and compiler allocates physical reg.
  Translation to machine code is performed in software
  All instructions can be predicated by 1-bit predicate registers, which can be set by setp instruction
  DAXPY example:
  shl.s32 R8, blockIdx, 9 ; R8 = i =blockIdx.x*blockDim.x (512 or 29)
  add.s32 R8, R8, threadIdx ; R8 = i = my CUDA thread ID
  ld.global.f64 RD0, [X+R8] ; RD0 = X[i]
  ld.global.f64 RD2, [Y+R8] ; RD2 = Y[i]
  mul.f64 RD0, RD0, RD4 ; Product in RD0 = RD0 * RD4 (scalar a)
  add.f64 RD0, RD0, RD2 ; Sum in RD0 = RD0 + RD2 (Y[i])
  st.global.f64 [Y+R8], RD0 ; Y[i] = sum (X[i]*a + Y[i])
Notes: blockDim.x = 512  i = blockDim.x * blockIdx.x + threadIdx.x (i is in R8)

## Slide 49: Control Flow Problem in GPUs
GPU uses SIMD pipeline to save area on control logic
  Group scalar threads into warps
Branch divergence occurs when threads inside warps branch to different execution paths
Branch
Path A
Path B
Branch
Path A
Path B
Slide credit: Tor Aamodt

## Slide 50: Branch Divergence Handling
-
G
1111
TOS
B
C
D
E
F
A
G
Thread Warp
Common PC
Thread
2
Thread
3
Thread
4
Thread
1
B/1111
C/1001
D/0110
E/1111
A/1111
G/1111
-
A
1111
TOS
E
D
0110
E
C
1001
TOS
-
E
1111
E
D
0110
TOS
-
E
1111
A
D
G
A
Time
C
B
E
-
B
1111
TOS
-
E
1111
TOS
Reconv. PC
Next PC
Active Mask
Stack
E
D
0110
E
E
1001
TOS
-
E
1111
Slide credit: Tor Aamodt

## Slide 51: Conditional Branching
Similar to vector processors, but masks are handled internally
  Per-warp stack stores PCs and masks of non-taken paths
On a conditional branch
  Push the current mask onto the stack
  Push the mask and PC for the non-taken path
  Set the mask for the taken path
At the end of the taken path
  Pop mask and PC for the non-taken path and execute
At the end of the non-taken path
  Pop the original mask before the branch instruction
If a mask is all zeros, skip the block

## Slide 52: CUDA Code for Branch Divergence
if (X[i] != 0) X[i] = X[i] – Y[i];
else X[i] = Z[i];
ld.global.f64 RD0, [X+R8] ; RD0 = X[i]
setp.neq.s32 P1, RD0, #0 ; P1 is predicate register 1
@!P1, bra ELSE1, *Push ; Push old mask, set new mask
; if P1 false, go to ELSE1
ld.global.f64 RD2, [Y+R8] ; RD2 = Y[i]
sub.f64 RD0, RD0, RD2 ; Difference in RD0
st.global.f64 [X+R8], RD0 ; X[i] = RD0
@P1, bra ENDIF1, *Comp ; complement mask bits
; if P1 true, go to ENDIF1
ELSE1: ld.global.f64 RD0, [Z+R8] ; RD0 = Z[i]
st.global.f64 [X+R8], RD0 ; X[i] = RD0
ENDIF1: <next instruction>, *Pop ; pop to restore old mask
Notes: *Push, *Comp, *Pop are branch synchronization markers inserted by the PTX assembler

## Slide 53: What About Memory Divergence?
All loads are gathers, all stores are scatters
SM address coalescing unit detects sequential and strided patterns, coalesces memory requests
Modern GPUs have caches, and ideally want all threads in the warp to hit (without conflicting with each other)
  Problem: one thread in a warp can stall the entire warp if it misses in the cache
  Need techniques to
    Tolerate memory divergence
    Integrate solutions to branch and memory divergence

## Slide 54: NVIDIA GPU Memory Structures
Each SIMD Lane has private section of off-chip DRAM, called private memory
  Contains stack frame, spilling registers, private variables
  Rely on multithreading to hide long latencies
Each SM (multithreaded SIMD processor) also has on-chip local memory
  Shared by SIMD lanes/threads within a block
Memory shared by SIMD processors is GPU memory
  Host can read and write GPU memory

## Slide 55: GPU Memory Structures
GPU Memory is shared by all grids
Local Memory is shared by all threads of SIMD instructions within a thread block
Private Memory is private to a single CUDA Thread
Fig. 4.18

## Slide 56: Fermi SM
Fig. 4.20
Each SIMD Lane has a pipelined floating-point unit, a pipelined integer unit, some logic for dispatching instructions and operands to these units, and a queue for holding results. The four Special Function units (SFUs) calculate functions such as square roots, reciprocals, sines, and cosines.

## Slide 57: Summary: NVIDIA GPU Architecture
Similarities to vector machines:
  Works well with data-level parallel problems
  Scatter-gather transfers
  Mask registers
  Large register files
Differences:
  No scalar processor
  Uses multithreading to hide memory latency
  Has many functional units, as opposed to a few deeply pipelined units like a vector processor