## Slide 1: CS5102 High Performance Computer Systems Symmetric Multiprocessors
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. O. Mutlu, Prof. Hsien-Hsin Lee, Prof. K. Asanovic,
http://compas.cs.stonybrook.edu/courses/cse502-s14/)

## Slide 2: Outline
Introduction (Sec. 5.1)
Centralized shared-memory architectures (Sec. 5.2)
Distributed shared-memory and directory-based coherence (Sec. 5.4)
Synchronization: the basics (Sec. 5.5)
Models of memory consistency (Sec. 5.6)

## Slide 3: Centralized Shared-Memory Architecture
Key insight: large multilevel caches can substantially reduce memory bandwidth demands of a processor  allow multiple processors to share memory
  Support caching of shared and private data
  Private data: used by a single processor
  Shared data: used by multiple processors  provide (indirect) communication among processors through reads and writes of shared data

## Slide 4: Shared Memory Model
Many parallel programs communicate through shared memory
P0 writes to an address, followed by P1 reading
  This implies communication between the two
Each read should receive the value last written not only by itself but also by anyone  need synch.
  What does last written mean?
What if Mem[A] is cached (at either end)?
Proc 0
Mem[A] = 1
Proc 1
…
Print Mem[A]

## Slide 5: Shared Memory Model
SMP needs to provide the illusion of a single shared memory
But, actually, it has multiple private caches for performance reasons
  Closer cache level can be private, and multiple copies of a cache block can be present in the private local cache across different processors
Basic question: If multiple processors cache the same block, how do they ensure they all see a consistent state (value)?
Local updates lead to incoherent state
  Problem in both write-through and writeback caches

## Slide 6: Example: Write-Back Cache
P0
Cache
Memory
P1
X= -100
X= -100
Cache
Pn
Cache
X= -100
X= 505
LD?
X= -100
LD?

## Slide 7: Example: Write-Through Cache
P0
Cache
Memory
P1
X= -100
X= -100
Cache
Pn
Cache
X= -100
X= 505
X= 505
X= 505
LD?

## Slide 8: Maintaining Coherence
Need to guarantee that all processors see a consistent value (i.e., consistent updates) for the same memory location
Informally:
  Any read must return the most recent write
  (Too strict and very difficult to implement)
Better:
  Any write must eventually be seen by a read
    If P0 writes x and P1 reads it, P0’s write will be seen if the read and write are sufficiently far apart
  All writes are seen in same order (“serialization”)
    e.g., w1 followed by w2 seen by a read from P1, will be seen in the same order by all reads by other processors

## Slide 9: Hardware Cache Coherence
System ensures everyone always sees latest value
  Basic strategy: let a write be known by all
  A processor/cache “broadcasts” its write/update to a memory location to all other processors/caches
  Another cache that has a local copy of the memory location either updates or invalidates its local copy
  Serialization: only one can broadcast at a time
How can we safely update replicated data?
  Option 1 (update protocol): push the update to all copies
  Option 2 (invalidate protocol): invalidate all others to ensure there is only one valid copy (local), and update it
    On a read: If local copy isn’t valid, request it either from the memory or from the node holding the valid copy

## Slide 10: Two Cache Coherence Methods
How to “broadcast” the update?
Snoopy bus: (you shout at everyone)
  Bus-based, single point of serialization for all requests
  Processor broadcasts updates on bus  totally ordered
  Processors observe (“snoop”) other processors’ actions
Directory: (you tell someone to inform all others)
  Directory tracks ownership (sharer set) for each block
  Processors explicitly request for blocks through directory
  Directory coordinates invalidation/update appropriately
  Serves as ordering point for conflicting requests in unordered networks
  No single broadcast media  more complex but scalable

## Slide 11: Snoopy Cache Coherence
All caches “snoop” all other caches’ read/write requests and keep the cache block coherent
  Cache controller updates cache block states in response to processor & snoop events and generates bus transactions
  Snoopy cache tags are dual-ported
Proc.
Cache
Snoopy read port
attached to memory bus
Data
(blocks)
Tags and
State
A
D
R/W
Used to drive memory bus
when cache is bus master
A
R/W

## Slide 12: Snoopy Cache Coherence
Easy to implement if all caches share a common bus
  Each cache broadcasts its read/write operations on bus
  Simple finite state machine (FSM) for each cache block
  Good for small-scale multiprocessors
CPU1
Memory
Bus
Main Memory (DRAM)
DMA
Snoopy Cache
CPU2
Snoopy Cache
CPU3
Snoopy Cache
Disk
DMA
Network

## Slide 13: Bus Snooping for Write-Through Cache
Allows multiple readers, but writes always through to memory via bus
All the writes will be seen as a transaction on the shared bus to memory
Two protocols
  Update-based protocol
  Invalidation-based protocol
P
P
P
$
Bus-based shared memory
$
$
Memory

## Slide 14: Bus Snooping (Update-based Protocol on Write-Through Cache)
Update local copies upon snoop hit
P1
Cache
Memory
P2
X= -100
X= -100
Cache
Pn
Cache
X= 505
Bus transaction
Bus snoop
X= 505
X= 505

## Slide 15: Bus Snooping (Invalidation-based Protocol on Write-Through Cache)
Invalidate local copies upon snoop hit (but the updated data has already been broadcasted on bus!)
P1
Cache
Memory
P2
X= -100
X= -100
Cache
Pn
Cache
X= 505
Bus transaction
Bus snoop
X= 505
Load X
X= 505

## Slide 16: Effects of Bus Snooping
When a processor writes to its local copy, this fact is broadcasted to all other caches and all caches will see the same update  write propagation
When two processors write to their individual local copy of the same data at almost the same time, one processor will win the bus and broadcast its update information to all other caches. The other update must wait until it can grab the bus. This guarantees that all other caches see the same order  write serialization

## Slide 17: Update vs. Invalidate Tradeoffs
Update
  + If sharer set is constant and updates are infrequent, avoid the cost of invalidate-reacquire (broadcast update pattern)
  - If data is rewritten without intervening reads by other processors, updates are useless
  - Write-through cache policy  bus becomes bottleneck
Invalidate
  + After invalidation broadcast, processor has exclusive rights
  + Only processors that keep reading after a write keep copy
  - Longer delay in reacquire the invalidated block
  - If write contention is high, leads to ping-ponging (rapid mutual invalidation-reacquire)

## Slide 18: A Simple Snooping Coherence Protocol
For a write-through, invalidation-based, no write-allocate cache
Processor requests
  Load, Store
Bus messages
  BusRd, BusWr
1 bit state per cache block
  Valid/Invalid
Store/BusWr
BusWr/--
Store/BusWr
Load/BusRd
Load/--
Valid
Invalid
Processor-initiated transaction
Bus-snooper-initiated transaction
Observed / Bus transaction
Notes: 9

## Slide 19: How about Write-Back Caches?
Write-back caches only write to local caches until the block is to be replaced
  Cache and memory may be incoherent
  Reduce bus write bandwidth  no bus activities on writes
What problems the valid-invalid protocol may have?
Solution 1: force every store to go to bus
Solution 2: ensure exclusive right to write
  No other cache, nor memory, has a valid copy except local  can write to local copy many times without letting others know
  Need to further differentiate Valid state: (1) exclusive and dirty, (2) shared and clean

## Slide 20: How about Write-Back Caches?
Divide “Valid” state into exclusive-dirty (Modified) and shared-clean (Shared)
  Modified: a cache block is in “Modified” state if it is the only valid and dirty copy in the SMP
    No other caches, nor memory, has a valid copy
    A cache owns its “Modified” blocks and can update them freely
    When another cache wants to read a “Modified” block, the block is updated to memory and supplied to that cache; its state now becomes “Shared”
  Shared: a cache block is in “Shared” state if it is clean  memory and perhaps other caches have up-to-date copies

## Slide 21: Cache Coherence Protocol (Update-based Protocol on Write-back Cache)
Update data for all processors who share the same data
Do not make sense for write-back caches  do not consider!
P1
Cache
P2
Cache
Pn
Cache
Bus transaction
X= -100
X= -100
X= -100
Store X
X= 505
update
update
X= 505
X= 505
Memory

## Slide 22: Cache Coherence Protocol (MSI) (Invalidation-based Protocol on Write-back Cache)
Invalidate the data copies for the sharing processor nodes
Reduced traffic when a processor node keeps updating the same memory location
P1
Cache
P2
Cache
Pn
Cache
Bus transaction
X= -100
X= -100
X= -100
Store X
invalidate
invalidate
X= 505
Memory

## Slide 23: Cache Coherence Protocol (MSI) (Invalidation-based Protocol on Write-back Cache)
Invalidate the data copies for the sharing processor nodes
Reduced traffic when a processor node keeps updating the same memory location
P1
Cache
P2
Cache
Pn
Cache
Bus transaction
X= 505
Load X
Bus snoop
Miss !
Snoop hit
X= 505
Memory

## Slide 24: Cache Coherence Protocol (MSI) (Invalidation-based Protocol on Write-back Cache)
Invalidate the data copies for the sharing processor nodes
Reduced traffic when a processor node keeps updating the same memory location
P1
Cache
P2
Cache
Pn
Cache
Bus transaction
X= 505
Store X
Bus snoop
X= 505
X= 333
Store X
X= 987
Store X
X= 444
Memory

## Slide 25: MSI Writeback Invalidation Protocol
Store/
BusWr
BusWr/--
Store/
BusWr
Load/
BusRd
Load/--
Valid
Invalid
Load, Store/--
BusRdX/--
Store/
BusWB
Load/
BusRd
Load/--
Shared
Invalid
Modified
Store/
BusRdX
BusRdX/--
BusRd/BusWB

## Slide 26: MSI Writeback Invalidation Protocol
Track 3 states per cache block
  Invalid: cache does not have a copy
  Shared: cache has a read-only, clean copy (memory or other caches are up-to-date)
  Modified: cache has the only valid copy; the copy is writable for local processor but dirty (memory or other caches are out-of-date)
Processor actions
  Load, Store, Evict (write back)
Bus transactions posted by cache controller
  BusRd, BusRdX, BusWB, …

## Slide 27: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
Memory
BusRd
X=10
X=10
S
Processor action | State in P1 | State in P2 | State in P3 | Bus transaction | Data supplier
S
---
---
BusRd
Memory
P1 reads X

## Slide 28: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
Memory
X=10
S
BusRd
X=10
S
X=10
Processor action | State in P1 | State in P2 | State in P3 | Bus transaction | Data supplier
S
---
---
BusRd
Memory
P1 reads X
P3 reads X
S
---
S
BusRd
Memory

## Slide 29: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
X=10
S
X=10
S
BusRdX
---
I
M
X=10
X=-25
Memory
Processor action | State in P1 | State in P2 | State in P3 | Bus transaction | Data supplier
S
---
---
BusRd
Memory
P1 reads X
P3 reads X
S
---
S
BusRd
Memory
P3 writes X
I
---
M
BusRdX
---

## Slide 30: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
X=-25
M
---
I
BusRd
X=-25
S
S
X=10
X=-25
Memory
Processor action | State in P1 | State in P2 | State in P3 | Bus transaction | Data supplier
S
---
---
BusRd
Memory
P1 reads X
P3 reads X
S
---
S
BusRd
Memory
P3 writes X
I
---
M
BusRdX
---
P1 reads X
S
---
S
BusRd
P3 Cache

## Slide 31: MSI Example
P1
Cache
P2
P3
Bus
Cache
Cache
X=-25
M
X=-25
S
S
X=10
X=-25
BusRd
X=-25
S
Memory
Processor action | State in P1 | State in P2 | State in P3 | Bus transaction | Data supplier
S
---
---
BusRd
Memory
P1 reads X
P3 reads X
S
---
S
BusRd
Memory
P3 writes X
I
---
M
BusRdX
---
P1 reads X
S
---
S
BusRd
P3 Cache
P2 reads X
S
S
S
BusRd
Memory

## Slide 32: Summary of the Two Coherence Protocols
Valid-Invalid: for write-through cache
State | Copies in caches | Copy in memory
--- | Single | Stale
V | Single | Up-to-date
--- | Multiple | Stale
V | Multiple | Up-to-date
I | Don’t know | Don’t know

## Slide 33: Summary of the Two Coherence Protocols
MSI: for invalidation-based write-back cache
State | Copies in caches | Copy in memory
M | Single | Stale
S | Single | Up-to-date
--- | Multiple | Stale
S | Multiple | Up-to-date
I | Don’t know | Don’t know

## Slide 34: Tradeoffs of MSI
Should a downgrade from M go to S or I?
  S: if data is likely to be reused (before it is written to by another processor)
  I: if data is not likely reused (before written to by another)
On a BusRd, should cache or memory supply data?
  Another cache: faster, if memory is slow or contended
  Memory: simpler, no need to see if cache has data first
    Less contention at the other caches
    Requires writeback on M downgrade
Is writeback to memory on ModifiedShared necessary?
  Discussed later in the MOESI protocol

## Slide 35: Problems with MSI
Problem 1: Read-modify-write on private data is common. But on a read, the block immediately goes to “Shared” state although it may be the only copy to be cached (i.e., no other processor will cache it)
  Suppose the cache wants to write it, it needs to broadcast “invalidate” even though it has the only cached copy!
  Could write to the block without notifying any other cache
Problem 2: Operations may not be atomic on bus
  e.g. detect miss, acquire bus, receive a response
  Creates possibility of deadlock and races
  Processor that sends invalidate should hold onto bus until other processors receive the invalidate

## Slide 36: Illustration of Problem 2
Atomic transaction bus:
  Simple, but low throughput!
Split-transaction and pipelined bus
  Supports multiple simultaneous transactions
  Higher throughput, but responses may be OOO
  Often implemented as multiple buses (req+resp)
  What happens to coherence?
(MIT 6.888 - Sanchez and Emer - L07)

## Slide 37: Solution to Problem 1: MESI
Idea: add another state indicating that this is the only cached copy and it is clean
  Exclusive state: write to copy without generating BusRdX
A block is placed into the exclusive state if, during BusRd, no other cache had it
  Wired-OR “shared” signal on bus can determine this: snooping caches assert the signal if they also have a copy
Transition Exclusive  Modified is possible on write
  MESI is also called the Illinois protocol
    Papamarcos, Patel, “A low-overhead coherence solution for multiprocessors with private cache memories,” ISCA 1984

## Slide 38: MESI: An Enhanced MSI Protocol
M
E
S
I
M: Modified Exclusive
E: Exclusive but unmodified
S: Shared
I: Invalid
Each cache block has a tag
Address tag
state
bits
Write miss
Other processor
intent to write
Read miss,
shared
Other processor
intent to write
P1 write
Read by any
processor
Other processor reads
P1 writes back
P1 read
P1 write
or read
Cache state in processor P1
P1 intent to write
Read miss, not shared
Other processor
reads
Other processor intent to write, P1 writes back

## Slide 39: Summary of MESI
MESI: for invalidation-based write-back cache
State | Copies in caches | Copy in memory
M | Single | Stale
E | Single | Up-to-date
--- | Multiple | Stale
S | Multiple | Up-to-date
I | Don’t know | Don’t know

## Slide 40: The Problem with MESI
Shared state requires the data to be clean
  i.e., all caches that have the block have the up-to-date copy and so does the memory
Problem: need to write the block to memory when BusRd happens when the block is in Modified state
Why is this a problem?
  Memory can be updated unnecessarily  some other processor may want to write to the block again while it is cached

## Slide 41: Improving on MESI
Idea 1: Do not transit from MS on a BusRd Invalidate the copy and supply the modified block to the requesting processor directly without updating memory
Idea 2: Transit from MS, but designate one cache as the owner (O), who will write the block back when it is evicted
  Now “Shared” means “Shared and potentially dirty”
  This is a version of the MOESI protocol

## Slide 42: MOESI Protocol
Add one additional state ─ Owner state
Similar to Shared state
The O state processor will be responsible for supplying data (copy in memory may be stale)
Employed by Sun UltraSparc, AMD Opteron
Core0
L2
Core1
L2
System Request Interface
Crossbar
Hyper-
Transport
Mem
Controller

## Slide 43: Summary of MOESI
MOESI: for invalidation-based write-back cache
State | Copies in caches | Copy in memory | 
M | Single | Stale | 
E | Single | Up-to-date | 
S/O | Multiple | Stale | One node is designated as O
S | Multiple | Up-to-date | 
I | Don’t know | Don’t know | 

## Slide 44: Summary of Snoopy Cache Coherence
Write through
Write back
Update
Invalidate
none
V
I
M
I
S
Correctness
Performance
M
S
I
E
M
S
I
E
O

## Slide 45: Summary
Symmetric multiprocessor (SMP):
  Shared single memory with uniform memory latency  centralized shared memory, uniform memory access
  Often use buses as interconnection
Snoopy protocol works well for ensuring cache coherence in bus-based SMP
  Bus-based, single point of serialization for all requests
  When any processor gets a miss, must probe every other cache and all processors observe other processors’ actions
Scaling up to more processors limited by:
  Communication bandwidth of and contention to bus
  Snoop bandwidth into tags

## Slide 46: Slides for Self-Study

## Slide 47: Implication on Multi-Level Caches
How to guarantee coherence in a multi-level cache hierarchy
  Snoop all cache levels?
Maintaining inclusion property
  Ensure data in the outer level present in the inner level
  Only snoop the outermost level (e.g., L2)
  L2 needs to know L1 has write hits
    Use write-through cache
    Use write-back but maintain a “modified-but-stale” bit in L2
Not so easy to ensure inclusion property
  Different bus observes different access activities, e.g., L2 may replace a block frequently accessed in L1
  Different cache block sizes

## Slide 48: Intervention
When a read-miss for A occurs in cache-2,
a read request for A is placed on the bus
  Cache-1 needs to supply and change its state to shared
  The memory may respond to the request also!
Does memory know it has stale data?
Cache-1 needs to intervene through memory controller to supply correct data to cache-2
cache-1
A 200
CPU-Memory bus
CPU-1
CPU-2
cache-2
memory (stale data)
A 100

## Slide 49: False Sharing
A cache block contains more than one word
But, cache coherence is done at the block level and not word level
Suppose M1 writes wordi and M2 writes wordk and both words have the same block address
  What can happen?
False sharing misses
  Read an unmodified word in an invalidated block
state block addr data0 data1 ... dataN
Notes: The block may be invalidated many times unnecessarily because
the addresses share a common block.

## Slide 50: Coherency Misses
True sharing misses arise from the communication of data through the cache coherence mechanism
  Invalidates due to 1st write to shared block
  Reads by another CPU of modified block in different cache
  Miss would still occur if block size were 1 word
False sharing misses when a block is invalidated because some word in the block, other than the one being read, is written into
  Invalidation does not cause a new value to be communicated, but only causes an extra cache miss
  Block is shared, but no word in block is actually shared  miss would not occur if block size were 1 word

## Slide 51: Example: True v. False Sharing v. Hit?
Time | P1 | P2 | True, False, Hit? Why?
1 | Write x1 |  | 
2 |  | Read x2 | 
3 | Write x1 |  | 
4 |  | Write x2 | 
5 | Read x2 |  | 
Assume x1 and x2 in same cache block
P1 and P2 both read x1 and x2 before
True miss; invalidate x1 in P2
False miss; x1 irrelevant to P2
False miss; x1 irrelevant to P2
True miss; x2 not writeable
True miss; invalidate x2 in P1

## Slide 52: Performance of SMPs
Cache performance is combination of:
Uniprocessor cache miss traffic
Traffic caused by communication
  Results in invalidations and subsequent cache misses
Coherence misses
  True sharing misses, false sharing misses
  Sometimes called a Communication miss
  4th C of cache misses along with Compulsory, Capacity, and Conflict