## Slide 1: CS5102 High Performance Computer Systems Distributed Shared Memory
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. O. Mutlu, Prof. Hsien-Hsin Lee, Prof. K. Asanovic,
http://compas.cs.stonybrook.edu/courses/cse502-s14/)

## Slide 2: Outline
Introduction
Centralized shared-memory architectures (Sec. 5.2)
Distributed shared-memory and directory-based coherence (Sec. 5.4)
Synchronization: the basics (Sec. 5.5)
Models of memory consistency (Sec. 5.6)

## Slide 3: Distributed Shared Memory (DSM)
Non-uniform memory access (NUMA) architecture
  Memory distributed among processors, logically shared
  All processors can directly access all memory
  Can use scalable point-to-point interconnection networks  no single point of coordination  simultaneous communications
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
R
R
R
R
R
R
R
R
PE
PE
PE
PE
R
R
R
R
R
R
R
R

## Slide 4: Can snoopy protocol work for cache coherence on DSM?
Write propagation and write serialization?
Broadcast

## Slide 5: Races in DSM
Consider a DSM with a mesh interconnection NW
  Different caches (PEs) will see different orders of writes
  Races due to network
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
NI
Mem
P
$
1
X
1
X
1
X
st X,0
st X,2

## Slide 6: Scalable Cache Coherence
We need a mechanism to serialize/order writes
Idea: instead of relying on interconnection network to provide serialization, ask a coordinate node  directory
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
1
X
1
X
1
X
X
Directory

## Slide 7: Scalable Cache Coherence
Directory:
  Single point of serialization, one entry for one block
    An entry tracks cached copies (sharer set) for each block
  Processors make requests for blocks through directory
  Directory coordinates invalidation appropriately and communicate only with processors that have copies
    e.g. P1 asks directory for exclusive copy, directory asks all sharers to invalidate, waits for ACKs, then responds to P1
  Communication with directory and copies is through network transactions but is independent of the network, as long as it provides point-to-point communications
  Directory can be centralized or distributed

## Slide 8: Directory-based Cache Coherence
Directory tracks who has what
Every memory block has an entry in the directory
  HW overhead for the directory (~ # blocks * # nodes)
Can work with UMA SMP, too!
P
$
P
$
P
$
P
$
Memory
Interconnection Network
(Centralized)
Directory
Modified bit
Presence bits, one for each node

## Slide 9: Directory-based Cache Coherence
P
$
P
$
P
$
P
$
Memory
Interconnection Network
P
$
1
1
1
0
0
0
0
0
0
0
0
0
0
1
0
1
C(k)
C(k+1)
0
0
0
1
0
1
0
0
C(k+j)
1 presence bit for each processor, each cache block in memory
1 modified bit for each cache block in memory
(Centralized)
Directory

## Slide 10: Distributed Directory Cache Coherence
Distributed directories track local memory to maintain cache coherence (CC-NUMA)
  Assumptions: reliable network, FIFO message delivery between any given source-destination pair

## Slide 11: Directory Coherence Protocol: Read Miss
Every memory block has a “home” node, where its directory entry resides
  Home node can be calculated from block address
$
Interconnection Network
0
0
1
1
Pn
$
Memory
Memory
P0
Read Z (missed)
Go to Home Node
Memory
Pn-1
Z
Z
1
Block Z is
shared (clean)
Home of Z
$
Z

## Slide 12: Directory Coherence Protocol: Read Miss
Block Z is dirty (“Modified” in Pn-1)
Interconnection Network
1
0
1
0
Memory
Memory
Read Z (missed)
Memory
Go to Home node
Z
0
1
1
Block Z is now clean, “Shared” by 3 nodes (MS)
$
$
$
Z
Z
Pn
P0
Pn-1
Ask Owner
Reply block
Reply to the request node
Notes: Design choice: who is responsible for sending the up-to-date copy to the requesting node?

## Slide 13: Directory Coherence Protocol: Write Miss
Interconnection Network
0
0
1
Memory
Memory
Write Z (missed)
Memory
1
Z
Go to Home Node
Invalid sharers
0
0
1
1
P0 can now write to block Z (IM)
$
$
$
Z
Z
Z
Pn
P0
Pn-1
X
X
Ack
Reply block
Notes: Design choice: who invalidate other caches, directory or requesting node?

## Slide 14: Directory: Basic Operations
Follow semantics of snoop-based system (MSI)
  but with explicit request and reply messages
Directory:
  Receives Read, ReadEx requests from nodes
  Sends Invalidate messages to sharers if needed
  Forwards request to memory if needed
  Replies to requestor and updates sharing state
Protocol design is flexible
  Exact forwarding paths depend on implementation, e.g. directory node or requesting node perform all bookkeeping operations?
  Must not have race conditions

## Slide 15: A Possible 4-hop Implementation
L has a cache read miss on a load instruction
H is the home node
R is the current owner of the block, who has the most up-to-date data for that block, which is in the Modified state
L
H
1: Read Req
4: Read Reply
R
State: M Owner: R
2: Recall Req
3: Recall Reply

## Slide 16: A Possible 3-hop Implementation
L has a cache read miss on a load instruction
H is the home node
R is the current owner of the block, who has the most up-to-date data for that block, which is in the Modified state
L
H
1: Read Req
3: Read Reply
R
State: M Owner: R
2: Fwd’d Read Req
3: Fwd’d Read Ack

## Slide 17: Example Cache States
For each block, a home directory maintains its state:
  Shared: one or more nodes have the block cached, value in memory is up-to-date
  Modified: exactly one node has a dirty copy of the cache block, value in memory is out-of-date
  May add transient states to indicate the block is waiting for previous coherence operations to complete
Caches in the nodes also need to track the state (e.g. MSI) of the cached blocks
Nodes send coherence messages to home directory
  Home directory only sends messages to nodes that care

## Slide 18: Operations in Directory (MSI)
For uncached block:
  Read miss: requesting node is sent the requested data and is made the only sharing node, block is now shared in directory and in requesting node
  Write miss: the requesting node is sent the requested data and becomes the owner node, block is now modified in directory and in requesting node

## Slide 19: Operations in Directory (MSI)
For shared block:
  Read miss: the requesting node is sent the requested data from memory, node is added to sharing set and block is shared in directory and in requesting node
  Write miss: the requesting node is sent the block, all nodes in the sharing set are sent invalidate messages, sharing set now only contains requesting node, block is now modified in directory and in requesting node

## Slide 20: Operations in Directory
For modified block:
  Read miss: the owner is sent a data request message, block becomes shared, owner replies the block to the directory, block written back to memory, sharers set now contains old owner and requestor, block is shared in directory and in requesting node
  Write miss: the owner is sent an invalidation message, requestor becomes new owner, block remains modified in directory and in requesting node
  Data write back: the owner replaces and writes back the block, block becomes uncached, sharer set is empty

## Slide 21: Read Miss to Uncached or Shared Block
Directory Controller
DRAM Bank
CPU
Cache
1
Load request at head of CPU->Cache queue.
2
Load misses in cache.
3
Send ReadReq message to directory.
4
Message received at directory controller.
5
Access state and directory for block. Block’s state is S, with 0 or more sharers
6
Update directory by setting bit for new processor sharer.
7
Send ReadReply message with contents of cache block.
8
ReadReply arrives at cache.
9
Update cache tag and data and return load data to CPU.
Interconnection Network
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 22: Write Miss to Read Shared Block
Directory Controller
DRAM Bank
CPU
Cache
1
Store request at head of CPU->Cache queue.
2
Store misses in cache.
3
Send ReadReqX message to directory.
4
ReadReqX message received at directory controller.
5
Access state and directory for block. Block’s state is S, with some set of sharers
6
Send one InvReq message to each sharer.
11
ExRep arrives at cache
12
Update cache tag and data, then store data from CPU
Interconnection Network
CPU
Cache
7
InvReq arrives at cache.
8
Invalidate cache block. Send InvRep to directory.
9
InvRep received. Clear down sharer bit.
10
When no more sharers, send ExRep to cache.
Multiple sharers
CPU
Cache
CPU
Cache
Notes: Delay is a fact of life
Serialization by directory, no longer the bus
SC not guarantied

## Slide 23: Directory: Data Structures
Key operation to support is set inclusion test
  False positives are OK: want to know which caches may contain a copy of a block, and spurious invalidations are ignored
  False positive rate determines performance
Most accurate (and expensive): full bit-vector
Compressed representation, linked list, Bloom filters are all possible
Directory
Modified bit
Presence bits, one for each node

## Slide 24: Issues with Contention Resolution
May have concurrent transactions to cache blocks
  Can have multiple requests in flight to same cache block!
Need to escape race conditions by:
  NACKing requests to busy (pending invalidate) entries
    Original requestor retries
  OR, queuing requests and granting in sequence
  (Or some combination thereof)
Fairness
  Which requestor should be preferred in a conflict?
  Interconnect network delivery order, and distance, both matter

## Slide 25: An Example Race: Writeback and Read
L has dirty copy, wants to write back to H
R concurrently sends a read to H
H
1: WB Req
5: Read Reply
R
State: M Owner: L
3: Fwd’d Read Req
4:
Race! WB and Fwd Rd
No need to ack
6:
Race!
Final State: S
No need to Ack
  Races require complex intermediate states
L
2: Read Req

## Slide 26: Hybrid Snoopy and Directory
Stanford DASH (4 CPUs per cluster, total 16 clusters)
  Invalidation-based cache coherence
  Keep one of 3 states of a cache block at its home directory
    Uncached, shared (unmodified state), dirty
P
$
Memory
P
$
Memory
Directory
Interconnection Network
Snoop bus
P
$
Memory
P
$
Memory
Directory
Snoop bus

## Slide 27: Snoopy vs. Directory Coherence
Snoopy
  + Miss latency (critical path) is short
  + Global serialization is easy: bus arbitration
  + Simple: adapt bus-based uniprocessors easily
  - Relies on broadcast seen by all caches (in same order):
   single point of serialization (bus): not scalable
Directory
  - Adds miss latency: request  dir.  mem.
  - Requires extra storage space to track sharer sets
  - Protocols and race conditions are more complex
  + Does not require broadcast to all caches
  + Exactly as scalable as interconnect and directory storage
Notes: Make reference to SGI Origin paper