## Slide 1: CS5102 High Performance Computer Systems Synchronization
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. O. Mutlu, Prof. Hsien-Hsin Lee, Prof. K. Asanovic,
http://compas.cs.stonybrook.edu/courses/cse502-s14/)

## Slide 2: Outline
Introduction
Centralized shared-memory architectures (Sec. 5.2)
Distributed shared-memory and directory-based coherence (Sec. 5.4)
Synchronization: the basics (Sec. 5.5)
Models of memory consistency (Sec. 5.6)

## Slide 3: Introduction
Coherence protocols guarantee that a reading processor sees most current update to shared data
  Make caches in SMPs as invisible as in single-core systems
  Typically deal with one cache block at a time
However, coherence protocols do not:
  Specify on the interaction of accesses to multiple blocks
  Ensure that processors access shared data in certain order
  Ensure that at most k processors access a shared HW (I/O device) or SW (linked list) resource at a time
  Force processors to start executing particular sections of code together
Operations of processors need to be synchronized

## Slide 4: Why Synchronization?
Need to know when it is safe for different threads/processes/processors to use shared data
  Producer-consumer: a consumer must wait until the producer has produced data (access ordering)
  Mutual exclusion: only one processor uses a hardware or software resource (specified as memory) at a given time
  Barrier: all processors start executing together
producer
consumer
Shared Resource
P1
P2

## Slide 5: Access Ordering
Pass data between threads/processes/processors
Use semaphores: P(S) and V(S)
What happen if data and mutex can be cached in private caches of the processors?
...
data = 1; P(mutex);
...
...
V(mutex);
if (data==1)
...
Processor 1
Processor 2

## Slide 6: Synchronize among Many Processors
Synchronize operations (e.g. computation phases) among many threads/processes/processors
Use barrier: barrier()
...
data[1] = a;
barrier(B1);
sum += data[1];
...
...
data[2] = b;
barrier(B1);
sum += data[2];
...
Processor 1
Processor 2

## Slide 7: Mutual Exclusion
At most k=1 threads/processes/processors can access shared resources at a time
Use locks or semaphores: lock()/unlock() or P()/V()
...
P(mutex);
sum = sum + a;
V(mutex);
...
...
P(mutex);
sum = sum + b;
V(mutex);
...
Processor 1
Processor 2
Critical Section (CS)

## Slide 8: Critical Sections
A sequence of code that only one thread/processor can execute at a time
  Provides mutual exclusion
    A thread/processor has exclusive access to the code and thus the data that the code accesses  indirect protection
    Guarantees that only one thread/processor can update shared data at a time
  To execute a critical section, a thread/processor
    Acquires a lock/semaphore that guards it
    Executes its code to operate on the protected data
    Releases the lock/semaphore
The effect is to synchronize/order the access of the threads/processors to the shared data

## Slide 9: Synchronization at Different Layers
Disable Interrupts Test&Set Comp&Swap
Locks Semaphores Monitors
Shared Programs
Hardware
Library/API
Programs

## Slide 10: Synchronization Hardware
Many systems provide hardware support for critical section code
Uniprocessors: could disable interrupts
  Currently running code would execute without pre-emptive context switches due to interrupts
  System’s clock still needs to be updated by interrupts
Consequently, a naive implementation of locks:
LockAcquire { disable Ints; }
LockRelease { enable Ints; }
Problem with this approach:
  CS cannot be too long, otherwise system cannot respond to interrupts

## Slide 11: Synchronization Hardware
Special atomic machine instructions
  Atomic = non-interruptable (why atomic?)
  Atomic instructions allow either to test and modify the content of a word or to swap the contents of two words
Basic building blocks:
  Atomic exchange: swaps register with memory location
  Test-and-set: sets memory location under condition
  Fetch-and-increment: reads original value from memory and increments it in memory
  Load linked/store conditional: if content of memory location specified by load linked are changed before store conditional to the same address, the store conditional fails

## Slide 12: Atomic Exchange
Swap a value in a register and a value in memory in one atomic operation
  Set the register to 1
  Swap the register value and the lock value in memory  one load and one store in one atomic operation
  New register value determines whether got the lock
  Spin lock with atomic exchange:
DADDUI R2,R0,#1 ;R2  1
lockit: EXCH R2,0(R1) ;atomic exchange
BNEZ R2,lockit ;already locked?
  Also call atomic read-modify-write a location in memory
What happen if the lock value 0(R1) can be cached?

## Slide 13: Caching Lock Value
If read-modify-write is not atomic and the lock value can be cached  race condition
How to make read-modify-write atomic?
P0
Cache
Memory
P1
Lock=0
R2=1
Cache
P3
Cache
R2=1
EXCH R2,Lock
Lock=0
Lock=0
EXCH R2,Lock
0
1
0
1

## Slide 14: Implement Atomic Exchange by Spin Lock
Option 1: keep the lock variable (O(R1)) in memory and non-cacheable
  How to guarantee atomic for exchange (load-and-store)?
  Very heavy bus traffic for exchange
Option 2: allow the lock variable to be cached
  Does it really help the bus traffic?
  Every exchange will attempt a write
  Many invalidates and lock value keeps changing ownership  heavy bus traffic again
Want to spin on cached copy and at the same time avoid bus transaction
  Likely to get cache hits when spin

## Slide 15: Implement Atomic Exchange by Spin Lock
Option 3:
  Processors spin on local copy of lock variable
  When the lock value is changed (unlocked) by the lock owner, then try atomic exchange (e.g. holding onto the bus until exchange is done) to compete for the lock
lockit: LD R2,0(R1) ;load lock
BNEZ R2,lockit ;not avail.-spin
DADDUI R2,R0,#1 ;R2  1
EXCH R2,0(R1) ;swap
BNEZ R2,lockit ;spin if not 0

## Slide 16: Coherence Traffic for Atomic Exchange
Each processor keeps reading the lock value
  This read will be from the local cached copy and does not generate coherence traffic. Every processor thus spins on its locally cached copy
When lock owner releases the lock by writing a 0
  This write invalidates all other cached copies through cache coherence mechanism
  Each spinning processor now has a read miss, acquires a new copy, sees the 0, attempts an atomic exchange
  First processor to acquire the block in Modified state acquires the lock; others jump to spin again (what are the states of the cached copies?)

## Slide 17: Race for Atomic Exchange
Step P0 $ P1 $ P2 $ Bus/Directory activity
1. Has lock ?? spins Sh spins Sh None
2. lock 0 Mod Inv Inv P0 Invalidates lock
3. lock = 0 Mod miss Inv miss Sh P2 gets bus; P0 WB
4. lock = 0 Sh waits Inv lock = 0 Sh P2 cache filled; P1 gets bus
5. lock = 0 Sh lock = 0 Sh exch Sh P1 cache filled
6. Inv exch Inv R2 = 0 Mod P2 invalidates lock
lock  1
7. Inv R2 = 1 Mod enters CS Inv P1 invalidates lock; P2 WB
lock = 1 with lock = 1
8. Inv spins Mod Inv None
Notes: Bus transactions due to exch can be interleaved!

## Slide 18: Load-Linked and Store-Conditional
Problem with atomic read-modify-write:
  Two memory operations in one
Alternative: make pair of instructions appears atomic
  Avoid need for uninterruptible memory read and write
Load-locked (LL) and store-conditional (SC)
  LL R1,x: loads the value at memory address x into register R1, and saves the address x into a link register
  SC x,R1,R2: stores R1 into address x only if it is the first store after the local LL R1,x (and there is no bus traffic in between for cache coherent cache)  “effectively” atomic
    The success is reported by returning a value (e.g. R2=1); otherwise the store fails and R2=0 is returned
Notes: If LL and SC are for memory accesses without caching  SC successes if no other store since last local LL
If LL and SC are for caching  SC successes if no bus traffic since last local LL

## Slide 19: Load-Linked and Store-Conditional
An illustrative example:
  do {
  int x = LL(p);
  int y = x + 1;
  } while (!SC(p,y));
Corresponding code:
  lockit: LL R1,p
  Add R1,1
  SC p,R1,R2
  BNZ R2,lockit
(Prof. Andrew Lenharth, UT Austin)
Notes: Consider LL and SC with caching  must no have bus traffic in between

## Slide 20: Load-Linked and Store-Conditional
Example: lock and unlock with LL & SC
lockit: LL R2,0(R1) ;load linked BNEZ R2,lockit ;not free=>spin DADDUI R2,R0,#1 ;locked value SC 0(R1),R2,R3 ;store BEQZ R3,lockit ;branch if fails
Critical Section
ST 0(R1),#0
Example: fetch and increment with LL & SC:
try: LL R2,0(R1) ; load linked DADDUI R2,R2,#1 ; increment SC 0(R1),R2,R3 ; store BEQZ R3,try ; branch SC fails

## Slide 21: Summary
Need synchronization for access ordering (producer-consumer), mutual exclusion, barrier
Hardware supports for synchronization
  Disabling interrupts
  Atomic exchange instruction with spin lock
    How to spin on cached lock?
  Load linked/store conditional instructions