## Slide 1: DAC-Aware AIG Re-writing (ABC Tool)

## Slide 2: And-Inverter Graph
And-Inverter Graph (AIG)
  Simple structure
  And-Gates as nodes (shown as circles) with two inputs as edges (shown as arrows)
  Inverter edges marked with a dot
  Used in ABC

## Slide 3: AIG Structure
A directed graph where
node = and gate
edge = wire
circle on edge = inverter
a
c
d
F = (a c ) d’

## Slide 4: Example
Ex: y = f( x1,x2,x3) =( (x1 ‧ x2 )’ ‧ (x2 ‧ x3)’)’
= ( x1 ‧ x2 ) ＋ (x2 ‧ x3)

## Slide 5: To Derive a Baseline AIG
  Find SOPs and then factored forms of nodes in a logic network
  Convert AND and OR gates of factored form into 2-input ANDs and inverter using DeMorgan’s rule
  Apply structural hashing during AIG construction to ensure that no two AND gates have identical pairs of incoming edges

## Slide 6: Different AIG Structures for the Same Function
F = a b c

## Slide 7: A Simple Example of AIG Rewriting
A rule based transformation

## Slide 8: How to Re-Write?

## Slide 9: A Cut
  A cut of C of node N is a set of nodes of the network, called leaves, such that each path from PIs to N passes at least one leaf
  A trivial cut of the nodes is the node itself
  A cut is K-feasible if the number of leaves does not exceed K

## Slide 10: An Example of 4-feasible Cut
a
c
a
d
b
c
a 4-feasible cut
not a cut
Find subfunctions rooted at F
F

## Slide 11: Re-Writing Algorithm
Step 1: Pre-compute all AIG implementations of 4-input functions and store them in a table
  216 4-input functions
  222 equivalence classes (NPN)
  40 found experimentally to lead to improvement
  4-input function stored using 16-bit string (signature)
  AIG subgraphs stored in shared DAC with about 2000 nodes

## Slide 12
Step 2:
- For a node, find its 4-feasible cuts
- For each cut, find its NPN equivalence
- compute the cost of a subgraph
- choose the subgraph that leads to
the largest improvement
  Nodes are processed in topological order
  Logic sharing is checked between the new subgraph and nodes already in the network using reference counters
  The old subgraph is dereferenced and the new subgraph is added

## Slide 13: Delay-aware Re-writing
A subgraph representation will not be accepted if the final logic level is increased
  Using slack of the node
  No negative slack after replacement

## Slide 14: AIG Refactoring
Produce deeper permutations of the logic structures
  Work for larger cuts, K, for 10 <= K <= 20
  The function is converted to SOP, factored, AIGs built using baseline AIG rewriting

## Slide 15: AIG Balancing
For delay optimization
  A(BC) = (AB)C = (AC)B is applied to maximally reduce the number of levels of AIG
  One linear time sweep over the network in a topological order

## Slide 16: Zero-cost Replacement Enabled
Create new re-writing opportunity
  If the option is enabled, the node is replaced by a new subgraph if the cost = 0
  Enabled later in the script

## Slide 17: An Example of Script in ABC
A re-writing script, resyn2, in abc.rc
b (balance) ;
rw (rewrite);
rf (refactor);
b;
rw;
rwz (re-write with 0 cost);
b ;
rfz (refactor with 0 cost);
rwz;
b
Perform 10 times over the network