## Slide 1
計 算 機 結 構
國立清華大學資訊工程系 黃婷婷教授

## Slide 2
為什麼電腦不用十進位而用二進位？

## Slide 3: Signal: Two States (二進制)
對、錯
正、反
陰、陽
勝、負
真、偽
high、low
本土化、非本土化

## Slide 4: Switch (電子開關)
“gate” as the switch

## Slide 5: A Working Transistor (1/5)
Transistors consist of three terminals; the source, the gate, and the drain:

## Slide 6: A Working Transistor (2/5)
In the n-type transistor, both the source and
the drain are negatively-charged and
sit on a positively-charged well of p-silicon.

## Slide 7: A Working Transistor (3/5)
When positive voltage is applied to the gate, electrons in the p-silicon are attracted to the area under the gate forming an electron channel between the source and the drain.

## Slide 8: A Working Transistor (4/5)
When positive voltage is applied to the drain,
the electrons are pulled from the source to the drain.
In this state the transistor is on.
開

## Slide 9: A Working Transistor (5/5)
If the voltage at the gate is removed, electrons are not attracted to the area between the source and drain. The pathway is broken and the transistor is turned off.
關

## Slide 10: 相關電壓電流特性 及電路分析等知識 我們是在＿＿＿課中介紹的
答：「電子電路學」「超大型積體電路設計」

## Slide 11: 有了開關就可以做邏輯閘
CMOS NAND:

## Slide 12: Switch (電子開關)
“gate” as the switch

## Slide 13: 有了邏輯閘就可做邏輯電路
A
B
Cl
S
A
A
B
B
Cl
CO
加法器：

## Slide 14: 也可以做記憶元件
R'
clock'
S'
R
S
Q'
Q
可存一個bit的東西：

## Slide 15: 這部份的學問叫＿＿＿＿
答：「數位邏輯設計」

## Slide 16: 最後，電腦的主要部份就都可以做了
Z
N
暫存器
記憶體
PC
IR
控制器
ALU
clock
控制信號

## Slide 17: Basic Organization of Any Computer
Processor
(active)
Computer
Control
(“brain”)
Datapath
(“brawn”)
Memory
(passive)
(where
programs,
data
live when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk (where
programs,
data
live when
not running)
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 18: Computer Organization
Capabilities and performance characteristics of principal functional units, e.g., registers, ALU, shifters, ...
Ways in which these components are interconnected (structure)
Information flows between components (data, datapath)
Logic and means by which such information flow is controlled (control logic)
Register Transfer Level (RTL) description
Notes: Deeper view. Design state of art organization in 1990. This is only the computer organization. What is computer architecture ?

## Slide 19: What is Computer Architecture?
Computer Architecture = Instruction Set Architecture + Machine Organization
I/O system
Processor
Compiler
Operating
System
(MS Windows)
Application (IE)
Digital Design
Circuit Design
Datapath & Control
Transistors
Memory
Hardware
Software
Assembler
Instruction Set
Architecture
Machine Organization

## Slide 20: Instruction Set as a Critical Interface
instruction set
software
hardware
Does it have to be hardware?
Coordination of many levels of abstraction

## Slide 21: Another Perspective
High Level Language Program
Assembly Language Program
Machine Language Program
Control Signal Specification
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
°
°
ALUOP[0:3] <= InstReg[9:11] & MASK
ISA

## Slide 22: Instruction Set Architecture (ISA)
“... the attributes of a [computing] system as seen by the programmer, i.e. the conceptual structure and functional behavior, as distinct from the organization of the data flows and controls, the logic design, and the physical implementation.” — Amdahl, Blaaw, and Brooks, 1964
Organization of Programmable Storage
Data Types and Data Structures: Encodings and Representations
Instruction Set
Instruction Formats
Modes of Addressing and Accessing Data Items and Instructions
Exceptional Conditions
SOFTWARE

## Slide 23: MIPS R3000 ISA
Instruction categories:
  Load/Store
  Computational
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
Registers

## Slide 24: Example ISA
Digital Alpha (v1, v3) 1992-97
HP PA-RISC (v1.1, v2.0) 1986-96
Sun Sparc (v8, v9) 1987-95
SGI MIPS (MIPS I, II, III, IV, V) 1986-96
Intel (8086,80286,80386, 1978- 80486,Pentium, MMX, SIMD, IA-64, ...)
ARM (v1,v2…v8) 1985-
RISC-V

## Slide 25: Why Do Computer Architecture?
RAPID CHANGES
It is exciting!
It has never been more exciting!
It impacts every other aspect of electrical engineering and computer science

## Slide 26
Flipped Classroom

## Slide 27: Group Performance
Forming study groups (14 groups) by TA. Each group has 7-8 students.
  For members in the same group, their group performance will be the same
  Advanced learner will help less advanced learner!

## Slide 28: Flipped Classroom
Before class:
  Watch video and learn it by yourself (or group study)
  Submit two question-and-answers to eeclass by each group before noon every Friday
In class:
  First part:
  Question and answer (for general question)
  Second part:
  Group study or individual student tutored by TAs and teacher
  A set of questions discussed in each group
  Third part:
  Tournament
  Submission of final answer sheet per group

## Slide 29: Flipped Classroom
After class
  Review the course and take a quiz online after each class
  Complete three homework assignments
  Take midterm and final exams
  Submit one final project

## Slide 30: In Class – Second & Third Parts
  Group Discussion:
    TA will select several questions from the questions uploaded by each group and give a question sheet on Sunday
    Group discussion
  Tournament:
    TA selects some questions from question sheet (Q-group)
    TA randomly select one member of groups whose question is not selected to answer the question (A-group)
    If A-group can not answer the question, a member randomly selected from Q-group has to give the answer
    The question is answered on the blackboard
    Points are given to these two groups based on their performance
  Submission:
    Your group answer-sheet at the end of class

## Slide 31: In Class – Second & Third Parts
Second and third parts:
  TA is the moderator
  Each group prepares two question-and-answers and upload the questions to https://eeclass.nthu.edu.tw by Friday noon.
  Moderator checks all questions and may ask some groups to reload questions if there is too much duplication among groups.
  Good question is important. If it is selected by TA in tournament, it is worth points!

## Slide 32: After Class – Quiz
    Quiz contains a set of single or multiple-choice questions
    Quiz is uploaded before 20:00 every Monday after class
    Questions are all from the question sheet !!
    Complete the quiz before Thursday noon each week
    Grading: Total number of correct answers/total number of answers x 7%

## Slide 33: Group Performance
Group performance (in each class period)
  First part: Student participation and interaction with teacher (teacher asks question or students raise question)
  Second and third parts:
    Group discussion : prepare your answers
    Tournament – points are given to the two groups (Q-group and A-group)
    Submission of answer sheet

## Slide 34: Course Administration
授課老師: 黃婷婷
  辦公室: 資電442 電話: 31310 email: tingting@cs.nthu.edu.tw
助教:
鄭翔駿 jimmy980189@gmail.com Online office hours: 星期二19:00~21:00
姜柏丞 qwezxcasd6306@gmail.com Online office hours: 星期三19:00~21:00
林承賢 s110062801@m110.nthu.edu.tw Online office hours: 星期四19:00~21:00
許子麗 a0920203860@gmail.com Online office hours: 星期五19:00~21:00
上課時間:
  CS4100-00: 星期一 13:20-16:00
上課地點: DELTA 台達 109
課程網頁: http://www.cs.nthu.edu.tw/~tingting/cs4100.html

## Slide 35: Text Book
Computer Organization and Design: The Hardware/Software Interface, 5th ed. David Patterson and John Hennessy, 2013
史丹福大學
校長
RISC, RAID

## Slide 36: Topics Covered
Computer Organization and Design: The Hardware/Software Interface, D. Patterson and J. Hennessy
Topic
--------------------------------------------
Introduction
The Role of Performance
Instructions: Language of the Machine
Arithmetic for Computers
The Processor: Datapath and Control
Enhancing Performance with Pipelining
Exploiting Memory Hierarchy

## Slide 37: Prerequisite
Prerequisite courses:
  Logic design

## Slide 38: Expected Course Workload
Learn MIPS instruction set
Learn processor emulators and benchmarking
1 final project
One mid-term and one final examination
Grade breakdown
  In-class performance 23%
  Quizzes 7%
  Assignments & Final project 10%
  Midterm Exam (Nov 6) 30%
  Final Exam (Jan 8) 30%

## Slide 39: Resource on Internet to Help Your Learning
Course Website
  http://www.cs.nthu.edu.tw/~tingting/cs4100.html
ShareCourse (Please register)
  https://www.sharecourse.net/sharecourse/course/view/courseInfo/2731
FB粉絲專頁 (TA online office)
  https://www.facebook.com/NTHUArch
Open Course Ware (OCW)
  http://ocw.nthu.edu.tw/ocw/index.php?page=course&cid=76&

## Slide 40: Course Problems
Cannot attend the class
  One absence is allowed but no point of group performance will be given for that class
  Two absents => you don’t have to come any more
Cannot be in the class on time
  Late = absent
Cannot turn in homework on time
  No late homework is accepted
What is cheating?
  Study together in group is encouraged
  Work must be your own. Copying is cheating!