## Slide 1: Memory Hierarchy
國立清華大學資訊工程學系
黃婷婷教授

## Slide 2: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 3: Memory Technology
Random access:
  Access time same for all locations
  SRAM: Static Random Access Memory
    Low density, high power, expensive, fast
    Static: content will last (forever until lose power)
    Address not divided
    Use for caches
  DRAM: Dynamic Random Access Memory
    High density, low power, cheap, slow
    Dynamic: need to be refreshed regularly
    Addresses in 2 halves (memory as a 2D matrix):
      RAS/CAS (Row/Column Access Strobe)
    Use for main memory
Magnetic disk
Notes: The technology we used to build our memory hierarchy can be divided into two categories: Random Access and Non-so-Random Access.
Unlike all other aspects of life where the word random usually associates with bad things, random, when associates with memory access, for the lack of a better word, is good!
Because random access means you can access any random location at any time and the access time will be the same as any other random locations.
Which is NOT the case for disks or tape where the access time for a given location at any time can be quite different from some other random locations at some other random time.
As far as Random Access technology is concerned, we will concentrate on two specific technologies: Dynamic RAM and Static RAM.
The advantages of Dynamic RAMs are high density, low cost, and low power so we can have a lot of them without burning a hole in our budget or our desktop.
The disadvantages of DRAM are they are slow. Also they will forget what you tell them if you don remind them constantly (Refresh). We will talk more about refresh later today.
SRAM only has one redeeming feature: it is fast. Other than that, they have low density, expensive, and burn a lot of power. Oh, SRAM actually has another redeeming feature. They will not forget what you tell them. They will keep whatever you write to them forever.
Well orever?is a long time. So lets just say it will keep your data as long as you don pull the plug on your computer.
In the next two lectures, we will be focusing on DRAMs and SRAMs.
We will not get into disk until the Virtual Memory lecture a week from now.
+3 = 19 min. (X:59)

## Slide 4: Comparisons of Various Technologies
Memory
technology
$ per GB
in 2008
SRAM
$2000 – $5,000
DRAM
Magnetic
disk
$0.20 – $2
Typical access
time
0.5 – 2.5 ns
50 – 70 ns
5,000,000 –
20,000,000 ns
$20 – $75
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk
Notes: From the truth table we had before the break, we can derive the logic equation for ALUctr bit 2 but collecting all the rows that has ALUCtr bit 2 equals to 1 and this table is the result.
Each row becomes a product term and we need to OR the prodcut terms together.
Notice that the last row are identical except the bit<3> of the func fields. One is zero and the other is one. Together, they make bit<3> a don care term.
With all these don care terms, the logic equation is rather simple.
The first prodcut term is: not ALUOp<2> and ALUOp<0>.
The second product term, after we making Func<3> a don care becomes ...
+2 = 57 min. (Y:37)

## Slide 5: Solution: Memory Hierarchy
Control
Datapath
Memory
Processor
Memory
Memory
Memory
Memory
Fastest
Slowest
Smallest
Biggest
Highest
Lowest
Speed:
Size:
Cost:
An Illusion of a large, fast, cheap memory
  Fact: Large memories slow, fast memories small
  How to achieve: hierarchy, parallelism
An expanded view of memory system:

## Slide 6: Memory Hierarchy: Principle
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Block X
Block Y
At any given time, data is copied between only two adjacent levels:
  Upper level: the one closer to the processor
    Smaller, faster, uses more expensive technology
  Lower level: the one away from the processor
    Bigger, slower, uses less expensive technology
Block: basic unit of information transfer
  Minimum unit of information that can either be present or not present in a level of the hierarchy

## Slide 7: Why Hierarchy Works?
Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time
  90/10 rule: 10% of code executed 90% of time
Two types of locality:
  Temporal locality: if an item is referenced, it will tend to be referenced again soon, e.g., loop
  Spatial locality: if an item is referenced, items whose addresses are close by tend to be referenced soon., e.g., instruction access, array data structure
Probability
of reference
address space
0
2n - 1
Notes: The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
This is kind of like in real life, we all have a lot of friends. But at any given time most of us can only keep in touch with a small group of them.
There are two different types of locality: Temporal and Spatial. Temporal locality is the locality in time which says if an item is referenced, it will tend to be referenced again soon.
This is like saying if you just talk to one of your friends, it is likely that you will talk to him or her again soon.
This makes sense. For example, if you just have lunch with a friend, you may say, let go to the ball game this Sunday. So you will talk to him again soon.
Spatial locality is the locality in space. It says if an item is referenced, items whose addresses are close by tend to be referenced soon.
Once again, using our analogy. We can usually divide our friends into groups. Like friends from high school, friends from work, friends from home.
Let say you just talk to one of your friends from high school and she may say something like: o did you hear so and so just won the lottery.
You probably will say NO, I better give him a call and find out more.
So this is an example of spatial locality. You just talked to a friend from your high school days. As a result, you end up talking to another high school friend. Or at least in this case, you hope he still remember you are his friend.
+3 = 10 min. (X:50)
Temporal locality: loop
Spatial locality: instruction executed sequentially, access of array element.

## Slide 8
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Transfer Unit
prog./compiler
cache controller
OS
user/operator
Upper Level
Lower Level
faster
Larger

## Slide 9: How Is the Hierarchy Managed?
Registers <-> Memory
  by compiler (programmer?)
cache <-> memory
  by the hardware
memory <-> disks
  by the hardware and operating system (virtual memory)
  by the programmer (files)

## Slide 10: Memory Hierarchy: Terminology
Lower Level
Memory
Upper Level
Memory
To Processor
From Processor
Block X
Block Y
Hit: data appears in upper level (Block X)
  Hit rate: fraction of memory access found in the upper level
  Hit time: time to access the upper level
    RAM access time + Time to determine hit/miss
Miss: data needs to be retrieved from a block in the lower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty: time to replace a block in the upper level + time to deliver the block to the processor (latency + transmit time)
Hit Time << Miss Penalty
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the Upper level. Then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.
+2 = 14 min. (X:54)

## Slide 11: 4 Questions for Hierarchy Design
Q1: Where can a block be placed in the upper level? => block placement
Q2: How is a block found if it is in the upper level? => block finding
Q3: Which block should be replaced on a miss? => block replacement
Q4: What happens on a write? => write strategy

## Slide 12: Summary of Memory Hierarchy
Two different types of locality:
  Temporal Locality (Locality in Time)
  Spatial Locality (Locality in Space)
Using the principle of locality:
  Present the user with as much memory as is available in the cheapest technology.
  Provide access at the speed offered by the fastest technology.
DRAM is slow but cheap and dense:
  Good for presenting users with a BIG memory system
SRAM is fast but expensive, not very dense:
  Good choice for providing users FAST accesses
Notes: Let summarize today lecture. The first thing we covered is the principle of locality.
There are two types of locality: temporal, or locality of time and spatial, locality of space.
We talked about memory system design.
The key idea of memory system design is to present the user with as much memory as possible in the cheapest technology while by taking advantage of the principle of locality, create an illusion that the average access time is close to that of the fastest technology.
As far as Random Access technology is concerned, we concentrate on 2: DRAM and SRAM.
DRAM is slow but cheap and dense so is a good choice for presenting the use with a BIG memory system.
SRAM, on the other hand, is fast but it is also expensive both in terms of cost and power, so it is a good choice for providing the user with a fast access time.
I have already showed you how DRAMs are used to construct the main memory for the SPARCstation 20.
On Friday, we will talk about caches.
+2 = 78 min. (Y:58)

## Slide 13: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 14: Processor Memory Latency Gap
Proc
60%/yr.
(2X/1.5 yr)
DRAM
9%/yr.
(2X/10 yrs)
1
10
100
1000
1980
1981
1983
1984
1985
1986
1987
1988
1989
1990
1991
1992
1993
1994
1995
1996
1997
1998
1999
2000
1982
Processor-memory
performance gap: (grows 50% / year)
Performance
Year
Moore’s Law
Notes: Y-axis is performance
X-axis is time
Latency
Clich?
Not e that x86 didn have cache on chip until 1989

## Slide 15: Levels of Memory Hierarchy
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Transfer Unit
prog./compiler
cache controller
OS
user/operator
Upper Level
Lower Level
faster
Larger

## Slide 16: Inside the Processor
Computer Abstractions and Technology-15
AMD Barcelona: 4 processor cores

## Slide 17: Basics of Cache
Our first example: direct-mapped cache
Block Placement :
  For each item of data at the lower level, there is exactly one location in cache where it might be
  Address mapping: modulo number of blocks
M
e
m
o
r
y
0
0
0
0
1
0
0
1
0
1
0
1
0
0
1
0
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
0
0
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1

## Slide 18: Tags and Valid Bits: Block Finding
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 19: Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 20: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 21: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 22: Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 23: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 24: Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11->10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 25: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 26: Memory Address
100000
101000
100100
100001
100010
100011
100101
100111
100110

## Slide 27
Cache:
1K words, 1-word block:
  Cache index: lower 10 bits
  Cache tag: upper 20 bits
  Valid bit (When start up, valid is 0)
Address Subdivision

## Slide 28: Example: Larger Block Size
64 blocks, 16 bytes/block
  To what block number does address 1200 map?
Block address (memory) = 1200/16 = 75
Block number (cache index) = 75 modulo 64 = 11
1200=00…00100101100002 /100002 =>00…0010010112
10010112 =>0010112
Tag
Index
Offset
0
3
4
9
10
31
4 bits
6 bits
22 bits

## Slide 29: Example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
28

## Slide 30: Example: Intrinsity FastMATH
29
  Cache: 16KB
  256( )blocks ×
  16 ( ) words/block

## Slide 31: Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
Larger miss penalty
  Larger blocks  pollution
  Can override benefit of reduced miss rate
  Early restart and critical-word-first can help
Notes: Eearly restart: to resume the execution as soon as the requested word of block is returned rather than wait for the entire block. Work good for instruction.
critical word first: the requested word is transferred first. Then the remaining transfer start from the word next to the requested word and wrapping around to the beginning.

## Slide 32: Block Size on Performance
Increase block size tends to decrease miss rate
Notes: Each line represents a cache of different size.

## Slide 33: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 34: Cache Hit and Miss
Cache read
  Read hit
  Read miss
Cache write
  Write hit
    Write-through
    Write-back
  Write miss

## Slide 35: Read Cache
Read Hit:
On cache hit, CPU proceeds normally
Read Miss:
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 36: Write Hit: Write-Through
There are two copies of data: one in cache and one in memory.
Write Hit:
Write through: also update memory
Increase the traffic to memory
Also makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 37: Avoid Waiting for Memory in Write Through
Use a write buffer (WB):
  Processor: writes data into cache and WB
  Memory controller: write WB data to memory
Write buffer is just a FIFO:
  Typical number of entries: 4
Memory system designer’s nightmare:
  Store frequency > 1 / DRAM write cycle
  Write buffer saturation => CPU stalled
Processor
Cache
Write Buffer
DRAM
Notes: You are right, memory is too slow. We really didn't writ e to the memory directly. We are writing to a write buffer.
Once the data is written into the write buffer and assuming a cache hit, the CPU is done with the write. The memory controller will then move the write buffer contents to the real memory behind the scene.
The write buffer works as long as the frequency of store is not too high. Notice here, I am referring to the frequency with respect to time, not with respect to number of instructions.
Remember the DRAM cycle time we talked about last time. It sets the upper limit on how frequent you can write to the main memory.
If the store are too close together or the CPU time is so much faster than the DRAM cycle time, you can end up overflowing the write buffer and the CPU must stop and wait.
+2 = 60 min. (Y:40)

## Slide 38: Write Hit: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first
Data in cache and memory is inconsistent

## Slide 39: Write Miss: Write Allocation
Write Miss:
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 40: Example: Intrinsity FastMATH
Embedded MIPS processor
  12-stage pipeline
  Instruction and data access on each cycle
Split cache: separate I-cache and D-cache
  Each 16KB: 256 blocks × 16 words/block
  D-cache: write-through or write-back
SPEC2000 miss rates
  I-cache: 0.4%
  D-cache: 11.4%
  Weighted average: 3.2%

## Slide 41: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 42: Memory Design to Support Cache
How to increase memory bandwidth to reduce miss penalty?
Fig. 5.11

## Slide 43: Interleaving for Bandwidth
D1 available
Start access for D1
Start access for D2
Cycle time
Access time
Access Bank 0 again
Access Bank 0,1,2, 3
Access pattern without interleaving:
Access pattern with interleaving
Transfer time
Data ready

## Slide 44: Miss Penalty for Different Memory Organizations
Assume
1 memory bus clock to send the address
15 memory bus clocks for each DRAM access initiated (cycle time)
1 memory bus clock to send a word of data
A cache block = 4 words
Three memory organizations :
  A one-word-wide bank of DRAMs
  Miss penalty = 1 + 4 x 15 + 4 x 1 = 65
  A four-word-wide bank of DRAMs
  Miss penalty = 1 + 15 + 1 = 17
  A four-bank, one-word-wide bus of DRAMs
  Miss penalty = 1 + 1 x 15 + 4 x 1 = 20
Notes: Shall transfer time overlap with the cycle time?

## Slide 45: Access of DRAM
21-0
2048 x 2048
array

## Slide 46: DRAM Generations
Year | Capacity | $/GB
1980 | 64Kbit | $1500000
1983 | 256Kbit | $500000
1985 | 1Mbit | $200000
1989 | 4Mbit | $50000
1992 | 16Mbit | $15000
1996 | 64Mbit | $10000
1998 | 128Mbit | $4000
2000 | 256Mbit | $1000
2004 | 512Mbit | $250
2007 | 1Gbit | $50
Trac:access time to a new row
Tcac:column access time to existing row

## Slide 47: DDR SDRAM
Double Data Rate Synchronous DRAMs
Burst access from a sequential locations
Starting address, burst length
Data transferred under control of clock
(300 MHz, 2004)
Clock is used to eliminate the need of synchronization and the need of supplying successive address
Data transfer on both leading an falling edge of clock

## Slide 48: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 49: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:

## Slide 50: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
  Compute the actual CPI?
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 51: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 52: Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 53: Improving Cache Performance
Reduce the time to hit in the cache
Decreasing the miss ratio
Decreasing the miss penalty

## Slide 54: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 55: Direct Mapped
Block Placement :
  For each item of data at the lower level, there is exactly one location in cache where it might be
  Address mapping: modulo number of blocks
M
e
m
o
r
y
0
0
0
0
1
0
0
1
0
1
0
1
0
0
1
0
1
1
0
1
1
0
0
0
1
1
0
1
0
1
1
1
0
0
1
1
1
1
0
1
0
0
0
0
0
1
0
1
0
0
1
1
1
0
0
1
0
1
1
1
0
1
1
1

## Slide 56: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 57: Associative Cache Example
Placement of a block whose address is 12:

## Slide 58: Possible Associativity Structures
An 8-block cache

## Slide 59: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 
time

## Slide 60: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 
time
time

## Slide 61: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 62: A 4-Way Set-Associative Cache
Increasing associativity shrinks index, expands tag

## Slide 63: Comparing Data Available Time
Direct mapped cache
  Cache block is available BEFORE Hit/Miss:
  Possible to assume a hit and continue, recover later if miss
N-way set-associative cache
  Data comes AFTER Hit/Miss decision
  Extra MUX delay for the data
62

## Slide 64: Data Placement Policy
Direct mapped cache:
  Each memory block mapped to one location
  No need to make any decision
  Current item replaces previous one in location
N-way set associative cache:
  Each memory block has choice of N locations
Fully associative cache:
  Each memory block can be placed in ANY cache location
Misses in N-way set-associative or fully associative cache:
  Bring in new block from memory
  Throw out a block to make room for new block
  Need to decide on which block to throw out

## Slide 65: Cache Block Replacement
Direct mapped: no choice
Set associative or fully associative:
  Random
  LRU (Least Recently Used):
    Hardware keeps track of the access history and replace the block that has not been used for the longest time
  An example of a pseudo LRU (for a two-way set associative) :
    use a pointer pointing at each block in turn
    whenever an access to the block the pointer is pointing at, move the pointer to the next block
    when need to replace, replace the block currently pointed at

## Slide 66: Comparing the Structures
N-way set-associative cache
  N comparators vs. 1
  Extra MUX delay for the data
  Data comes AFTER Hit/Miss decision and set selection
Direct mapped cache
  Cache block is available BEFORE Hit/Miss:
  Possible to assume a hit and continue, recover later if miss

## Slide 67: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 68: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 69: Multilevel Cache Example
Given
  CPU base CPI = 1, clock rate = 4GHz
  Miss rate/instruction = 2%
  Main memory access time = 100ns
With just primary cache
  Miss penalty = 100ns/0.25ns = 400 cycles
  Effective CPI = 1 + 0.02 × 400 = 9

## Slide 70: Example (cont.)
Now add L-2 cache
  L-1 miss rate to L-2 = 2% (with one cache: to M)
  L-2 access time = 5ns (to M: 100ns)
  L-2 miss rate to main memory = 0.5%
Primary miss with L-2 hit (2%)
  Penalty to access L-2 = 5ns/0.25ns = 20 cycles
Primary miss with L-2 miss (0.5%)
  Penalty to access memory = 400 cycles
CPI = 1 + 0.02 × 20 + 0.005 × 400 = 3.4
Performance ratio = 9/3.4 = 2.6

## Slide 71: Multilevel Cache Considerations
Primary cache
  Focus on minimal hit time
L-2 cache
  Focus on low miss rate to avoid main memory access
  Hit time has less overall impact
Results
  L-1 cache usually smaller than a single-level cache
  L-1 block size smaller than L-2 block size

## Slide 72: Interactions with Advanced CPUs
Out-of-order CPUs can execute instructions during cache miss
  Pending store stays in load/store unit
  Dependent instructions wait in reservation stations
    Independent instructions continue
Effect of miss depends on program data flow
  Much harder to analyze
  Use system simulation

## Slide 73: Interactions with Software
Misses depend on memory access patterns
  Algorithm behavior
  Compiler optimization for memory access

## Slide 74: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 75: Levels of Memory Hierarchy
Registers
Cache
Memory
Disk
Tape
Instr. Operands
Blocks
Pages
Files
Staging
Transfer Unit
prog./compiler
cache controller
OS
user/operator
Upper Level
Lower Level
faster
Larger

## Slide 76: Virtual Memory
pages
register
cache
memory
disk
frame
75

## Slide 77: Diagram of Process State
new
ready
running
terminated
waiting
admitted
interrupt
exit
scheduler dispatch
I/O or event wait
I/O or
event completion

## Slide 78: CPU Scheduler
selecting one of the ready processes, and allocates the CPU to it.
ready queue
I/O queue(s)
I/O
CPU

## Slide 79: Virtual Memory
Programs share main memory (Multi-programming and I/O)
  Program executed in a name space (virtual address space) different from memory space (physical address space)
  Each gets a private virtual address space holding its frequently used code and data, starting at address 0, only accessible to itself
    yet, any can run anywhere in physical memory
    virtual memory implements the translation from virtual space to physical space
  Every program has lots of memory (> physical memory)
  Protected from other programs
Use main memory as a “cache” for secondary (disk) storage
  Managed jointly by CPU hardware and the operating system (OS)

## Slide 80: Virtual Memory - Continued
CPU and OS translate virtual addresses to physical addresses
  VM “block” is called a page
  VM translation “miss” is called a page fault

## Slide 81: Virtual Memory

Notes: 80

## Slide 82: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 83: Basic Issues in Virtual Memory
Size of data blocks that are transferred from disk to main memory
Which region of memory to hold new block => placement policy (how to the page?)
When memory is full, then some region of memory must be released to make room for the new block => replacement policy
When to fetch missing items from disk?
  Fetch only on a fault => demand load policy
pages
register
cache
memory
disk
frame

## Slide 84: Block Size and Placement Policy
Huge miss penalty: a page fault may take millions of cycles to process
  Pages should be fairly large (e.g., 4KB) to amortize the high access time
  Reducing page faults is important
    fully associative placement => use page table (in memory) to locate pages

## Slide 85: Address Translation
Fixed-size pages (e.g., 4K)

## Slide 86: Paging
Virtual and physical address space partitioned into blocks of equal size
Key operation: address mapping
MAP: V  M  {} address mapping function
MAP(a) = a' if data at virtual address a is present in physical address a' and a' in M
=  if data at virtual address a is not present in M
page frames
pages
Processor
Name Space V
Addr Trans
Mechanism
fault
handler
Main
Memory
Secondary
Memory
a
a
a'

missing item fault
physical address
OS does this transfer

## Slide 87: Page Tables
Stores placement information
  Page table stored in main memory
  Array of page table entries, indexed by virtual page number
  Page table register in CPU points to page table in physical memory
If page is present in memory
  PTE stores the physical page number
  Plus other status bits (referenced, dirty, …)
If page is not present
  PTE can refer to location in swap space on disk

## Slide 88: Page Tables
all addresses generated by the program are virtual addresses
table located in physical memory
Fig. 5.21
How many memory references for each address translation?

## Slide 89: Page Fault: What Happens When You Miss?
Page hit, proceed normally
Page fault means that page is not resident in memory
Huge miss penalty: a page fault may take millions of cycles to process
Hardware must detect situation but it cannot remedy the situation
Can handle the faults in software instead of hardware, because handling time is small compared to disk access
  the software can be very smart or complex
  the faulting process can be context-switched

## Slide 90: OS Handling Page Faults
Hardware must trap to the operating system so that it can remedy the situation
  Pick a page to discard (may write it to disk)
  Load the page in from disk
  Update the page table
  Resume to program so HW will retry and succeed!
In addition, OS must know where to find the page
  Create space on disk for all pages of process (swap space)
  Use a data structure to record where each valid page is on disk (may be part of page table)
  Use another data structure to track which process and virtual addresses use each physical page => for replacement purpose

## Slide 91: When to Fetch Missing Items From Disk
Fetch only on a fault
  => Demand load policy

## Slide 92: Page Replacement and Writes
To reduce page fault rate, prefer least-recently used (LRU) replacement
  Reference bit (aka use bit) in PTE set to 1 on access to page
  Periodically cleared to 0 by OS
  A page with reference bit = 0 has not been used recently
Disk writes take millions of cycles
  Block at once, not individual locations
  Write through is impractical
  Use write-back
  Dirty bit in PTE set when page is written

## Slide 93: Problems of Page Table
Page table is too big
Access to page table is too slow (needs one memory read)

## Slide 94: Problems of Page Table
Page table is too big
Access to page table is too slow (needs one memory read)

## Slide 95: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 96: Impact of Paging: Huge Page Table
Page table occupies storage 32-bit VA, 4KB page, 4bytes/entry => 220 PTE, 4MB table
Possible solutions:
  Use bounds register to limit table size; add more if exceed
  Let pages to grow in both directions => 2 tables, 2 limit registers, one for hash, one for stack
  Use hashing => page table same size as physical pages
  Multiple levels of page tables
  Paged page table (page table resides in virtual space)

## Slide 97: Hashing: Inverted Page Tables
28-bit virtual address,4 KB per page, and 4 bytes per page-table entry
The number of pages: 64K
The number of physical frames: 16K
  Page table size : 64 K (pages #) x 4 = 256 KB
  Inverted page table : 16 K (frame #) x (4+?) = 64 KB
  => TLBs or virtually addressed caches are critical
V.Page P. Frame
Hash
Virtual
Page
=
Notes: Page 520

## Slide 98: Two-level Page Tables
32-bit address:
P1 index
P2 index
page offset
4 bytes
4 bytes
4KB
10
10
12
1K
PTEs
4 GB virtual address space
4 KB of PTE1
(Each entry indicate if any page in the segment is allocated)
4 MB of PTE2
  paged, holes
What about a 48-64 bit address space?

## Slide 99: Problems of Page Table
Page table is too big
Access to page table is too slow (needs one memory read)

## Slide 100: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 101: Impact of Paging: More Memory Access !
Each memory operation (instruction fetch, load, store) requires a page-table access!
  Basically double number of memory operations
  One to access the PTE
  Then the actual memory access
access to page tables has good locality

## Slide 102: Fast Translation Using a TLB
Access to page tables has good locality
  Fast cache of PTEs within the CPU
  Called a Translation Look-aside Buffer (TLB)

## Slide 103: Fast Translation Using TLB (Translation Lookaside Buffer)
Fig. 5.23
TLB

## Slide 104: Translation Lookaside Buffer
Typical RISC processors have memory management unit (MMU) which includes TLB and does page table lookup
  TLB can be organized as fully associative, set associative, or direct mapped
  TLBs are small, typical: 16–512 PTEs, 0.5–1 cycle for hit, 10–100 cycles for miss, 0.01%–1% miss rate
  Misses could be handled by hardware or software

## Slide 105: TLB Hit
TLB hit on read
TLB hit on write:
  Toggle dirty bit (write back to page table on replacement)

## Slide 106: TLB Miss
If page is in memory
  Load the PTE from memory and retry
  Could be handled in hardware
    Can get complex for more complicated page table structures
  Or in software
    Raise a special exception, with optimized handler
If page is not in memory (page fault)
  OS handles fetching the page and updating the page table (software)
  Then restart the faulting instruction

## Slide 107: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 108: Making Address Translation Practical
In VM, memory acts like a cache for disk
  Page table maps virtual page numbers to physical frames
  Use a page table cache for recent translation => Translation Lookaside Buffer (TLB)
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
20 t
t
1/2 t
Translation
with a TLB

## Slide 109: Integrating TLB and Cache
Fig. 5.24
V
a
l
i
d
T
a
g
D
a
t
a
P
a
g
e
o
f
f
s
e
t
P
a
g
e
o
f
f
s
e
t
V
i
r
t
u
a
l
p
a
g
e
n
u
m
b
e
r
V
i
r
t
u
a
l
a
d
d
r
e
s
s
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
V
a
l
i
d
1
2
2
0
2
0
1
6
1
4
C
a
c
h
e
i
n
d
e
x
3
2
C
a
c
h
e
D
a
t
a
C
a
c
h
e
h
i
t
2
B
y
t
e
o
f
f
s
e
t
D
i
r
t
y
T
a
g
T
L
B
h
i
t
P
h
y
s
i
c
a
l
p
a
g
e
n
u
m
b
e
r
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
t
a
g
T
L
B
P
h
y
s
i
c
a
l
a
d
d
r
e
s
s
3
1
3
0
2
9
1
5
1
4
1
3
1
2
1
1
1
0
9
8
3
2
1
0
(Data)

## Slide 110: TLBs and caches

## Slide 111: Possible Combinations of Events
Cache
TLB
Page
table
Possible? Conditions?
Miss
Hit
Hit
Yes; but page table never checked if
TLB hits
Hit
Miss
Hit
TLB miss, but entry found in page
table;after retry, data in cache
Miss
Miss
Hit
TLB miss, but entry found in page
table; after retry, data miss in cache
Miss
Miss
Miss
TLB miss and is followed by a page
fault; after retry, data miss in cache
Miss
Hit
Miss
impossible;
not in TLB if page not in memory
Hit
Hit
Miss
impossible;
not in TLB if page not in memory
Hit
Miss
Miss
impossible;
not in cache if page not in memory

## Slide 112: Virtual Address and Cache
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
CPU
data
Trans-
lation
Cache
Main
Memory
VA
hit
PA
CPU
TLB access is serial with cache access
  Cache is physically indexed and tagged
Alternative: virtually addressed cache
  Cache is virtually indexed and virtually tagged

## Slide 113: Virtually Addressed Cache
Require address translation only on miss!
Problem:
  Same virtual addresses (different processes) map to different physical addresses:
  Synonym/alias problem: two different virtual addresses map to same physical address
    Two different cache entries holding data for the same physical address!
    For update: must update all cache entries with same physical address or memory becomes inconsistent
    Determining this requires significant hardware, essentially an associative lookup on the physical address tags to see if you have multiple hits;
    Or software enforced alias boundary: same least-significant bits of VA &PA > cache size
tag + process id

## Slide 114: Integrating TLB and Cache
Fig. 5.24

## Slide 115: An Alternative:Virtually Indexed but Physically Tagged (Overlapped Access)
TLB
Cache
10
2
00
4 bytes
index
1 K
page #
displace
20
12
associative
lookup
32
PA
Hit/
Miss
PA
Data
Hit/
Miss
=
IF cache hit AND (cache tag = PA) then deliver data to CPU
ELSE IF [cache invalid OR (cache tag ! = PA)] and TLB hit THEN
access memory with the PA from the TLB
ELSE do standard VA translation

## Slide 116: Problem with Overlapped Access
11
2
00
virt page #
disp
20
12
cache
index
This bit is changed by VA translation, but is needed for cache lookup
Solutions:
go to 8K byte page sizes;
go to 2 way set associative cache
SW guarantee VA[13]=PA[13]
1K
4
4
10
2-way set associative cache
Address bits to index into cache must not change as a result of VA translation
  Limits to small caches, large page sizes, or high n-way set associativity if want a large cache
  Ex.: cache is 8K bytes instead of 4K:

## Slide 117: Outline
Memory hierarchy
The basics of caches
  Direct-mapped cache
  Address sub-division
  Cache hit and miss
  Memory support
Measuring cache performance
Improving cache performance
  Set associative cache
  Multiple level cache
Virtual memory
  Basics
  Issues in virtual memory
  Handling huge page table
  TLB (Translation Lookaside Buffer)
  TLB and cache
A common framework for memory hierarchy

## Slide 118: The Memory Hierarchy
Common principles apply at all levels of the memory hierarchy
  Based on notions of caching
At each level in the hierarchy
  Block placement
  Finding a block
  Replacement on a miss
  Write policy
The BIG Picture

## Slide 119: Block Placement
Determined by associativity
  Direct mapped (1-way associative)
    One choice for placement
  n-way set associative
    n choices within a set
  Fully associative
    Any location
Higher associativity reduces miss rate
  Increases complexity, cost, and access time

## Slide 120: Finding a Block
Hardware caches
  Reduce comparisons to reduce cost
Virtual memory
  Full table lookup makes full associativity feasible
  Benefit in reduced miss rate
Associativity | Location method | Tag comparisons
Direct mapped | Index | 1
n-way set associative | Set index, then search entries within the set | n
Fully associative | Search all entries | #entries
 | Full lookup table | 0

## Slide 121: Replacement
Choice of entry to replace on a miss
  Least recently used (LRU)
    Complex and costly hardware for high associativity
  Random
    Close to LRU, easier to implement
Virtual memory
  LRU approximation with hardware support

## Slide 122: Write Policy
Write-through
  Update both upper and lower levels
  Simplifies replacement, but may require write buffer
Write-back
  Update upper level only
  Update lower level when block is replaced
  Need to keep more state
Virtual memory
  Only write-back is feasible, given disk write latency

## Slide 123: Sources of Misses
Compulsory misses (aka cold start misses)
  First access to a block
Capacity misses
  Due to finite cache size
  A replaced block is later accessed again
Conflict misses (aka collision misses)
  In a non-fully associative cache
  Due to competition for entries in a set
  Would not occur in a fully associative cache of the same total size

## Slide 124: Challenge in Memory Hierarchy
Every change that potentially improves miss rate can negatively affect overall performance
Design change Effects on miss rate Possible effects
size  capacity miss  access time 
associativity  conflict miss  access time 
block size  spatial locality  miss penalty 
Trends:
  Synchronous SRAMs (provide a burst of data)
  Redesign DRAM chips to provide higher bandwidth or processing
  Restructure code to increase locality
  Use prefetching (make cache visible to ISA)

## Slide 125: Outline
Memory hierarchy
The basics of caches
Measuring and improving cache performance
Virtual memory
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 126: Cache Control
Example cache characteristics
  Direct-mapped, write-back, write allocate
  Block size: 4 words (16 bytes)
  Cache size: 16 KB (1024 blocks)
  32-bit byte addresses
  Valid bit and dirty bit per block
  Blocking cache
    CPU waits until access is complete
Tag
Index
Offset
0
3
4
13
14
31
4 bits
10 bits
18 bits

## Slide 127: Interface Signals
Cache
CPU
Memory
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
32
32
Read/Write
Valid
Address
Write Data
Read Data
Ready
32
128
128
Multiple cycles per access

## Slide 128: Cache Controller FSM
Could partition into separate states to reduce clock cycle time

## Slide 129: Finite State Machines
Use an FSM to sequence control steps
Set of states, transition on each clock edge
  State values are binary encoded
  Current state stored in a register
  Next state = fn (current state, current inputs)
Control output signals = fo (current state)

## Slide 130: Outline
Memory hierarchy
The basics of caches
Measuring and improving cache performance
Virtual memory
A common framework for memory hierarchy
Using a Finite State Machine to Control a Simple Cache
Parallelism and Memory Hierarchies: Cache Coherence

## Slide 131: Cache Coherence Problem
Suppose two CPU cores share a physical address space
  Write-through caches
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1
Two different processors have two different values for the same location

## Slide 132: Coherence Defined
Informally: Reads return most recently written value
Formally:
  P writes X; P reads X (no intervening writes)  read returns written value
  P1 writes X; P2 reads X (sufficiently later)  read returns written value
    c.f. CPU B reading X after step 3 in example
  P1 writes X, P2 writes X  all processors see writes in the same order
    End up with the same final value for X

## Slide 133: Cache Coherence Protocols
Operations performed by caches in multiprocessors
  Migration of data to local caches
    Reduces bandwidth for shared memory
  Replication of read-shared data
    Reduces contention for access
Snooping protocols
  Each cache monitors bus reads/writes
Directory-based protocols
  Caches and memory record sharing status of blocks in a directory

## Slide 134: Invalidating Snooping Protocols
Cache gets exclusive access to a block when it is to be written
  Broadcasts an invalidate message on the bus
  Subsequent read in another cache misses
    Owning cache supplies updated value
CPU activity | Bus activity | CPU A’s cache | CPU B’s cache | Memory
 |  |  |  | 0
CPU A reads X | Cache miss for X | 0 |  | 0
CPU B reads X | Cache miss for X | 0 | 0 | 0
CPU A writes 1 to X | Invalidate for X | 1 |  | 0
CPU B read X | Cache miss for X | 1 | 1 | 1

## Slide 135: Multilevel On-Chip Caches
§5.10 Real Stuff: The AMD Opteron X4 and Intel Nehalem
Per core: 32KB L1 I-cache, 32KB L1 D-cache, 512KB L2 cache
Intel Nehalem 4-core processor

## Slide 136: 2-Level TLB Organization
 | Intel Nehalem | AMD Opteron X4
Virtual addr | 48 bits | 48 bits
Physical addr | 44 bits | 48 bits
Page size | 4KB, 2/4MB | 4KB, 2/4MB
L1 TLB (per core) | L1 I-TLB: 128 entries for small pages, 7 per thread (2×) for large pages L1 D-TLB: 64 entries for small pages, 32 for large pages Both 4-way, LRU replacement | L1 I-TLB: 48 entries L1 D-TLB: 48 entries Both fully associative, LRU replacement
L2 TLB (per core) | Single L2 TLB: 512 entries 4-way, LRU replacement | L2 I-TLB: 512 entries L2 D-TLB: 512 entries Both 4-way, round-robin LRU
TLB misses | Handled in hardware | Handled in hardware

## Slide 137: 3-Level Cache Organization
 | Intel Nehalem | AMD Opteron X4
L1 caches (per core) | L1 I-cache: 32KB, 64-byte blocks, 4-way, approx LRU replacement, hit time n/a L1 D-cache: 32KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | L1 I-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, hit time 3 cycles L1 D-cache: 32KB, 64-byte blocks, 2-way, LRU replacement, write-back/allocate, hit time 9 cycles
L2 unified cache (per core) | 256KB, 64-byte blocks, 8-way, approx LRU replacement, write-back/allocate, hit time n/a | 512KB, 64-byte blocks, 16-way, approx LRU replacement, write-back/allocate, hit time n/a
L3 unified cache (shared) | 8MB, 64-byte blocks, 16-way, replacement n/a, write-back/allocate, hit time n/a | 2MB, 64-byte blocks, 32-way, replace block shared by fewest cores, write-back/allocate, hit time 32 cycles
n/a: data not available |  | 

## Slide 138: Pitfalls
Byte vs. word addressing
  Example: 32-byte direct-mapped cache, 4-byte blocks
    Byte 36 maps to block 1
    Word 36 maps to block 4
Ignoring memory system effects when writing or generating code
  Example: iterating over rows vs. columns of arrays
  Large strides result in poor locality

## Slide 139: Pitfalls
In multiprocessor with shared L2 or L3 cache
  Less associativity than cores results in conflict misses
  More cores  need to increase associativity
Using AMAT (Average Memory Access Time) to evaluate performance of out-of-order processors
  Ignores effect of non-blocked accesses
  Instead, evaluate performance by simulation

## Slide 140: Concluding Remarks
Fast memories are small, large memories are slow
  We really want fast, large memories 
  Caching gives this illusion 
Principle of locality
  Programs use a small part of their memory space frequently
Memory hierarchy
  L1 cache  L2 cache  …  DRAM memory  disk
Memory system design is critical for multiprocessors