## Slide 1: CS5100 Advanced Computer Architecture Performance Evaluation
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. Hsien-Hsin Lee, Prof. Yasun Hsu)

## Slide 2: Outline
Goal of this lecture:
  To learn how to evaluate the performance of computers as the basis of a quantitative approach to computer design
    Know performance evaluation and understand the implications behind the numbers
Lecture outline
  Measuring, reporting, summarizing performance (Sec. 1.8)
  Quantitative principles of computer design (Sec. 1.9)

## Slide 3: Which Device Has the Best Performance?

## Slide 4: Things to Clarify
What do you mean by “performance”?
  How to quantify the performance?
  What performance metrics to use?
  Best performance  Best!
How to measure the “performance”?
  What configurations of the devices are used?
  What workloads are used?
  How to get the performance data?
How to summarize and compare the performance?
  A total ordering needed
How to report the results?

## Slide 5: Which Design is Better?
P0
P1
P2
P3
L1$
L1$
L1$
L1$
Bus
Memory
L2$
Bus
P0
L1$
P1
L1$
P2
L1$
P3
L1$
Memory

## Slide 6: Things to Clarify
What do you mean by “better”?
How to estimate the performance of designs, even before hardware is ready and software is running?
  What kinds of tools are available?
  At what level of details do you want the performance be studied? e.g. get performance data only or get correct execution outputs also, specific component or whole system, accurate to clock cycle or to function, single application or OS+applications, …

## Slide 7: What Do You Mean by “Performance”?
Many performance metrics:
  GHz, number of cores
  MIPS (million instructions per second)
  MFLOPS (million floating-point operations per second)…
Time is the primary measure of performance
  Execution/response time (latency) vs. throughput (BW)
  Wall clock time: latency to complete a task, including all system overheads
  CPU time: the time that the processor is computing, not including I/O or running other programs
  Single program vs. whole system
6
Notes: MIPS (meaningless indicator of performance from salesman): lack of a uniform measure of work
-- instruction sets are not equivalent
-- different programs use different instruction mix
-- instruction count is not a reliable indicator of work (some optimizations add instructions)
FLOPS:
-- programs must be FP intensive
-- ignore other instructions, e.g. loads and stores
-- peak GFLOPS: manufacturer guarantees not to exceed

## Slide 8: CPU Performance (of a Program)
Execution Time = Seconds/Program
=
Programmer
Algorithms
ISA
Compilers
Microarchitecture
System architecture
Microarchitecture, pipeline depth
Circuit design
Technology
CPI

## Slide 9: Cycles Per Instruction (CPI)
Alternative formula: instruction frequency
CPU time = CycleTime   CPIi  Ii
i = 1
n
CPI =  CPIi  Fj where Fj = Ij
i = 1
n
Instruction Count
CPI = Cycles / Instruction Count
  = (CPU Time * Clock Rate) / Instruction Count
How about pipelined processors?

## Slide 10: Example: Calculating CPI
Run benchmarks, collect workload characterization (by simulation, machine counters, or sampling)
9
Base Machine (Reg - Reg)
Op Freq Cycles CPI(i) (% Time)
ALU 50% 1 .5 (33%)
Load 20% 2 .4 (27%)
Store 10% 2 .2 (13%)
Branch 20% 2 .4 (27%)
1.5

## Slide 11: Accounting Stalls
CPI = CPIideal + CPIstall
  CPIideal: cycles per instruction if no stall
  CPIstall contributors
    Data dependences: RAW, WAR, WAW
    Structural hazards
    Control hazards: branches, exceptions
    Memory latency: cache misses

## Slide 12: New Breed of Metrics
Performance/Watt
  Performance achievable at the same cooling capacity
Performance/Joule (Energy)
  Achievable performance at the lifetime of the same energy source (i.e., battery = energy)
  Equivalent to reciprocal of energy-delay product (ED product)
11

## Slide 13: Outline of Performance Evaluation
What do you mean by “performance”?
  Performance metrics
What to evaluate?
  Workloads, benchmarks
How to evaluate?
How to summarize and report?

## Slide 14: Performance Benchmarking
Benchmark: a standard of measurement as a reference point for comparison
  Model real job mix with a small set of representative programs
Kernels:
  Small key pieces of real programs, e.g. Linpack
  Best used to isolate performance of individual features
(Toy) programs:
  Typically 10 to 100 lines to test a special function and/or its performance, e.g. quicksort, matrix multiply

## Slide 15: Performance Benchmarking
Synthetic benchmarks:
  Try to match the average frequency and operation of a large set of programs , e.g. Dhrystone, Whetstone
(Real) programs
  Having inputs, outputs, and options; running on standard OS, e.g. SPEC2006, TPC-C, SYSMARK, 3D Winbench
  Often come with a suite
14

## Slide 16: Benchmark Suites: SPEC
SPEC goal: a fair and useful set of metrics to compare performance
  www.spec.org
SPECCPU: popular desktop benchmark suite
  CPU only, split between integer and floating-point programs, where SPECint2006 has 12 integer, SPECfp2006 has 17 floating-point programs
  Use geometric mean
SPECSFS (NFS file server) and SPECWeb (WebServer) added as server benchmarks (mainly for I/O: disk and network)

## Slide 17: Benchmark Suites
TPC (Transaction Processing Council) measures server performance and cost-performance for databases
  TPC-C Complex query for Online Transaction Processing
  Metrics: # transactions per sec and response time
EEMBC (EDN embedded Microprocessor Benchmark Consortium)
  Set of 41 kernels for performance of embedded applications
Benchmarks for mobile phones:
  Quadrant, AnTuTu, CFBench, MobileBench

## Slide 18: Some Warnings about Benchmarking
Benchmarks reflect yesterday’s programs
Benchmarks can lead to positive feedbacks
  If you make an operation fast (slow), it will be used more (less) often; so you make it faster (slower), and so on…
Tricks and common mistakes in benchmarking:
  Different system configurations
  Compiler and libraries optimized for benchmarks
  Workload/inputs arbitrarily picked
  Very small benchmarks  ignore caching effects
  Only average behavior represented in test workload
  Ignoring monitoring overhead
  Too much data but too little analysis

## Slide 19: Outline of Performance Evaluation
What do you mean by “performance”?
  Performance metrics
What to evaluate?
  Workloads, benchmarks
How to evaluate?
How to summarize and report?

## Slide 20: To Evaluate Real Machines
Run the benchmark and obtain performance
  How to measure program execution time?
  How to obtain instruction count?
  How to separate effects of OS, virtual machine, and measuring tool itself?
Programs use timer API
Instrumentation
  PinTool: dynamic binary instrumentation engine for Intel x86
Performance monitor and profiler
  Oprofile: monitor HW/SW events through CPU perf. counters
  Linux perf

## Slide 21: Instrumentation
A technique that inserts code into a program to collect run-time information
  Source code instrumentation
  Static binary instrumentation
  Dynamic binary instrumentation
Tevi Devor, Intel

## Slide 22: To Evaluate Designs
Scope: full system vs. component
  Component simulators: instruction set simulator, cache, network-on-chip (NoC), DRAM, disk, …
  Full-system: simulate an entire computer that complete software stacks from real systems can run without any modification  a virtual hardware, e.g. QEMU, Gem5
Detail: functional vs. timing
  Timing simulators: cycle accurate, cycle-count accurate
Input: trace-driven vs. execution-driven
Tradeoffs between simulation speed and accuracy

## Slide 23: QEMU
A processor emulator using dynamic binary translation
  Full system emulation
  User mode emulation
Notes: Full system emulation. In this mode, QEMU emulates a full system (for example a PC), including one or several processors and various peripherals. It can be used to launch different Operating Systems without rebooting the PC or to debug system code.
User mode emulation. In this mode, QEMU can launch processes compiled for one CPU on another CPU. It can be used to launch the Wine Windows API emulator (http://www.winehq.org) or to ease cross-compilation and cross-debugging.

## Slide 24: QEMU
Helper functions
  Inserted during binary translation (guest code -> TCG IR) to handle extra works, e.g. profiling

## Slide 25: Outline of Performance Evaluation
What do you mean by “performance”?
  Performance metrics
What to evaluate?
  Workloads, benchmarks
How to evaluate?
How to summarize and report?

## Slide 26: Run and Reporting Rules
Goal #1: reproducible results
  Document everything
  Others should be able to reproduce your results
Goal #2: fair results
  Restrict “tricks” that can be played, e.g. optimizations must work for more than just this benchmark
  Specify how results may be summarized, e.g. use an appropriate averaging technique
How to reduce n performance indices into a single number to produce a total ordering of computers?

## Slide 27: Summarize Performance
A straightforward idea:
  Sum individual benchmark times and then average
  Arithmetic Mean (Weighted Arithmetic Mean)
The problem:
  Benchmark Comp 1 Comp 2 Comp 3
  A 1 10 20
  B 1000 100 20
  Total 1001 110 40
  Is Computer 3 really the fastest?
  Benchmark B dominates the performance!

## Slide 28: Summarize Performance with Ratios
Arithmetic mean of ratios: (Ri)/n
  Normalized with respect to Computer 3: Benchmark Comp 1 Comp 2 Comp 3 A 1 (0.05) 10 (0.5) 20 (1) B 1000 (50) 100 (5) 20 (1) Mean 25.025 2.75 1
  Computer 3 is the fastest!
  But, if normalized with respect to Computer 1: Benchmark Comp 1 Comp 2 Comp 3 A 1 (1) 10 (10) 20 (20) B 1000 (1) 100 (0.1) 20 (0.02) Mean 1 5.05 10.01
  Computer 1 is the fastest! 3 is the slowest!

## Slide 29: Geometric Mean for Ratios
Geometric mean:
  Independent of the reference machine Benchmark Comp 1 Comp 2 Comp 3 A 1 (0.05) 10 (0.5) 20 (1) B 1000 (50) 100 (5) 20 (1) Mean wrt 3 1.58 1.58 1
  Computer 3 is the fastest!
  Benchmark Comp 1 Comp 2 Comp 3 A 1 (1) 10 (10) 20 (20) B 1000 (1) 100 (0.1) 20 (0.02) Mean wrt 1 1 1 0.63
  Computer 3 is the fastest!

## Slide 30: Geometric Mean for Ratios
Geometric mean is not consistent with time:
  Benchmark Comp 1 Comp 2 Comp 3 A 12 6 24 B 16 32 8
  Total time 28 38 32
  Normalize to 1 1.00 1.36 1.14
  G. mean wrt 1 1.00 1.00 1.00
So, what can we say about summarizing performance?

## Slide 31: Geometric Mean for Ratios
If benchmark execution times are normalized to some reference machine, and means of normalized execution times are computed, only the geometric mean gives consistent results no matter what the reference machine is.
  This has led to declaring the geometric mean as the preferred method of summarizing execution time (e.g., SPEC2006)

## Slide 32: Summarizing Performance
Time is the ultimate measure of performance
(Weighted) arithmetic mean tracks time:
  But may be skewed by individual programs
  Is meaningless with normalized numbers
Geometric mean:
  Consistent regardless of reference
  Independent of execution times of individual programs
  Does not predict execution time
Best strategy: show the summarized number as well as numbers of individuals

## Slide 33: Performance Evaluation: Summary
Performance evaluation affects and guides the design of computers
Good performance evaluation requires:
  Good benchmarks
  Good ways to summarize performance
Execution time is the ultimate measure of computer performance!

## Slide 34: Outline
Measuring, reporting, summarizing performance (Sec. 1.8)
Quantitative principles of computer design (Sec. 1.9)
  Take advantage of parallelism: e.g. multiple processors, disks, memory banks, pipelining, multiple functional units
  Principle of locality: Reuse of data and instructions
  Focus on the common case
    Amdahl’s Law

## Slide 35: 1) Taking Advantage of Parallelism
Increasing throughput of server computer via ILP, multiple cores/processors or multiple disks
Examples of detailed HW designs
  Carry lookahead adders uses parallelism to speed up from linear to logarithmic in number of bits per operand
  Multiple memory banks searched in parallel in set-associative caches
  Pipelining: overlap instruction execution to reduce the total time to complete an instruction sequence.
    Not every instruction depends on immediate predecessor  executing instructions completely/partially in parallel
  Superscalar, multithreading

## Slide 36: 2) Principle of Locality
Programs access a relatively small portion of the address space at any instant of time
  90/10 rule: a program spends 90% of its execution time in only 10% of the code
Two different types of locality:
  Temporal locality (locality in time): If an item is referenced, it tends to be referenced again soon (e.g., loops, reuse)
  Spatial locality (locality in space): If an item is referenced, items whose addresses are close by tend to be referenced soon (e.g., straight-line code, array access)
Last 30 years, HW relied on locality for memory performance

## Slide 37: 3) Focus on the Common Case
Common sense guides computer design
  Since its engineering, common sense is valuable
In making a design tradeoff, favor the frequent case over the infrequent case
  e.g., Instruction fetch and decode unit used more frequently than multiplier, so optimize it first
Frequent case is often simpler and can be done faster than the infrequent case
  e.g., overflow is rare when adding 2 numbers, so improve performance by optimizing no-overflow
What is frequent case and how much performance improved by making case faster  Amdahl’s Law

## Slide 38: Amdahl’s Law (Law of Diminishing Returns)
Speedup due to enhancement E:
= Perfnew / Perfold = Told / Tnew =
Performance improvement from using enhancement E is limited by the fraction that E can be applied
  The best that one can hope is 1/(1-f)
f
(1 - f)
Told
(1 - f)
Tnew
f/P

## Slide 39: Amdahl’s Law Analogy
Driving from NTHU in Hsinchu to NCKU in Tainan
  Driving at 110 km/hr using Highway 3 to ChangHua and then Highway 1 to Tainan  2 hr
  Driving at Hsinchu local (10 min.), Tainan local (20 min.)
What is speedup using high-speed rail?
  High-speed rail at 230 km/hr: 1.1 hr (Speedup = 2/1.1 = 1.82)
  Including local driving:
  Total Speedup = 2.5 hr / 1.6 hr = 1.56
The efforts to resolve a bottleneck will lead to new bottlenecks in other parts
Key is to speed up the frequently executed blocks
38

## Slide 40: Maximum Speedup
f = 0.9, s∞
Speedup=10
G.M. Amdahl, “Computer Architecture and Amdahl’s Law,” Computer, Dec. 2013.

## Slide 41: Recap
Performance evaluation
  Performance metrics
  Performance benchmarking
  Performance summary
Computer design principles
  Take advantage of parallelism
  Principle of locality
  Focus on the common case