## Slide 1: CS5100 Advanced Computer Architecture Memory Technology & Protection
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. Hsien-Hsin Lee, Prof. Yasun Hsu)

## Slide 2: About This Lecture
Goal:
  To understand the technology inside the memory chips and their innovative, internal organizations
  To understand how virtual memory and virtual machines provide protections to a computer system
Outline:
  Memory technology and optimizations (Sec. 2.3)
  Protection: virtual memory and virtual machines (Sec. 2.4)

## Slide 3: Memory Background
Past memory designs focused on organizing multiple DRAM chips, e.g., multiple banks. Recent innovations are more inside DRAM chips
Performance metrics:
  Latency: affect cache miss penalty
    Access time: time between request and word arrival
    Cycle time: minimum time between unrelated requests
  Bandwidth: I/O and large block miss penalty (L2)
Main memory uses DRAM, cache uses SRAM
Size: DRAM/SRAM @ 4-8, Cost/cycle time: SRAM/DRAM @ 8-16

## Slide 4: Memory Background
SRAM:
  Typically 6 transistors/bit  no refresh  access time close to cycle time, but area is 10X
  Requires low power to retain bit
  Address not divided: full address
DRAM:
  One transistor/bit  destructive read
  Must be rewritten after read and periodically refreshed
    Every ~ 8 ms and each row can be refreshed simultaneously
  Addresses divided into 2 halves (memory as a 2D matrix):
    Upper half of address: row access strobe (RAS)
    Lower half of address: column access strobe (CAS)

## Slide 5: DRAM Cell and DRAM Access
Destructive read  rewritten after read  cycle time longer than access time
Leaky charges  refresh periodically
Word Line (Control)
Storage Capacitor
Bit Line (Data)
1T1C DRAM cell
Fig. 2.12
Notes: Figure 2.12 Internal organization of a DRAM. Modern DRAMs are organized in banks, typically four for DDR3. Each bank consists of a series of rows. Sending a PRE (precharge) command opens or closes a bank. A row address is sent with an Act (activate), which causes the row to transfer to a buffer. When the row is in the buffer, it can be transferred by successive column addresses at whatever the width of the DRAM is (typically 4, 8, or 16 bits in DDR3) or by specifying a block transfer and the starting address. Each command, as well as block transfers, are synchronized with a clock.

## Slide 6: DRAM Access
Access to a “closed row”
  If another row already active, first issue PRECHARGE (close the active row)
  ACTIVATE to open a new row
  READ/WRITE to access row buffer
Access to an “open row” (the row is in a buffer)
  No need for ACTIVATE command
  READ/WRITE to access row buffer

## Slide 7: DRAM Refresh
Leaky storage
Periodic refresh across DRAM rows (~ 8 ms)
  Read and write the same data back
  Each row can be refreshed simultaneously
Un-accessible when refreshing
  Variable memory latency and cache miss penalty
Example:
  4K rows in a DRAM, 100ns read cycle, decay in 64ms
  4096*100ns = 410s to refresh once
  410s / 64ms = 0.64% unavailability

## Slide 8: Memory Design
Amdahl suggests a rule of thumb:
  Memory capacity should grow linearly with processor speed for a balanced system, e.g., 1000 MB for 1000 MIPS
But DRAM performance cannot catch up with processor performance (Fig. 2.13)
  Row access time improves ~5%/year, while CAS transfer time at ~10%
Memory capacity growth is actually slowing down
  Before 1998, 4X every 3 years (following Moore’s Law)
  1998~2006, 2X every 2 years
  2006~2010, 2X only
Memory design becomes more challenging

## Slide 9: Memory Optimizations
Multiple accesses to the row buffer without another row access time
Synchronous DRAM (SDRAM)
  Original DRAMs had asynch. interface to mem. controller
  Add clock to DRAM interface for repeated transfers without handshaking overhead
  Burst mode w/o new address and with critical word first
Wider interfaces with 4-bit or 16-bit buses
Multiple banks inside a DRAM chip (Fig. 2.12)
  DRAM address now consists of bank number, row address, and column address

## Slide 10: Memory Optimizations
Double data rate (DDR):
  Transfer data on rising as well as falling edge of DRAM clock
  DDR: (Fig. 2.14)
    A 133 MHz DDR chip is called DDR266 and can transfer 266 Mbits/sec
    A DIMM (dual inline memory module) with DDR chips can transfer 133 MHz  2  8 bytes  2100 MB/sec (PC2100)
  DDR2:
    Lower power from 2.5 V  1.8 V
    Higher clock rates: 266 MHz, 333 MHz, 400 MHz
  DDR3: 1.5 V, 800 MHz
  DDR4: 1-1.2 V, 1600 MHz

## Slide 11: Memory Optimizations
DRAM scheduling policies
  In what order should we service DRAM requests
FCFS (First come first serve)
  Oldest request first
FR-FCFS (First ready, FCFS) [Rixner et al. ISCA 2000]
  Goal: maximize row buffer hit rate  maximize DRAM throughput
  Row hit first
  Oldest first
FCFS
FR-FCFS
(Row 0, Col 0)
(Row 1, Col 10)
(Row 0, Col 1)
(Row 0, Col 0)
(Row 0, Col 1)
(Row 1, Col 10)

## Slide 12: Memory Optimizations
Graphics memory (GDRAM):
  Based on SDRAM for high bandwidth demands of GPU
  Achieve 2~5 X bandwidth per DRAM vs. DDR3
    Wider interfaces: 32 bits vs. 16 bits
    Higher clock rate: connected directly to GPU and attached to board via soldering instead of socketted DIMM modules
Reducing power in SDRAMs:
  Lower voltage (to 1.35 ~ 1.5 V)
  Use multiple banks (only the row in a single bank is read)
  Power down mode (ignores clock, continues to refresh)

## Slide 13: Flash Memory
A type of EEPROM (Electronically Erasable Programmable Read-Only Memory)
Must be erased (in blocks) before being overwritten
Static and non-volatile, drawing lower power when not reading or writing
Limited number of write cycles (~100,000 times)  wear levering
Cheaper than SDRAM, more expensive than disk
Slower than SRAM, faster than disk
Future: a replacement for hard disks and an intermediate storage between DRAM and disk

## Slide 14: Memory Dependability
Memory is susceptible to cosmic rays
Soft errors: dynamic errors
  Changes to a cell’s contents, not circuitry
  Detected and fixed by error correcting codes (ECC)
Hard errors: permanent errors
  May be due to manufacturing defects
  Use sparse rows to replace defective rows

## Slide 15: Outline
Memory technology and optimizations (Sec. 2.3)
Protection: virtual memory and virtual machines (Sec. 2.4)

## Slide 16: Virtual Memory
As a part of memory hierarchy
  Separation of logical memory from physical memory
    Virtual address: generated by CPU, seen by compiler and linker
    Physical address: seen by the memory
  Allow only a part of program in memory for execution logical address space can be much larger than physical
Serve to protect processes from each other
  Keeps processes in their own memory space
  Yet allow memory spaces to be shared among processes

## Slide 17: Virtual Memory Design
How is virtual memory different from caches?
  What controls replacement?
  Size (transfer unit, mapping mechanisms)
Review: four questions for virtual memory:
  Q1: Where can a block be places in the upper level?
  Q2: How is a block found if it is in the upper level?
  Q3: Which block should be replaced on a miss?
  Q4: What happens on a write?
Notes: Q1: Where can a block be places in the upper level? fully associative, set associative (?), direct mapped (?)
Q2: How is a block found if it is in the upper level? tag/block, page table
Q3: Which block should be replaced on a miss? LRU, random (?)
Q4: What happens on a write? write back, write through (?)

## Slide 18: Implementation of Virtual Memory
Architecture must:
  Provide restartable (or resumable) instructions
    Must resume program after recovering from a page fault
  Mark a page not present and raise a page fault when referencing such a page
  Have status bits per page
    R (referenced): for use by replacement algorithm
    M (modified): to determine when page is dirty
OS maintains
  Page table for user process, page frame table, free page list
  Pages evicted using a replacement policy, e.g. random, LRU
  If M-bit is clear, needn’t copy page back to disk  write back

## Slide 19: Protection by Virtual Memory
OS & architecture work together to provide protection
Role of architecture for VM protection:
  Provide user mode and supervisor mode
  Provide a portion of CPU state that a user process can use but not write, e.g., user/supervisor mode bit, exception enable/disable bit, memory protection information, etc.
  Provide mechanisms for switching between user mode and supervisor mode, e.g., system calls
  Provide mechanisms to limit memory accesses
  Provide protection restrictions to each page, e.g. read-only
  Provide TLB for fast translation of addresses

## Slide 20: Privileged Mode for Protection
Supervisor mode or kernel mode
In unprivileged mode (user mode)
  Can only access memory in range [B, B+L-1]
  Cannot access B and L, and I/O devices
Relocation registers and I/O devices are privileged resources
In privileged mode a process can access everything
  Can access privileged registers, all of memory
  Can access system tables, e.g. load B and L for other processes, allocate and deallocate memory segments, access I/O devices

## Slide 21: Switching between Modes
Enter kernel mode only by system calls
  Call gates
  x86 INT #<int number>
Atomically change
  Control flow (PC)
  Addressing environment
  Usually requires a special instruction for both entry and return
Services must be completely trusted
All
Memory
User
LNS
User Mode
Privileged Mode
User
Code
Service
1
Service
2
Service
3
Gates

## Slide 22: Fast Address Translation
How often address translation occurs?
Where the page table is kept?
Keep translation in the hardware
Use Translation Lookaside Buffer (TLB)
  Instruction-TLB and Data-TLB
  Essentially a cache (tag array = VPN, data array=PPN)
  Small (32 to 256 entries are typical)
  Typically fully associative (using a content addressable memory, CAM) or highly associative to minimize conflicts
  Include process ID or be flushed on each process switch or system call
  Referenced and modified bits are copied back on changes
Notes: VM means every memory access takes at least twice as long, one access to obtain physical address and a second to get data

## Slide 23: Protection via Virtual Machines
Support isolation and security
  First developed in the late 1960s
Focus on virtual machines that provide a complete system-level environment at the binary ISA level
  Particularly on virtual machines that support same ISA as the underlying hardware  system virtual machine (SVM)
  e.g., IBM VM/370, VMware ESX, Xen
  Present the illusion that the user has the entire computer, including a copy of OS
Other benefits of virtual machines:
  Managing software: run programs on own OS releases
  Managing hardware: migration

## Slide 24: Virtual Machines
The software that supports VMs is called virtual machine monitor (VMM) or hypervisor
  Individual virtual machines run under the monitor are called guest VMs
  The underlying hardware, whose resources are shared by guest VMs, is called the host
VMM determines how to map virtual resources to physical resources
  Time-shared, partitioned, emulated in software
Processor virtualization cost depends on workload
  User-level processor-bound (SPEC CPU2006) vs. I/O-intensive

## Slide 25: Requirements of VMM
Present a software interface to guest software
Isolate the state of guests from each other
Protect itself from guest software
Must control everything on the computer system, even with guest VM and OS temporarily using them
Be at a higher privilege level than guest VMs
  If a guest OS attempts to access or modify information related to hardware resources via a privileged instruction, it will trap to the VMM; VMM can intercept and support a virtual version of the sensitive information as the guest OS expects

## Slide 26: Impact of VMs on Virtual Memory
Virtualization of memory:
Each guest OS maintains its own set of page tables
  VMM adds a level of memory between physical and virtual memory called “real memory”
  VMM maintains shadow page table that maps guest virtual addresses to physical addresses
    Requires VMM to detect guest’s changes to its own page table
    Occurs naturally if accessing the page table pointer is a privileged operation
Virtualization of I/O

## Slide 27: Summary
Memory technology and optimizations
  DRAM
Protection: virtual memory and virtual machines
  Virtual memory
  Virtual machine
Have you
  Understood the technology inside the memory chips and other innovative, internal organizations
  Understood how virtual memory and virtual machines provide protections to a computer system