## Slide 1: CS5100 Advanced Computer Architecture Dynamic Scheduling
Prof. Chung-Ta King
Department of Computer Science
National Tsing Hua University, Taiwan
(Slides are from textbook, Prof. Hsien-Hsin Lee, Prof. Yasun Hsu)

## Slide 2: About This Lecture
1
Goal:
  To understand the basic concepts of dynamic scheduling and the Tomasulo algorithm
Outline:
  Overcoming data hazards with dynamic scheduling (Sec. 3.4)
  Dynamic scheduling: examples and algorithm (Sec. 3.5)

## Slide 3: Maximum ILP
What make a sequence of code to have the highest ILP?
Data dependence
Control dependence
Can a compiler give you such code?
Notes: No name dependences; true dependences do not cause hazards; a lot of independent instructions to fill in the available execution slots
Control dependences: always know where to jump so that instructions form a stream

## Slide 4: Compiler Has Its Limitations
Even though compiler can see a lot of ILP, it still outputs sequential code for conventional processors (next page)
  Many ILP lost in code generation
Code targeting one processor may not be optimized for another with a different microarchitecture
A lot of information unavailable at compile time, e.g. branch direction and target, pointer addresses, …

## Slide 5: Compiler Sees Data Flow Graph (DFG)
i1: r2 = 4(r22)
i2: r10 = 4(r25)
i3: r10 = r2 + r10
i4: 4(r26) = r10
i5: r14 = 8(r27)
i6: r6 = (r22)
i7: r5 = (r23)
i8: r5 = r6 – r5
i9: r4 = r14 * r5
i10: r15 = 12(r27)
i11: r7 = 4(r22)
i12: r8 = 4(r23)
i13: r8 = r7 – r8
i14: r8 = r15* r8
i15: r8 = r4 – r8
i16: (r28) = r8
i1
i2
i3
i4
i6
i7
i8
i5
i9
i11
i12
i13
i10
i14
i15
i16
Data Flow Graph (DFG)
(Data Dependency Graph)
Code generation
Fired
Notes: With DFG, an instruction can be executed (fired) immediately after
All source operands are ready
Execution unit available
Destination is ready (to be written)

## Slide 6: If Processor Just Follows the Code
In-order execution:
  Instructions executed in the order defined by the program/compiler  simple hardware
  A long (perhaps unexpected) latency may block ready instructions from executing: DIVD F0,F2,F4 ; multicycle instruction ADDD F10,F0,F8 ; stalled SUBD F12,F8,F14 ; independent of above
  It happens just because the compiler decides to put SUBD behind ADDD at code generation
Need to be out-of-order execution:
  Processor uncovers DFG from the code sequence itself

## Slide 7: Out-of-Order Execution
i1
i2
i3
i4
i6
i7
i8
i5
i9
i11
i12
i13
i10
i14
i15
i16
i1: r2 = 4(r22)
i2: r10 = 4(r25)
i3: r10 = r2 + r10
i4: 4(r26) = r10
i5: r14 = 8(r27)
i6: r6 = (r22)
i7: r5 = (r23)
i8: r5 = r6 – r5
i9: r4 = r14 * r5
i10: r15 = 12(r27)
i11: r7 = 4(r22)
i12: r8 = 4(r23)
i13: r8 = r7 – r8
i14: r8 = r15* r8
i15: r8 = r4 – r8
i16: (r28) = r8

## Slide 8: Dynamic Scheduling
Exploit ILP at run-time
  Execute instructions out-of-order by a restricted data flow execution model (still use PC!)
Hardware will
  Maintain true dependency (data flow manner)
  Maintain exception behavior
  Find ILP within an instruction window (pool)
    Need an accurate branch predictor
Hardware can also eliminate name dependency by renaming

## Slide 9: Dynamic Scheduling
Pros
  Cope with variable latency at run time, e.g. cache misses
  Compiler does not need to have knowledge of microarchitecture:
    Avoid recompiling old binaries
    Avoid bottleneck of small named register sets
  Handle cases where dependency is unknown at compile-time
Cons
  Hardware complexity (main argument from the VLIW/EPIC camp)
  Complicates exceptions

## Slide 10: Out-of-Order (OOO) Execution
OOO execution  out-of-order completion
  Begin execution as soon as operands are available
  Complete execution as soon as output operand generated
OOO execution  out-of-order retirement (commitment, write result)
  Machine state is not changed until instruction commits
  No (speculative) instructions are allowed to retire until they are confirmed to be on the right path
Fetch, decode, issue (i.e. front-end) are still done in the program order

## Slide 11: Dynamic Scheduling by Tomasulo Algo.
Two techniques in one:
  Dynamic scheduling for out-of-order execution
  Register renaming to avoid WAR and WAW hazards
Developed by Robert Tomasulo at IBM in 1967
First implemented in the IBM System/360 Model 91’s floating point unit
IBM System/360 introduced
  8-bit = 1 byte
  32-bit = 1 word
  Byte-addressable memory
  Differentiate an “architecture” from an “implementation”

## Slide 12: Problems with IBM 360/91 ISA
2 register specifiers/instruction in IBM 360
  e.g. MULTD F2, F0 // F2  F2  F0
  Make WAW and WAR much worse
4 FP registers in IBM 360 ISA
  Instructions can only see and use 4 FP registers  architecture visible registers
  Make compiler difficult to allocate registers, e.g. need to reuse registers, creating name dependences
Memory-to-register and FP operations
  Long and variable instruction execution time

## Slide 13: Motivation for Tomasulo Algorithm
Cope with only 4 FP registers
  Use more internal, architecture invisible registers (virtual registers) to break name dependences  reg. renaming
High FP performance without specialized compilers
  Hardware detects data dependences via registers used
  Hardware schedules instruction execution following DFG
Overcome long memory and FP delays
  OOO execution to allow instruction execution overlapped
Support execution of multiple iterations of a loop
  Even if loop branches can be predicted perfectly, still need to handle name dependence across iterations

## Slide 14: Key Features of Tomasulo Algorithm
Each functional unit is associated with a number of reservation stations (RS)
  A RS controls the execution of one instruction that is going to use that FU, by tracking availability of its operands
    Contains the instruction, buffered operand values (when available), RS # of instruction providing the operand
    Instruction register specifiers are renamed with the RS tag  register renaming
  RS copies operands to its buffer when they are available  buffer+id: serves as virtual registers for reg. renaming
  When all operands are ready, instruction is fired to FU
  Hazard detection and interlocks are distributed to FUs
DFG

## Slide 15: Key Features of Tomasulo Algorithm
Results of FUs broadcasted directly to RSs over Common Data Bus (CDB), not through registers
  RS fetches and buffers an operand thru CDB as soon as it becomes available (not necessarily through register file)  similar to internal forwarding/bypass
  Do not change machine state
Register status table to track last RS to write the reg.
  Due to in-order issue, there is no WAW hazard
Structural hazards checked at issue stage
  If RSs are available, then allocate one RS to issue
Load and store units treated as FU with RS
Integer instructions can past branches, via prediction

## Slide 16: IBM 360/91 FPU w/ Tomasulo Algorithm
From Mem
FP Registers (FLR)
Reservation
Stations
Common Data Bus (CDB)
To Mem
FP operation stack (FLOS)
FP Load Buffers (FLB)
Store Data
Buffers
(SDB)
6
5
4
3
2
1
FP Adder
FP Mult/Div
3
2
1
2
1
architecture visible
Notes: Compare with traditional pipeline: pipeline registers vs reservation stations

## Slide 17: 3 Stages of Tomasulo Algorithm
Issue: get an instruction from instruction queue
  Issue if there is an empty RS
  Send operands to RS if in registers  register renaming, structural hazard detect
Execute:
  If operands unavailable, monitor CDB (common data bus)
  else, place operand into RS  internal forwarding
  When all operands are ready, execute the instruction
  Loads and store maintained in program order through effective address
  No instruction allowed to execute until all branches that proceed it in program order have completed

## Slide 18: 3 Stages of Tomasulo Algorithm
Write result:
  Write result on CDB, then to register (change machine state)
    No checking for WAW and WAR (eliminated with renaming); no need for dependent instructions to wait at register file (they wait at RS via internal forward through CDB)
  Load/store is treated as a functional unit
    Stores must wait until address and value are received

## Slide 19: Structure of Reservation Stations
Each reservation station has 6 fields:
  Op: the operation to perform in the unit
  Vj, Vk: value of the source operands
  Qj, Qk: tag of the RS to produce source operands
  Busy: the RS and associated FU being busy
Each register and store buffer has one field:
  Qi: tag of the RS containing the operation that will write to it; blank meaning register value available
Load and store buffers each require a busy field
Store buffer also has a field V, which holds the value to be stored to the memory

## Slide 20: Tomasulo Algorithm Loop Example
Loop: LD F0 0 R1
MULTD F4 F0 F2
SD F4 0 R1
SUBI R1 R1 #8
BNEZ R1 Loop
Assume multiply takes 4 cycles
Assume 1st load takes 8 cycles (cache miss?), 2nd load 4 cycles
Assume branches are taken
  More WAW and WAR across iterations
Need dynamic memory disambiguation to reorder load/store
  Check addresses in store buffer to detect dependences through memory
p. 179 of textbook (5/e):
Loop: L.D F0, 0(R1)
MUL.D F4, F0, F2
S.D F4, 0(R1)
DADDIU R1, R1, -8
BNE R1, R2, Loop
LD F0, 0(R1)
MULD F4, F0, F2
SD F4, 0(R1)
LD F0, 0(R1)
MULD F4, F0, F2
SD F4, 0(R1)

## Slide 21: Loop Example Cycle 0
Value of register used for address and iteration control, if branches are predicted to be taken

## Slide 22: Loop Example Cycle 1
LD 80:
cache miss

## Slide 23: Loop Example Cycle 2
Original: F2 is not freed until LD and MULT both finished
Tag “Load1” helps track flow dependence

## Slide 24: Loop Example Cycle 3

## Slide 25: Loop Example Cycle 4
Dispatching SUBI instruction (not in FP queue) to INT FU

## Slide 26: Loop Example Cycle 5
BNEZ (not in FP queue) with branch prediction

## Slide 27: Loop Example Cycle 6
F0 never sees Load1 result; WAW eliminated!
Why does it not cause any problem?
WAW
LD can be issued after checking store buffer to ensure no dependence

## Slide 28: Loop Example Cycle 7
1st & 2nd iteration overlapped; Why does SD not worry about F4 being destroyed?
WAR across
iteration?

## Slide 29: Loop Example Cycle 8
Does SD need to check load buffer to ensure no dependence?

## Slide 30: Loop Example Cycle 9
Load1 completing: what is waiting for it? Issuing 2nd SUBI

## Slide 31: Loop Example Cycle 10
Load2 completing: what is waiting for it? Issuing 2nd BNEZ
Got value from CDB

## Slide 32: Loop Example Cycle 11
Next load in 3rd iteration after checking store buffer

## Slide 33: Loop Example Cycle 12
Why not issue third multiply?
stall

## Slide 34: Loop Example Cycle 13
Why not issue third store?
Notes: In order issue

## Slide 35: Loop Example Cycle 14
Mult1 completing: what is waiting for it?

## Slide 36: Loop Example Cycle 15
Mult2 completing; what is waiting for it?
via CDB

## Slide 37: Loop Example Cycle 16
(3rd multiply)
via CDB

## Slide 38: Loop Example Cycle 17

## Slide 39: Loop Example Cycle 18

## Slide 40: Loop Example Cycle 19
19

## Slide 41: Loop Example Cycle 20
19
20
20
No WAR
In-order issue, OOO execution, completion, commitment

## Slide 42: Dependences through Memory in LD/ST
2 step process for both LD & ST:
  1st step: Calculate effective address and place into separate L or S buffers in program order
  2nd step: Access memory unit and the rest
    ST can update memory when it reaches write-result stage and whenever data is available
    Order between ST and LD can be OOO and cause hazard
Hazard detection (dynamic mem. disambiguation)
  LD: Check its address with addresses in store buffers; if match, delay sending LD to load buffer until store is done
  ST: Same as LD but check both load and store buffers (to avoid that the 2nd store may move ahead of the 1st store if they are to the same address)

## Slide 43: Load Bypassing and Load Forwarding
Bypassing: when load address does not match addresses of preceding stores, load is allowed to move ahead of these stores in the store buffer
Forwarding: If load address matches address of a store, to-be-stored data can be forwarded to load (RAW)
  If multiple preceding stores in store buffer that alias with the load, must determine which store is the most recent
  To avoid port contention, an additional read port is needed in the store buffer to forward data to load. The original read port is used to transfer data to data cache

## Slide 44: Summary of Tomasulo Algorithm
Distributed hazard detect and execute control:
  Distributed RSs; depends on RS availability not FU
  CDB broadcasts operands and releases multiple pending instructions (through associative tag matching)
    Internal forwarding without going through registers
Eliminate WAR and WAW  no need to check
  Register renaming through RSs
  Copy operands into RS when available  no WAR
  Last of successive writes actually write to reg.  no WAW
Load and store units are treated as FUs
Build data flow graph on the fly
Complex H/W for control, associative store, BCD