## Slide 1: Logic Representations

## Slide 2: Basic Definitions
- Let B = {0,1} Y = {0,1,2}
A logic function f in n inputs x1, x2, ...xn and
m outputs y1,y2, ...ym is a mapping.
f : Bn
Ym
- For each component fi, i = 1,2, ...,m, define
ON_SET:the set of input values x such that fi(x) =1
OFF_SET:the set of input values x such that fi(x) = 0
DC_SET:the set of input values x such that fi(x) = 2
- Completely specified function : DC_SET = f
Incompletely specified function : DC_SET
f
- m=1 => a single output function
m>1 => a multiple output function

## Slide 3: Representations
1. Truth Table
Full adder
X Y Cin Sum Cout
0 0 0 0 0
0 0 1 1 0
0 1 0 1 0
0 1 1 0 1
1 0 0 1 0
1 0 1 0 1
1 1 0 0 1
1 1 1 1 1
Multiple output function
Sum : on-set = {(0 0 1), (0 1 0), (1 0 0),
(1 1 1)}
off-set= {(0 0 0), (0 1 1), (1 0 1),
(1 1 0)}
Completely specified function

## Slide 4: Representations
2. Geometrical representation
  1 variable
0
1
  2 variables
00
01
10
11
3 variables
000
100
110
111
011
001
101
010
010
sum : on-set ={(0 0 1),(0 1 0),(1 0 0),(1 1 1)}
off-set ={(0 1 1),(1 0 1),(1 1 0),(0 0 0)}

## Slide 5: Representations
3. Algebraic representations
Canonical sum of product (list of minterms)
Reduced sum of product (two-level)
Cout = x’yCin + xy’Cin + xyCin’ + xyCin
Cout = yCin + xCin + xy
= yCin + xCin + xyCin’
Multi-level representation
Cout = Cin (x + y) + xy
    - List of cubes (Sum of Products (SOP), Disjunctive Normal Form (DNF))
    - List of conjuncts (Product of Sums (POS), Conjunctive Normal Form (CNF))

## Slide 6: 4. Reduced Ordered Binary Decision Diagrams

## Slide 7: Binary Decision Diagram
Vertex represents decision
Follow dashed line for value 0
Follow solid line for value 1
Function value determined by leaf value
Truth Table
Decision Tree
X1
X2
X2
X3
X3
X3
X3
0
0
0
1
0
1
0
1

## Slide 8: Reduced Ordered Binary Decision Diagram (ROBDD)
Binary decision graph:
f = x2x3 + x1x3
- Terminal node:
attribute
value (v) = 0
value (v) = 1
- Nonterminal node:
index (v) = i, i= 1~3
two children
low (v)
high (v)
- Evaluate an input vector
X1
X2
X2
X3
X3
X3
X3
0
0
0
1
0
1
0
1

## Slide 9: ROBDD
A BDD graph which has a vertex v as root
corresponds to the function Fv :
(1) If v is a terminal node:
a) if value (v) is 1, then Fv = 1
b) if value (v) is 0, then Fv = 0
(2) If F is a nonterminal node (with index(v) = i)
Fv(xi , ...xn) = xi’ Flow(v) (xi+1 , ...xn) +
xi Fhigh(v) (xi+1 , ...xn)
Shannon expansion

## Slide 10: Variable Ordering
Assign arbitrary total ordering to variable
e.g. X1 < X2 < X3
Variable must appear in ascending order along all paths
Properties
  No conflicting variable assignments along path
  Simplifies manipulation
X1
X2
X3
X1
X3
X3
X2
X1
X1
X3
OK
Not
OK

## Slide 11: Reduced OBDD
Reduced OBDD :
No distinct vertices v and w such that
subgraphs rooted by v and w are
isomorphism.
2. No vertex v with low (v) = high (v)

## Slide 12: Reduction Rule #1
Merge equivalent leaves
X1
X2
X2
X3
X3
X3
X3
0
0
0
1
0
1
0
1
X1
X2
X2
X3
X3
X3
X3
0
1
a
a
a

## Slide 13: Reduction Rule #2
Merge isomorphic nodes
X1
X2
X2
X3
X3
X3
X3
0
1
X1
X2
X2
X3
X3
0
1
X
X
Y
Z
X
Y
Z

## Slide 14: Reduction Rule #3
Eliminate redundant node
X1
X2
X2
X3
X3
0
1
X1
X2
X3
0
1
X
Y
Y
X2

## Slide 15: Reduction Rule #3
Eliminate redundant node
X1
X2
X2
X3
X3
0
1
X1
X2
X3
0
1
X
Y
Y

## Slide 16: ROBDD
After reduce
X1
X2
X3
0
1

## Slide 17: Implementation of Reduce
Visit OBDD bottom up and label each vertex with an identifier
Redundancy
  if id( low(v) ) = id( high(v) ), then vertex v is redundant
   set id(v) = id( low(v) )
  if index (v) = index(u) and id( low(v) ) = id( low(u) ) and id( high(v) ) = id( high(u) ), then set id(v) = id(u)
A different identifier is given to each vertex at level i
An ROBDD is identified by a subset of vertices with different identifiers

## Slide 18: Reduce
index=1
index=2
index=3
: 1
: 0
a
b
b
c
c
0
0
1
0
1
(a)
1
2
3
4
5
0
0
1
0
1
id=1
id=1
id=2
id=1
id=2
id=3
id=3
id=4
id=3
id=5
1
2
4
0
1
id=1
id=2
id=3
id=4
id=5
(b)
(c)

## Slide 19: Construct ROBDD Using Hash Table
Using a hash table called unique table
  Contain a key for each vertex of an OBDD
  Key : (variable, right child, left child)
  Each key uniquely identify the specific function
  Look up the table can determine if another vertex in the table implements the same function

## Slide 20: The Unique Table – Hash Table
Unique table : hash table mapping (Xi, G, H) into a node in the DAG
  before adding a node to the DAG, check if it already exists
  avoids creating two nodes with the same function
  constructed bottom up
  terminated when root is reached
  canonical form : pointer equality determines function equality
Hash Table Mapping
(X1, T1, 1 ) --> U1
(X1, T2, T1) --> U2
(X2, T3, 1 ) --> T1
(X2, 0 , T3) --> T2
(X3, 0 , 1 ) --> T3
X1
X2
X3
U2
X2
0
0
1
1
X1
1
U1
T1
T2
T3
true
false

## Slide 21: ROBDD Using Unique Table
a
b
c
0
1
id=1
id=2
id=3
id=4
id=5
f = (a+b) c
variable order (a, b, c)
Unique table
Key

## Slide 22: Multi-Rooted ROBDD
a
b
c
0
1
id=1
id=2
id=3
id=4
id=5
d
id=6
f = (a+b) c
g = b c d
variable order (d, a, b, c)
f is constructed first and is associated with id=5
g : id=6
Unique table
Key

## Slide 23: Ordering Effects
Ordered BDD: if x < y, then all nodes representing x precede all nodes representing y
Given an ordering of variables, reduced OBDD is canonical

## Slide 24: Example of a Good Ordering
The size of OBDD depends on the ordering of
variables
ex : x1x2 + x3x4
x1 < x2 < x3 < x4
x1
x2
x3
x4
0
1
0
1
0
1
0
1
0
1

## Slide 25: Example of a Less Good Ordering
x1
x3
x3
x2
x4
0
1
0
1
0
1
0
1
0
1
0
1
0
1
x2
x1 < x3 < x2 < x4
For a good ordering, the size of an OBDD
remains reasonably small
Multiplier is an exception

## Slide 26: Which Ordering is Better?
Let x3 x2 x1 x0 and y3 y2 y1 y0 be two binary numbers and carry-out3 the carry out of the most significant bit.
Two ordering :
x3 < x2 < x1 < x0 < y3 < y2 < y1 < y0
x3 < y3 < x2 < y2 < x1 < y1 < x0 < y0
Which ordering will result in smaller size and why?

## Slide 27: Sample Function Classes
General Experience
  Many tasks have reasonable ROBDD representations
  Algorithms remain practical for up to 100,000 vertex ROBDD
  Heuristic ordering methods generally satisfactory

## Slide 28: Operations on ROBDD
Apply f1 <op> f2
(f1, f2 must have the same ordering of variables,
then operations can be operated on f1, f2 )
0
1
0
1
1
x1
x1
x1
f1
f2
g1
g2
g3
g4
g1g3
g2g4
f1 f2
f1 f2 = (x1’g1 + x1g2)(x1’g3 + x1g4)
= x1’g1g3 + x1g2g4
= x1’(g1g3) + x1(g2g4)
f1 + f2
f1 f2
etc.
0

## Slide 29: ROBDD
complement : f
1
f1
f2 : f1’ + f1f2 (implication)
time complexity
Reduced O(
G
log
G
)
Apply O(
G1
G2
)

## Slide 30: Generating ROBDD from Network
Represent output functions of gate network as ROBDDs
0
1
a
0
1
b
0
1
c
0
1
b
a
0
1
c
b
0
1
c
b
b
a
A
B
C
T1
T2
Out
A new_var(“a”)
B new_var(“b”)
C new_var(“c”)
T1 AND(A, B)
T2 AND(B, C)
Out OR(T1, T2)
Evaluation
Network

## Slide 31: Property of ROBDD
(1) Commonly encountered functions have
reasonable representations.(except
multiplier)
(2) Complementation will not blow up the
representation.
(3) Canonical form so that equivalence,
satisfiability checking can be done easily.
(4) Multi-level representation
Achille’s heel function:
F = x1x2x3 + x4x5x6 + ……+ x3n-2x3n-1x3n
F’ has 3n terms

## Slide 32: 5. And-Inverter Graphs (AIGs)

## Slide 33: And-Inverter Graph
5. And-Inverter Graph (AIG)
  Simple structure
  And-Gates as nodes (shown as circles) with two inputs as edges (shown as arrows)
  Inverter edges marked with a dot
  Used in ABC

## Slide 34: Example
Ex: y = f( x1,x2,x3) =( (x1 ‧ x2 )’ ‧ (x2 ‧ x3)’)’
= ( x1 ‧ x2 ) ＋ (x2 ‧ x3)

## Slide 35: AIG Construction
  Start from SOP representation
  Convert to AIG using DeMorgan’s law
  x1 ＋ x2 = ( x1 ＋ x2) ’’= ( x1 ’ ‧ x2 ’) ’
2-input and
2-input nand
3-input and
2-input or

## Slide 36: AIG Attributes
  Size is the number of AND nodes in it
  Logic level is the number of AND-gates on the longest path from the primary inputs (PIs) to the primary outputs (POs)
  The inverters are ignored
6 nodes, 4 levels

## Slide 37: AIG Canonicity
AIGs are not canonical
  ROBDDs are canonical
  Same function represented by two functionally equivalent AIGs with different structures
  Different structures can still be optimal with different objectives

## Slide 38: AIG Canonicity
6 nodes, 4 levels => area optimal
7 nodes, 3 levels => speed (delay) optimal

## Slide 39: 6. Reed-Muller Form

## Slide 40: Representation
Reed-Muller Expression (with AND, XOR and 1)
Algebraic Normal Form (ANF)
Use un-complemented literals only
The above is called the Positive Polarity RM (PPRM), which is canonical (unique) for the given function
when are exclusive

## Slide 41: Example
f(x1, x2) = f(0, 0)x1’x2’ + f(0, 1)x1’x2 + f(1, 0)x1x2’
+ f(1, 1)x1x2
=f(0, 0)x1’x2’  f(0, 1)x1’x2  f(1, 0)x1x2’
 f(1, 1)x1x2
=f(0, 0)(x11)(x21) 
f(0, 1)(x11)x2 
f(1, 0)x1(x21) 
f(1, 1)x1x2
=f(0, 0)(x1x2x1x21) 
f(0, 1)(x1x2x2) 
f(1, 0)(x1x2x1) 
f(1, 1)x1x2
=f(0, 0) 
( )x1 
( )x2 
( )x1x2
f(0,0)f(1,0)
f(0,0)f(0,1)
f(0,0)f(0,1)f(1,0) f(1,1)

## Slide 42: Characteristic Functions

## Slide 43: Characteristic Function
Let be a set and
The characteristic function is the function
A
E
Ex:

## Slide 44: Characteristic Function
Given a Boolean function
the mapping relation denoted as
is defined as
The characteristic function of a function is defined for s.t. iff

## Slide 45: Characteristic Function
Ex:
x1 x2 y
0 0 0
0 1 1
1 0 1
1 1 1
x1 x2 y F
0 0 0 1 v
0 0 1 0
0 1 0 0
0 1 1 1 v
1 0 0 0
1 0 1 1 v
1 1 0 0
1 1 1 1 v

## Slide 46: Operations on Logic Functions

## Slide 47: Operation on Logic Function
Complement
Intersection
Union
Difference
XOR
F is a tautology
Cofactor
Boolean difference
Consensus operator
Smoothing operator

## Slide 48: Cofactor
Cofactor operation ( restriction )
cofactor of f with respect to xi=0
cofactor of f with respect to xi=1
Cofactor is a new function independent of xi

## Slide 49: Cofator
Cofactor with respect to any cube
Ex:

## Slide 50: Shannon Expansion

## Slide 51: Boolean Difference
is called Boolean difference of with respect to
is sensitive to the value of when
Ex:
Application: Test pattern generation

## Slide 52: Consensus Operator
evaluate f to be true for x=1 and x=0
Ex:
Universal quantification of function w.r.t. variable x

## Slide 53: Smoothing Operator
evaluate f to be true for x=1 or x=0
Ex:
Existential quantification of function w.r.t. variable x
Application: Image computation of sequential circuits