## Slide 1: CSC6032 – Advanced Operating Systems
Prof. Yeh-Ching Chung
School of Data Science
Chinese University of Hong Kong, Shenzhen

## Slide 2: Outline
Overview
  Background knowledge of I/O subsystem
  Introduction to I/O virtualization
Device Model
Optimization: Virt-I/O
  Introduction to Virt-IO
  Architecture of Virt-IO
  Important Operations
Hardware Assistant

## Slide 3: Background knowledge of I/O subsystem

## Slide 4: IO Virtualization
Goal
  Share or create I/O devices for virtual machines.
Two types of IO subsystem architecture :
  Port Mapped IO (PMIO)
    Port-mapped IO uses a special class of CPU instructions specifically for performing IO.
  Memory Mapped IO (MMIO)
    Memory Mapped IO uses the same address bus to address both memory and IO devices, and the CPU instructions used to access the memory are also used for accessing devices.
Traditional IO techniques :
  Direct memory Access (DMA)
  PCI / PCI Express

## Slide 5: Port Mapped IO
IO devices are mapped into a separate address space
  IO devices have a separate address space from general memory, either accomplished by an extra “IO" pin on the CPU's physical interface, or an entire bus dedicated to IO.
  Generally found on Intel microprocessors, specifically the IN and OUT instructions which can read and write one to four bytes (outb, outw, outl) to an IO device.
Pros & Cons
  Pros
    Less logic is needed to decode a discrete address.
    Benefits for CPUs with limited addressing capability.
  Cons
    More instructions are required to accomplish the same task.
    IO addressing space size is not flexible.

## Slide 6: Memory Mapped IO
IO devices are mapped into the system memory map along with RAM and ROM.
  To access a hardware device, simply read or write to those 'special' addresses using the normal memory access instructions.
  Each I/O device monitors the CPU's address bus and responds to any CPU access of an address assigned to that device, connecting the data bus to the desired device's hardware register.
Pros & Cons
  Pros
    Instructions which can access memory can be used to operate an IO device.
    Operate on the data with fewer instructions.
  Cons
    Physical memory addressing space must be shared with IO devices.
    The entire address bus must be fully decoded for every device.

## Slide 7: Direct Memory Access
What is DMA
  DMA is a memory-to-device communication method that bypasses the CPU.
  Allow certain hardware subsystems within the computer to access system memory for reading and/or writing independently of the CPU.
Two types of DMA
  Synchronous DMA
    The DMA operation is caused by software.
    For example, sound card driver may trigger DMA operation to play music.
  Asynchronous DMA
    The DMA operation is caused by devices (hardware).
    For example, network card uses DMA operation to load data into memory and interrupts CPU for further manipulation.

## Slide 8: PCI & PCI Express
What is PCI
  PCI (Peripheral Component Interconnect) is a computer bus for attaching hardware devices.
  Typical PCI cards used include :
    Network cards, sound cards, modems
    Extra ports such as USB or serial, TV tuner cards and disk controllers.
What is PCI Express ?
  PCIe is a computer expansion card standard designed to replace the older PCI, PCI-X, and AGP standards.
  Its topology is based on point-to-point serial links, rather than a shared parallel bus architecture.

## Slide 9: PCI & PCI Express
PCI based system build in a tree topology
  PCI bus
    Parallel connect devices and bridges
  PCI-PCI Bridge
    Connect two PCI buses
    Become the root of lower bus
  PCI-ISA Bridge
    Connect to conventional ISA device

## Slide 10: PCI & PCI Express
PCIe based system build in a point to point architecture
  Root Complex
    Similar to a host bridge in a PCI system, the root complex generates transaction requests on behalf of the processor, which is interconnected through a local bus.
  Switch
    Connect endpoint devices or other switches
  Endpoint Device
    Physical PCIe devices
    Legacy PCI devices
  PCI Express Bridge
    Connect to other legacy subsystems

## Slide 11: I/O virtualization

## Slide 12: IO Virtualization
Implementation Layers
  System call
    The interface between applications and guest OS.
  Driver call
    The interface between guest OS and IO device drivers.
  IO operation
    The interface between IO device driver of guest OS and virtualized hardware ( in VMM ).

## Slide 13: IO Virtualization
In system call level :
  When an application invokes a system call, the system call will be trapped to VMM first.
  VMM intercepts system calls, and maintains shadowed IO system call routines to simulate functionalities.
  After simulation, the control goes back to the application in gust OS.

## Slide 14: IO Virtualization
In device driver call level
  Adopt the para-virtualization technique, which means the IO device driver in guest OS should be modified.
  The IO operation is invoked by means of hyper-call between the modified device driver and VMM IO component.

## Slide 15: IO Virtualization
In IO operation level
  Port mapped IO
    Special input/output instructions with special addresses.
    The IO instructions are privileged .
  Memory mapped IO
    Loads/stores to specific region of real memory are interpreted as command to devices.
    The memory mapped IO region is protected.
Due to the privileged nature, these IO operations will be trapped to the VMM.

## Slide 16: Device model

## Slide 17: Device Model
Focus on IO operation level implementation.
  This is an approach of full virtualization.
Logic relation between guest OS and VMM :
  VMM intercepts IO operations from guest OS.
  Pass these operations to device model on a running platform.
  Device model needs to emulate the IO operation interfaces.
    Port mapped IO
    Memory mapped IO
    DMA
    ... etc.

## Slide 18: Device Model
Two different implementations of device model
  Device model is implemented as part of VMM.
  Device model is running in user space as a stand alone service.
Type 1 Virtualization
Type 2 Virtualization

## Slide 19: Device Model
IO virtualization flow
  Initialization – device discovery
    VMM will make guest OS discover the virtualized IO devices.
    Then guest OS will load the corresponding device driver.
  Operation – access interception
    When guest OS executes IO operations, VMM will intercept those accesses.
    After virtual device operations, VMM returns the control to guest OS.
  Virtualization – device virtualization
    Device model should emulate the real electronic logic to satisfy all device interface definitions and their effects.
    VMM may share physical devices to all virtual machines.

## Slide 20: Device Discovery
Virtualize physical bus devices
  Non-enumerable physical devices
    These devices have their own hard-coded numbers.
    VMM should setup some status information on the virtual device ports.
    For example, PS/2 keyboard and mouse.
  Enumerable physical devices
    These devices define a complete device discover method.
    VMM have to emulate not only the devices themselves, but the bus behavior.
    For example, PCI or PCI express devices.
Virtualize non-exist devices
  VMM must define and emulate all functions of these devices
    VMM may define them as either non-enumerable or enumerable devices.
    Guest OS needs to load some new drivers of these virtual devices.

## Slide 21: Access Interception (1)
After virtual devices discovered by guest OS, VMM has to intercept and control all the IO operations from guest OS.
Port mapped IO operation
  Direct device assignment
    VMM should turn ON the physical IO bitmap.
    All the IO instructions (IN/OUT) from guest OS will be directly performed onto hardware without VMM intervention.
  Indirect device assignment
    VMM should turn OFF the physical IO bitmap.
    All the IO instructions from guest OS will be intercepted by VMM and forward to physical hardware.

## Slide 22: Access Interception (2)
Memory mapped IO operation
  Direct device assignment
    VMM should use the shadow page table to map IO device addressing space of guest OS to the space of host.
    Then all the IO operations from guest OS will not be intercepted.
  Indirect device assignment
    VMM should make the all entries of the IO device addressing space in the shadow page table to be invalid.
    When guest OS accesses those addressing space, it will introduce the page fault which trap CPU to VMM for device emulation.
DMA mechanism
  Address remapping
    Because the device driver in the guest OS does not know the host physical address, VMM needs to remap the DMA target automatically when intercepting IO operations from guest OS.

## Slide 23: Device Virtualization (1)
IO device types
  Dedicated device
    Ex : displayer, mouse, keyboard …etc.
  Partitioned device
    Ex : disk, tape …etc
  Shared device
    Ex : network card, graphic card …etc.
  Nonexistent physical device
    Ex : virtual device, etc.

## Slide 24: Device Virtualization (2)
Dedicated device
  Do not need to be virtualized.
  In theory, requests of such device could bypass the VMM.
  However, they are handled by the VMM first since OS is running in user mode.
Partitioned device
  Partitioned into several smaller virtual devices as dedicated to VMs.
  VMM translates address spaces to those of the physical devices.

## Slide 25: Device Virtualization (3)
Shared device
  Should be shared among VMs.
  Each VM has its own virtual device state.
  VMM translates a request from a VM to a physical device .
Nonexistent physical device
  Virtual device “attached” to a VM for which there is no corresponding physical device.
  VMM intercepts requests from a VM, buffers them and interrupts other VMs.

## Slide 26: Performance Issues
When considering performance, two major issues :
  How to make guest OS directly access IO addresses ?
    Other than software approaches discussed above, we can make use of the hardware assistance (Intel EPT technique in memory virtualization) to map IO addresses from host to guest directly without software overhead.
  How to make DMA directly access memory space in guest OS ?
    For the synchronous DMA operation, guest OS will be able to assign the correct host physical memory address by EPT technique.
    For the asynchronous DMA operation, hardware must access memory from host OS which will introduce the VMM intervention.

## Slide 27: optimization: virt-io

## Slide 28: Overview
Device Emulation Environment
Full virtualization
Para-virtualization

## Slide 29: What is virtio
Virtio is a Linux IO virtualization standard for network and disk device drivers and cooperates with the hypervisor.
  It provides a set of APIs and structures for making virtio devices.
  The host implementation is in userspace - qemu, so no driver is needed in the host
  Only the guest's device drivers aware the virtual environment.
  This enables guests to get high performance network and disk operations, and gives most of the performance benefits of para-virtualization.

## Slide 30: Why it fast
A part of memory space (Virtqueue) are shared between guests and QEMU to accelerate the data accessing by each sides.
  Reduce the number of MMIOs.

## Slide 31: optimization: virt-io

## Slide 32: Architecture of Virt-IO
QEMU
Front-end driver
Back-end driver
Virtqueue
Virtio-buffer

## Slide 33: Driver
Front-end driver
  A kernel module in guest OS.
  Accepts I/O requests from user process.
  Transfer I/O requests to back-end driver.
Back-end driver
  A device in QEMU.
  Accepts I/O requests from front-end driver.
  Perform I/O operation via physical device.

## Slide 34: Transport
Virtual queue called virtqueue
  It is a part of memory of the guest.
  A channel between front-end and back-end.
  Implemented as rings called Vring to traverse the guest-to-hypervisor transition.
    Vring is a memory mapped region between QEMU & Guest
    Vring is the memory layout virtqueue
Virtio-buffer
  Buffer to put send/receive requests.
  Represented as a scatter-gather list.

## Slide 35: KVM without Virt-IO
Host
Guest Application
KVM
Hardware
QEMU
GUEST
Other
Processes
Driver
IO controller & device
Device driver
Host

## Slide 36: KVM with Virt-IO
KVM
Hardware
QEMU
GUEST1
Host
Other
Processes
Transport
VirtIO driver
VirtIO controller & device
Device driver

## Slide 37: optimization virt-io

## Slide 38: Virtqueue Initialization
Guest
QEMU
Virtio Driver
Virtio Device
Virtio PCI Controller
Virtio PCI Controller
Transport
Vring
Find virtqueue
Alloc Vring
Vring GPA

## Slide 39: Virtqueue Data Structure
QEMU
Guest
Virt queue Read
Vring
Virtio Driver
Virtio Device
Virt queue Write
Vring

## Slide 40: Data Exchange APIs
In guest
  virtqueue_add_buf
    Expose virtio-buffer to other end
  virtqueue_get_buf
    Get the results from virtqueue
  virtqueue_kick
    Update virtqueue after add_buf
    Notify QEMU to deal with the data
In QEMU
  virtqueue_pop
    Pop the data from virtqueue
  virtqueue_push
    Put data back to virtqueue

## Slide 41: Data Exchanging Flow (1)
QEMU
Guest
Virt queue Read
Vring
Virtio Driver
Virtio Device
Virt queue Write
Vring
Add Buf
In
Out
data

## Slide 42: Data Exchanging Flow (2)
QEMU
Guest
Virt queue Read
Vring
Virtio Driver
Virtio Device
Virt queue Write
Vring
Kick
In
Out
data

## Slide 43: Data Exchanging Flow (3)
QEMU
Guest
Virt queue Read
Vring
Virtio Driver
Virtio Device
Virt queue Write
Vring
In
Out
data
POP

## Slide 44: Data Exchanging Flow (4)
QEMU
Guest
Virt queue Read
Vring
Virtio Driver
Virtio Device
Virt queue Write
Vring
In
Out
data
Push

## Slide 45: Data Exchanging Flow (5)
QEMU
Guest
Virt queue Read
Vring
Virtio Driver
Virtio Device
Virt queue Write
Vring
In
Out
data
Get Buf

## Slide 46: Call Back APIs
In guest
  virtqueue_disable_cb
    Disable callbacks
    Need not necessarily synchronous
    Unreliable and only useful as an optimization
  virtqueue_enable_cb
    Restart callbacks after virtqueue_disable_cb

## Slide 47: Hardware assistant

## Slide 48: Software IO Virtualization
Software based sharing
  Implement virtualization by VMM software stack.
  Advantage
    Full virtualization without special hardware support.
  Disadvantage
    Significant CPU overhead may be required by the VMM.
    Software cannot make data access directly from devices.

## Slide 49: Hardware Solution
Tow hardware solutions
  Implement DMA remapping in hardware
    Remap DMA operations automatically by hardware.
    For example, Intel VT-d .
  Specify IO virtualization standards of PCI Express devices
    Implement virtualizable device with PCI Express interface.
    For example, SR-IOV or MR-IOV.

## Slide 50: Intel VT-d (1)
Add DMA remapping hardware component.
Software Approach
Hardware Approach

## Slide 51: Intel VT-d (2)
Advantages
  Data access bypass VMM
  Improve IO performance
Disadvantages
  Dedicate physical device assignment limits the system scalability.

## Slide 52: Single Root – IO Virtualization (1)
New industrial standard
  Instead of implementing virtualization in CPU or memory only, industry comes up with new IO virtualization standard in PCI Express devices.
  Advantages
    Fully collaboration with physical hardware devices.
    Improve system scalability.
    Improve system agility.
  Disadvantages
    IO devices must implement with new specification.

## Slide 53: Single Root – IO Virtualization (2)
What is SR-IOV ?
  The PCI-SIG Single Root I/O Virtualization and Sharing (SR-IOV) specification defines a standardized mechanism to create natively shared devices.
Basic components :
  Physical Functions (PFs)
    These are full PCIe functions that include the SR-IOV Extended Capability.
    The capability is used to configure and manage the SR-IOV functionality.
  Virtual Functions (VFs)
    These are “lightweight” PCIe functions that contain the resources necessary for data movement but have a carefully minimized set of configuration resources.

## Slide 54: Single Root – IO Virtualization (3)
SR-IOV works with VMM
  VMM
    An SR-IOV-capable device can be configured to appear in the PCI configuration space as multiple functions.
  VM
    The VMM assigns one or more VFs to a VM by mapping the actual configuration space of the VFs to the configuration space presented to the virtual machine by the VMM.